## Slide 1: Dissolved Oxygen
Issues and Challenges Associated with TMDL Development

## Slide 2: Data Assessment
What does the Monitoring Data Tell You?
  What is causing the impairment?
    Dry Weather Low Flow?
      Point Source Controlled
    Wet Weather High Flow?
      CSO, MS4, NPS
    Low Flow following High Flow?
      Point Source
      CSO, MS4, NPS
    Productivity?
      Diurnal Variations in DO
        Algae, Macrophytes, Periphyton
    Natural Condition?

## Slide 3: Low Flow

## Slide 4: Productivity

## Slide 5: Water Quality Standard
What is the Water Quality Standard
  Never less than 4 mg/l DO (Absolute Value)
  Daily Average of 5 mg/l (Allows for Diurnal Variation
  Combination of the Above
What Standard is Applicable for the Development of the TMDL
  What ever is Targeted must be protective
  Does Targeting the Absolute protect the Daily Average?
    It May
    It May Not

## Slide 6: Components of Dissolved Oxygen
Losses of Oxygen
  BOD
    BOD5
    BODUltimate
  Sediment Oxygen Demand
    Oxygen Consumed by Oxidation of Organic Material associated with the benthos
  Nitrification
    Oxygen Consumed in the conversion of Ammonia to Nitrite/Nitrate
  Respiration
    Algae
    Macrophytes
    Periphyton

## Slide 7: Components of Dissolved Oxygen
Sources of Oxygen
  Reaeration
    Hydraulic Reaeration
      Function of water velocity and depth
      Dam/Control Structures
    Wind Driven Reaeration
      Function of Wind Speed, Air Temperature, Water Temperature
  Productivity
    Algae
    Macrophytes
    Periphyton

## Slide 8: Components of Dissolved Oxygen
Dissolved Oxygen =
Reaeration + Productivity
(Source)
- (CBODDecay + SOD + Respiration + Nitrification
(Sink)

## Slide 9: Simplistic Example
POTW
Approximately 10 Mile Segment
Impaired Segment
Probably Cause of Impairment
CBOD
Nutrient Enrichment

## Slide 10: Assumptions for Example TMDL
Limited Monitoring Data
  Does not fully characterize the DO Sag at all periods
  Limited to No Chemical Data
  Have DMR data for POTW
Can Not Fully Calibrate Model Under All Conditions
  Steady State Low Flow Condition Simulated

## Slide 11: Calculating DO TMDL’s
The Approach and Assumptions Made Can Control the TMDL Calculation
  What Should Be Considered?
  What Should Not Be Considered?
What Should the MOS Be?

## Slide 12: Assumptions for Developing DO TMDLs
Target 5 mg/l

## Slide 13: Assumptions for Developing DO TMDLs

## Slide 14: Assumptions for Developing DO TMDLs

## Slide 15: Productivity/Nutrient Enrichment Impacts on DO
Algae/Macrophytes/Periphyton
  Produce Oxygen (Photosynthesis)
  Consume Oxygen (Respiration)
Cause Diurnal Swings in DO
  Day Time (High)
  Night Time (Low)
Productivity
  Controlled by
    Available Nutrients
      Nitrogen
      Phosphorus
      Light

## Slide 16: Target Identification
Water Quality Standards
  Nitrogen None
  Phosphorus None
Awaiting National Guidance/Criteria
  May not be applicable to all water bodies
Site Specific Criterion
  May need to be developed
    Biological Studies
    Reference Streams
    Modeled
    Combination of All Above

## Slide 17: Is the Dissolved Oxygen Influenced by Productivity?
What's the DO
Target?

## Slide 18: Assumptions for Developing DO TMDLs

## Slide 19
 | % Red
BOD | 19
NH3 | 0
NO3 | 0
 | % Red
BOD | 69
NH3 | 0
NO3 | 0
 | % Red
BOD | 81
NH3 | 70
NO3 | 0
 | % Red
BOD | 38
NH3 | 60
NO3 | 50
How Does the Assumption Change the TMDL

## Slide 20: Tailrace DO
A stream segment is listed for low dissolved oxygen. The
Segment represents tailwater release. Is a TMDL necessary
to address this impairment, and if so, how should the TMDL
be done. A dynamic model exists for the reservoir whereby
the relative effects of pollutants versus pollution can be
ascertained and analyzed.

## Slide 21: Nutrient Modeling
A reservoir is listed for nutrient enrichment. Simple screening
techniques, empirical and regression methods, and steady-state
and dynamic mechanistic models are being considered to develop
a TMDL for the reservoir.
What Model should be used?
Can EPA approve a TMDL developed with a screening model
and if so, is a phased approach necessary?

## Slide 22: Nutrient TMDL Endpoints
An impoundment is listed for nutrient enrichment. The waterbody is both light and phosphorus limited. The designated uses are both drinking water and recreation. The listing state has a narrative nutrient criteria. The 305(b) report indicated that nuisance algal blooms led to listing. How should the TMDL target be determined?

## Slide 23: Questions/Discussion