## Slide 1: Introduction to Modeling Rivers and Streams using WASP
General Characteristics of Rivers

## Slide 2: Characteristics of Rivers and Streams
- Rivers and streams vary widely in their size, flows and ecological characteristics
- They are strongly influenced by the characteristics of their watersheds.
- They range from small ephemeral or intermittent streams, which flow only in response to rainfall, to rivers such as the Mississippi-Missouri system
- The running nature of rivers and streams which generally distinguishes them from all other water bodies.
- Rivers and streams are lotic (from lotus, meaning washed) systems which are characterized by running water, as opposed to standing water or lentic (from lenis, meaning calm) water bodies
- Rivers and streams generally flow in a particular direction within a definite channel (the thalweg) and ultimately discharge into some other water body.

## Slide 3: Characteristics of Rivers and Streams
-Current is a major controlling or limiting factor in rivers and streams
- The flow often determines the expected variations in water quality
- Cross-sectional mixing is usually rapid in comparison with other waterbodies, so that rivers and streams are often assumed for modeling purposes to be one-dimensional (longitudinal) systems. That is, velocities are assumed to be adequately represented by a mean value.

## Slide 4: Factors Distinguishing Modeling Approaches
Flow model complexity
  Spatial resolution
  Temporal resolution
Water quality model complexity
  State variables
  Kinetic resolution

## Slide 5: Factors Distinguishing Modeling Approaches
Model complexity
  Spatial resolution
    Usually assume rivers are one-dimensional
    Length of river, location and number of segments will vary with application
  Temporal resolution

## Slide 6: Factors Distinguishing Modeling Approaches
Model complexity
  WASP Temporal resolution

## Slide 7: Dynamic Analysis
Quasi-steady approach
  Run a dynamic model (such as WASP) using steady flows (descriptive flows)
Dynamic Approach
  Run a dynamic model with descriptive flows
  Predict time-varying flows and quality
    Requires coupled hydrodynamic and quality model
    Typical approach is to run hydrodynamic model and save output (flows, volumes, depths, velocities) for use by quality model

## Slide 8: Dynamic Analysis
Application conditions
  When and for how long to apply ?
  Typical applications require continuous simulation (wet and dry weather periods)

## Slide 9: Dynamic Analysis
When to run a dynamic analysis?
  When flows are highly variable
    Below peaking hydropower facilities
    When considering the impact of transient inflows, such as from storm events
  When quality is variable over time
    Predicting seasonal variations
    Predicting impact of storm events or a sequence of dry weather and storm events
    When critical conditions are not known (dry before wet, and 1 yr vs a 2 yr storm)

## Slide 10: Factors Distinguishing Modeling Approaches
Water Quality Model Complexity
  State variables
    Simple dissolved oxygen (e.g. Streeter Phelps)
    Intermediate eutrophication
    Eutrophication
    Organic chemicals
    Metals
  Kinetic resolution
    Number and kind of processes included

## Slide 11: WASP Data Requirements for Transport
Channel Segmentation
Flows
Channel hydraulic characteristics
  Depths
  Velocities
Mixing coefficients

## Slide 12: WASP Channel Segmentation
How valid is one dimensional assumption
  Is there stratification?
  Are their lateral variations?
    ex. a considerable distance may be required for complete lateral mixing downstream of a discharge

## Slide 13: WASP Channel Segmentation
How long a reach of river must be simulated?
    Example if a material decays at a first order rate of 0.2/day, then the time for 90 percent of the material to decompose is 11.5 days. If the river has a mean velocity of 1 ft/s, then a parcel of water could travel 188 miles in that time.

## Slide 14: WASP Channel Segmentation
  Are their lateral variations ?
    Example, for a discharge into the side of a channel, the distance to downstream complete mixing can be estimated from:
u = channel velocity
u* = shear velocity
W = top width
Dt = transverse mixing coefficient
g = gravitational acceleration,
Y = depth
So = channel slope
c = coefficient (approximately 0.6)
example: if u = 0.5 m/s, Y = 2.5 m, W = 90 m, and So = 0.0003, then Lm = 12.6 km

## Slide 15: WASP Channel Segmentation
How much resolution (how many segments) are required ?
  Consequences of too little resolution
    Gradients not adequately characterized
    Increased numerical dilution (assumption that a segment is completely mixed)
  Consequences of too much resolution
    Simulation times increased (controlled in part by travel time through smallest segment)

## Slide 16: Specification of Flows to WASP
Descriptive Approach
  Based upon measured data
  examples include flow measurements and time of travel estimates
Predictive Approach
  Simple Hydrologic Stream Routing
  Steady, Uniform Flow Methods
  Hydraulic methods for steady, non-uniform flow
  Hydraulic methods for unsteady flows

## Slide 17: Measurement of Velocities and Flow
Float methods
Current meters
  Mechanical
  Acoustic
  Electromagnetic
Control structures
Dyes and tracers
Remote sensing

## Slide 18: Flow, Depth, Velocity Correlations
In addition to flow, WASP requires estimates of depth and velocity
These hydraulic characteristics affect processes such as reaeration and light penetration
May be specified (descriptive approach) or obtained from hydrodynamic model predictions

## Slide 19: Empirical Relationships (descriptive approach only)
where Q is flow, velocity u, depth Y, width W and a-f are empirical coefficients

## Slide 22: Empirical Relationships
So that

## Slide 23: Empirical Relationships
Source: WASP Manual (Ambrose, Wool and Martin 1993)

## Slide 24: Time of Travel and Dye studies
Purpose of dye studies
Time of travel
Dispersion and mixing
Lagrangian Sampling
Dilution in reaeration measurements
Circulation and stratification
Determining discharge in streams
Groundwater movement
Mass balance studies
Source (discharge) investigations

## Slide 25: Slug Dye Release
Source: Martin and McCutcheon 1998

## Slide 26: Continuous Release
Source: EPA EWLA Workshop

## Slide 27: Dye Studies: Flow measurements
Continuous (steady-state) conditions
C
Distance
Length
Velocity=Length/Travel Time
Centroid of Dye Cloud