## Slide 1: General Water Quality – Salinity, TDS, pH, TIC, and Alkalinity
Theory and Implementation in WASP7
Prepared by
Robert B. Ambrose, Jr.
February, 2010

## Slide 2: TDS Total Dissolved Solids in Freshwater [mg/L]
Measures combined inorganic and organic material in molecular, ionized, and colloidal form (2 μm sieve)
Parameter of interest freshwater streams, rivers, lakes
WQ target 100 mg/L drinking water, 1000 mg/L for aquatic ecosystems
Range of values:
  Soft water: 0 – 140 mg/L
  Moderately hard water: 140 – 320 mg/L
  Hard water: 320 – 530 mg/L
  Very hard water: >530 mg/L

## Slide 3: Salinity Total Dissolved Salts in Seawater
Measures total salt content in parts per thousand by weight
Expressed in practical salinity units [PSU]
  Calculated from conductivity ratio with standard solution
  Standard = 32.4356 g KCl / 1 kg solution at 15 C, 1 atm
http://en.wikipedia.org/wiki/Seawater

## Slide 4: Salinity Composition
Average seawater contains 35 g salts/kg seawater
Worldwide range: 31 – 38 g/kg
Composition:
http://en.wikipedia.org/wiki/Seawater

## Slide 5: Simulating TDS and Salinity
Conservative (non-reacting) variables
Either Salinity or TDS is simulated
  User selects which is simulated (Global Constants group)
  Water density is calculated:
  If Salinity is simulated, TDS is derived:
  If TDS is simulated, Salinity is derived:

## Slide 6: pH, TIC, and Alkalinity
pH is a primary water quality variable of interest
Gold Book standards:
  6.5-9, freshwater chronic
  6.5-8.5, saltwater chronic
TIC and Alkalinity are simulated to support the calculation of pH

## Slide 7: pH Negative Log of H+ Activity
p[H] = -log10(H+ molar concentration [mol/L])
pH = -log10(H+ activity), the product of:
  Molal concentration of H+ [mol/kg-water]
  Activity coefficient
[H+] is the result of several speciation reactions that balance the electrical charge of the water solution
Typical range of pH:
  Freshwater systems: 6 to 9
  Marine systems: 7.5 to 8.5

## Slide 8: Primary Freshwater Speciation Reactions

## Slide 9: Phosphate and Ammonia Speciation Reactions

## Slide 10: Additional Marine Speciation Reactions

## Slide 11: Electroneutrality
H2O
H+
OH-
K+
Mg2+
Na+
Ca2+
NO3-
H2PO4-
HPO42-
PO43-
H3PO4
F-
Cl-
HSO4-
SO42-
B(OH)4-
B(OH)3
SiO(OH)3-
SiO(OH)2
CO32-
HCO3-
H2CO3
NH4+
NH3

## Slide 12: Total Inorganic Carbon
TIC: total inorganic carbon [mg C/L]
  TICmol [mol/L] = H2CO3 + HCO3- + CO32-
  TIC [mg C/L] = TICmol × 12011 [mg C/mol]
Typical range of TIC
  Freshwater systems: 10 to 40 mg/L
  Marine systems: 22 to 27 mg/L

## Slide 13: Biological Reactions Affecting TIC and Alkalinity: Photosynthesis and Respiration
ammonia as substrate
nitrate as substrate
+ 106 O2

## Slide 14: TIC Kinetics
CO2
Phytoplankton
Periphyton
CBOD
P
R
kd
kr

## Slide 15: CO2 Reaeration
ka = O2 reaeration rate constant, day-1
KH = Henry’s law constant
0.923 = CO2 to O2 reaeration ratio
fCO2 = fugacity
pCO2 = partial pressure, atm

## Slide 16: CO2 Dam Reaeration

## Slide 17: Dam Reaeration Coefficients
Polluted State | A
Gross | 0.65
Moderate | 1.0
Slight | 1.6
Clean | 1.8
Dam Type | b
Flat broad-crested regular step | 0.70
Flat broad-crested irregular step | 0.80
Flat broad-crested vertical face | 0.60
Flat broad-crested straight-slope face | 0.75
Flat broad-crested curved face | 0.45
Round broad-crested curved face | 0.75
Sharp-crested straight slope face | 1.00
Sharp crested vertical face | 0.80
Sluice gates | 0.05
Water Quality Coefficient
Dam Type Coefficients

## Slide 18: Alkalinity
Ability of solution to neutralize acids
  to equivalence point of bicarbonate, pH 4.5
Stoichiometric sum of bases in solution
Carbonate alkalinity most important
  Carbonate rock
  CO2 in atmosphere
Other natural components of alkalinity
  Borate, hydroxide, phosphate, silicate, nitrate, ammonia

## Slide 19: Alkalinity Units and Range
Units and conversion:
  Alkeq in molar units [eq/L], or Alkmeq [meq/L]
  Alk in mass units [mgCaCO3/L]
  Alk = Alkmeq × 100.9 [g/mol] / 2 [eq/mol]
Typical range of alkalinity:
  Freshwater: 0.4 – 4 [meq/L], 20 – 200 mgCaCO3/L
    Low alkalinity: < 0.2 [meq/L], 10 [mgCaCO3/L]
    pH stabilized above 2 [meq/L], 100 [mgCaCO3/L]
  Marine: 2.25 - 2.5 [meq/L], 110 – 130 [mgCaCO3/L]
Notes: Information on alkalinity in seawater from: http://en.wikipedia.org/wiki/Alkalinity
Information on alkalinity in freshwater from http://bcn.boulder.co.us/basin/data/NEW/info/Alk.html and EPA Rates Manual, p. 241

## Slide 20: Alkalinity Equation
Water alkalinity
Carbonate alkalinity
Borate alkalinity
Phosphate alkalinity
Silicate alkalinity

## Slide 21: Some Biochemical Reactions Affecting Alkalinity
Nitrification
Denitrification

## Slide 22: Biological Reactions Affecting TIC and Alkalinity: Photosynthesis and Respiration
ammonia as substrate
nitrate as substrate
+ 106 O2

## Slide 23: Alkalinity Kinetics
Deposition
Phytoplankton
Periphyton
nitrification
PNH4
R
NH4
Alkalinity
PNO3
denitrification
ON hydrolysis
OP hydrolysis
NO3
PO4
PPO4

## Slide 24: Alkalinity Kinetics
PO4,sed
Notes: Need a picture illustrating these processes

## Slide 25: Alkalinity Kinetics
SPO4,sed
Notes: Need a picture illustrating these processes

## Slide 26: Initial and Boundary Conditions
Specify Salinity in [PSU] or TDS in [mg/L]
  Selection based on Global Constant 7, Sal_TDS_Opt
  Default is option 1, Salinity
Specify pH in standard pH units [su]
  WASP will convert pH IC’s and BC’s to TIC [mg C/L]
  Conversion is based on pH, alkalinity, T, Salinity
Specify alkalinity in [mg CaCO3/L]

## Slide 27: Loadings
ALL LOADINGS ARE IN [kg/day]
WASP displays the variable name and its concentration unit (not the units for loading)
For Salinity, units are [PSU], but loadings are [kg Salinity/day]
If simulating TDS, enter TDS loadings [kg TDS/day] in the Salinity loading field
Enter TIC loadings [kg TIC/day] in the pH field
Alkalinity loadings are [kg CaCO3/day]

## Slide 28: Information in Out File
Each simulation produces ASCII output file
  Name of input file + extension “.out”
  Echo of simulation input data
  Warning and error messages
New tables added:
  Adjusted Initial Conditions
  Initial K Array for Calculating pH
  Final Output Variables

## Slide 29: Adjusted Initial Condition Table
TIC from pH, Alkalinity, TW
pH adjusted from molar units
Salinity as input or as calculated from TDS
Water density from TW, S, P
Pressure from segment depths

## Slide 30: Initial K Array for Calculating pH
Produced if pH is simulated
Equilibrium constants for initial conditions
  Temperature, Salinity, Pressure