## Slide 1: Introduction to Hydrodynamic Modeling using EFDC

## Slide 2: Why EFDC Hydrodynamic Simulation?
To drive the WASP water quality model

## Slide 3: Description of EFDC
Development History
Capabilities
Hydrodynamic module
Applications
Example Application
Linkage file to WASP

## Slide 4: ENVIRONMENTAL FLUID DYNAMICS CODE
EFDC is a public domain surface water modeling system incorporating fully integrated hydrodynamics
EFDC is extremely versatile, and can be used for 1D, 2DV, 2DH, or 3D simulations of rivers, lakes, reservoirs, estuaries, coastal seas, and wetlands

## Slide 5: EFDC Development History
Developed by John Hamrick at Virginia Institute of Marine Science (VIMS) with primary support from the State of Virginia
Additional support has been provided by
EPA and NOAA
Presently maintained by Tetra Tech, Inc.
Currently used by federal, state and local agencies, consultants and universities

## Slide 6: EFDC Capabilities
Three-Dimensional hydrodynamics with coupled salinity, temperature, sediment and contaminant transport modules
Simulates wetting & drying of flood plains, mud flats, and tidal marshes
Integrated near-field mixing zone model
Simulates hydraulic control structures such as dams and culverts
Simulates wave boundary layers and wave-induced currents

## Slide 7: EFDC Hydrodynamic Module
Fully 3D, with 2DV, 2DH and 1D options
Boundary fitted curvilinear-orthogonal grid or
Cartesian grid can be used
Includes turbulence closure model
Highly efficient finite difference semi-implicit solution
Functionally similar to POM/ECOM and CH3D-WES

## Slide 8: Example EFDC Applications
Rivers – Flint (AL), Housatonic (MA), Chattahoochee (GA), Los Angeles (CA)
Lakes - Lake Okeechobee (FL), Lake Jordan (NC), Coosa River Reservoirs (AL), Lake Allatoona (GA), Hartwell Reservoir (GA/SC)
Estuaries - Mobile Bay (AL), Neuse River (NC), Savannah River/Harbor (GA), Charleston Harbor (SC), St Johns River (FL), Lower Duwamish Waterway (WA)
Lagoons – Curonian Lagoon (Lithuania)

## Slide 9: Neuse River Network plan view

## Slide 10: Neuse Bathymetry

## Slide 21
What Does the 3-D Hydrodynamic Model Get You?

## Slide 22
Filename | Description
ASER.INP | Atmospheric Info – Dew Pt. Air Temp, etc
CELL.INP | Model Grid in I-J Format
CELLLT.INP | Model Grid Activated for WASP Linkage
DXDY.INP | Corner Point Definitions for the Grid
EFDC.INP | Main EFDC Configuration File
LXLY.INP | Distance File for Corners of the projected Grid
MASK.INP | Used to Disable Areas of the Grid
PSER.INP | Water Surface Elevation Time Series
QSER.INP | Flow Time Series
SALT.INP | Initial Concentration of Salt
SHOW.INP | Configures the Runtime Screen
SSER.INP | Salt Concentration Time Series
TEMP.INP | Initial Temperature
TSER.INP | Temperature Time Series
WNDMAP.INP | Wind Mapping File
WSER.INP | Wind Time Series
EFDC.WSP | WASP Linkage Control File

## Slide 23: CELL.INP

## Slide 24: CELLLT.INP

## Slide 25: EFDC Configuration for WASP
Turns the Linkage Option On

## Slide 26: EFDC Configuration for WASP
Model Timestep = 86400/This #
Write Interval for HYD File

## Slide 27: EFDC Configuration for WASP
Dynamic Timestep
Option

## Slide 28: QSER.INP

## Slide 29: EFDC.WSP
HYD Filename
Number of Days Before
Starting to Write