## Slide 1: Modeling Mercury in Lake Waccamaw, North Carolina

## Slide 2: Lake Waccamaw, NC

## Slide 3: Lake Waccamaw, NC
Large Bay lake in Southeastern North Carolina
>60% of fish Hg conc >1 ppm. (NCDE, 1992)
Lake Waccamaw is a popular spot for recreational fishing
Fish Consumption Advisory in place
Variety of Mercury Sources
  2 Coal-Fired Electric Utility Boilers
  Lg Municipal Waste Incinerator
  Several Lg coal or oil-fired industrial boilers
  Pulp and paper mill

## Slide 4: Lake Waccamaw, NC
 | Measured Values | 
 | Range | Mean
Water Column MeHg, unfiltered | 0.132 – 0.233 ng/L | 0.18 ng/L
Water Column HgT, unfiltered | 1.06 – 3.89 ng/L | 2.41 ng/L
Sediment MeHg | 0.033 – 0.082 ng/g | 0.06 ng/g
Sediment HgT | 10.2 – 28.7 ng/g | 19.5 ng/g
Largemouth Bass Tissue Hg | 0.5 – 2 ug/g | 2 yr old bass: 0.60 ug/g

## Slide 5: Lake Waccamaw, NC
Lake Area: 34,706,448 m2
Mean Depth: 2.3 m
Lake Volume: 79,824,830 m3
Hydraulic Residence Time: 0.66 yrs
Inflow/Outflow: 1.2x108 m3/yr
pH 4.5
DOC 11 mg/L

## Slide 6: Lake Waccamaw, NC
Broad, flat bottom of gyttja (mud) and peat
Circled by sandy shallows that extend 500m from shore

## Slide 7: Lake Waccamaw, NC
Lake Area: 34,706,448 m2
Mean Depth: 2.3 m
pH 4.5
DOC 11 mg/L

## Slide 8: Lake Waccamaw Model Set-Up
Lake Waccamaw has two regions.
  A Sandy Bottom Ring around the edge
  Muddy/Gyttja layer in the middle of lake
Model can be set up two ways
  approximate these as one region
  model as two segments
Advantages/Disadvantages
  Simpler as one region
  May be more representative as 2 regions
    More complicated
    Requires more parameters
    May over-parameterize system

## Slide 9: One Segment Lake Waccamaw
Inflow
3.8 m3/s
2.3m
A = 34,706,448 m2
Outflow
3.8 m3/s
Lake
Surface Sediment
Subsurface Sediment
0.02m
0.10m
Segment | Description | Volume | Depth | Seg Type | Bottom Seg
1 | Epilimnion | 7.98248e7 | 2.3 | Surface | 2
2 | Surface Sediment | 6.94129e5 | 0.02 | Subsurface | 3
3 | Subsurface Sediment | 3.47064e6 | 0.10 | Surface Benthic | None

## Slide 10: Two Segment Lake Waccamaw
sand
gyttja
Lake Area: 34,706,448 m2
A=r2  R = sqrt(A/) = 3325m
r1 = 2825m, r2 = 500m
Areasand = 9,634,575 m2
Areagyttja = 25,071,873 m2
R
r2
r1

## Slide 11: Two Segment Lake Waccamaw
Inflow
3.8 m3/s
2.3m
Lake
Upper Gyttja
Lower Sediment
0.02m
0.18m
Sand
0.15m
Outflow
3.8 m3/s
Area = 25,071,873 m2
Area = 9,634,575 m2
Lake
2.3m
500m
2825m

## Slide 12: Setting up Lake Waccamaw
Name Project
Use Mercury
Model
Set
Start/End
Date/Time