## Slide 1: Setting-up and running R calibration scripts
John M. Davis

## Slide 2: R calibration project Overview
Developed by Region 4 modeling group to facilitate quantitative/qualitative calibration
Run interactively as R Project or via .BAT mode
  Requires R & R Studio
Uses Excel *.xlsx file to set calibration script options
  Allows user to run scripts w/ minimal knowledge of R
Reads in WASP *.BMD2 and monitoring data *.txt file
Processes and assesses model fit using common R packages
  e.g., hydroGOF, tidyverse, etc.
Generates
  Publication quality calibration figures
  Goodness of fit summary statistics

## Slide 3
Populate Excel calibration lookup table
Export monitoring data as *.txt
Execute ‘Master’ script in R Project
Run WASP model & save *.BMD2
Preproc
WRDB
WASP
R Studio
Excel
Install R,
R Studio, &
R packages
Evaluate calibration output
Unzip R calibration project
Update lookup table & WASP model
QA/QC & save monitoring data in WRDB
Overview of R calibration script workflow
Generate
plots & statistics
Map PCode crosswalk
Map segment crosswalk

## Slide 4: R calibration project Input data needs
Fully processed (QA/QC’d) ambient monitoring data
  Export from WRDB as a *.txt file
WASP model output
  Can use either a raw WASP *.BMD2 or a preformatted/extracted *.txt
Crosswalk of WASP model segments & monitoring stations
Crosswalk of WASP & monitoring station parameters
Excel lookup table (*.xlsx) w/ user defined arguments

## Slide 5: Data preprocessing steps

## Slide 6: R calibration project Export monitoring data from WRDB
Process, QA/QC, & save monitoring data in WRDB
Open WRDB
Output  Export  Data File
Save as *.txt
  Do not save monitoring data as R Dataframe
Name *.txt based on filename provided in Excel lookup *.xlsx
Monitoring data needs to be in same units as model output

## Slide 7: R calibration project Export monitoring data from WRDB
Format of exported monitoring data *.txt

## Slide 8: R calibration project WASP model output: BMD2
WASP model output in *.BMD2 format
Location of *.BMD2 based on ‘Filepath_BMD2’
Scripts use ‘BMD2_Extract.exe’ to extract data
Extraction based on PCode & segment crosswalk in lookup
  Examining *.BMD2 in BMDUtil can help create crosswalks
Model data extracted & saved as *.txt
Filename of extracted model data *.txt
If no *.BMD2 filename is provided, the scripts skip the ‘BMD2_Extract.exe’ and will use the Model_Extracted_Filename as model input datafile. *.txt file must be in correct format.

## Slide 9: R calibration project WASP model output: *.txt
‘BMD2_Extract.exe’ will automatically process the *.BMD2 & write-out the model *.txt in this format
If no .BMD2 filename is provided and extraction .exe is skipped, the *.txt supplied (Model_Extracted_Filename) to the R project must be preprocessed and already be in this format

## Slide 10: Opening R calibration scripts

## Slide 11: R calibration project Unzip and installation
Unzip *.zip file to local drive
  Recommend saving in modeling project folder
Automatically creates required subfolders
  Folders cannot be renamed
  Some folders can be moved (see instruction manual)
Recommend running scripts interactively as R Project
  Can also run via .BAT mode (see instruction manual)

## Slide 12: R calibration project Folder hierarchy
Lookup: Input — Location of Excel lookup table
Plot_Box: Output — Boxplot figure
Plot_Calib: Output — Multipanel calibration figure
Plot_Dens: Output — Density distribution figure
Plot_Geom: Output — Geometric mean figure
Proc_Out: Output — Paired and interpolated datafiles
Raw_In: Input — Raw measured data *.txt & default for model *.BMD2
Scripts: Input — R scripts & data extractor *.exe
Shapefile: Input — Watershed shapefiles (optional)
Stats: Output — Summary / goodness of fit stats
Double-click this to open calibration project in R Studio

## Slide 13: Setting-up Excel lookup table

## Slide 14: R calibration project Open Excel Calib_Lookup.xlsx
Scripts designed to interact with Excel *.xlsx
Set arguments w/o directly altering R scripts
Controller tab
  Calibration script options
Station_Lookup tab
  Crosswalk WASP segments & monitoring station IDs
PCode_Lookup tab
  Crosswalk WASP & monitoring station parameters

## Slide 15: R calibration project Model segment / monitoring station crosswalk
WASP_Segment: WASP segment number
WASP_Name: WASP segment name
  Must exactly match WASP segment name used in *.BMD2
Calib_Station_ID: Monitoring Station_ID
  Must exactly match monitoring Station_ID used in WRDB support table
Plot_Title: Custom name used to label segments in figures
  Plot_Title identical when multiple stations mapped to same segment
Plot_Order: Custom vector that orders stations downstream to upstream
  Plot_Order identical when multiple stations mapped to same segment
Lat/Long: (Optional) Include monitoring stations on calibration watershed map
Use this field to select/deselect which segments to calibrate
Spelling/capitalization matter

## Slide 16: R calibration project PCode crosswalk
User provides PCode crosswalk
  WASP analyte name to monitoring data PCode
PCode = WRDB PCode support table field
  User defined
  Must exactly match Pcode used in WRDB support table
Anal_Name = Model parameter name used in *.BMD2
  Defined by WASP and not customizable
  Must exactly match parameter name used in *.BMD2
Units = Used to label plots
  Scripts do not apply any unit conversions
Spelling/capitalization matter
Use this field to select/deselect which Pcodes to calibrate

## Slide 17: R calibration project Calibration tab — calibration settings
Model Run Code
  4-character code to help compare multiple model runs
Filepath_R_Scripts
  Location of R ‘Scripts’
Filepath_Model_Data_In
  Location of Raw model *.BMD2 / *.txt
  Where extracted model *.txt saved
Filepath_Calib_Data_In
  Location of raw calibration data
Filepath_ProcData_Out
  Location where GoF stats files will be saved
Calib_Data_In_Filename
  Name of monitoring data *.txt file
Model_BMD2_Filename
  Name of WASP output *.BMD2
Model_Extracted_Filename
  Name of extracted WASP output *.txt file
Allows user to set the location/names of input data
If blank, most will default to location of *.Rproj file
If blank, ‘Filepath_Model_Data_In’ defaults to ‘Raw_In’ subfolder of R Project working directory
When no BMD2 filename is provided, scripts assume ‘Model_Extracted_Filename’ is model input data source

## Slide 18: R calibration project Calibration tab — shapefile settings
Filepath_Shapefile
  Location of shapefiles
Watershed_Shapefile_Filename
  Name of watershed shapefile
  Required if ‘Map’ selected
Stream_Network_Filename
  Name of model network shapefile
  Required if ‘Map’ selected
Coord_Ref_Sys_Code
  4 digit EPSG code to define shapefile coordinate system
  Required if ‘Map’ selected
Allows user to set the location/names of shapefiles (optional)
If blank, will default to ‘Shapefile’ subfolder in *.Rproj file

## Slide 19: R calibration project Changing subfolder filepaths
If subfolders moved, must provide filepath in Excel lookup
Filepath & name provided by *.bat file
Cannot change in interactive mode.
Subfolders linked to specific filepaths
Scripts will use defaults if filepaths left blank

## Slide 20: R calibration project Calibration tab — plot selection
Enter ‘X’ in ‘Plot’ field to activate corresponding plot
If watershed map is activated, need watershed & network shapefile
Annual option = include year-by-year geomean/boxplot comparisons
  Can slow down plotting
Allows user to select which calibration figures to generate

## Slide 21: R calibration project Calibration tab — filter settings
Geomean_First_Month/Geomean_Last_Month
  Months to use for TN, TP, & Chl-a geomean calculations (inclusive)
Minimum_Observations
  Minimum # of samples a monitoring station needs to be used for calibration (inclusive)
Rcode_Flag_Exclusion
  Character vector of Remark Codes (Rcode)
  Excluded from statistics
  Flagged on figures
Model_Timezone
  Set time zone of monitoring & model data
Allows user to apply various data filter options

## Slide 22: Running R project

## Slide 23: R calibration project Opening R project
Double-click this to open calibration project in R Studio
Online resources for creating/using R Studio projects
https://support.rstudio.com/hc/en-us/articles/200526207-Using-Projects

## Slide 24: R calibration project R project pane view
Active SOURCE script
R console
R global environment
R history
Files directory
Plots

## Slide 25: R calibration project Opening master R script
SOURCE pane may be missing if no active script
Open ‘Master_Mrgd_JD_v4.2.R’ in SOURCE pane
Do not open or alter any other files in this subfolder
Master script will call secondary scripts as needed
To open ‘Master’ script, double-click ‘Master_Mrgd_JD_v4.2.R’ in ‘Files’ pane

## Slide 26: R calibration project Customizing pane views
Customize pane views: View  Panes  Pane Layout
Select which panes to display

## Slide 27: R calibration project Running master calibration script
To execute ‘Master’ script in R console, click ‘Source’ button
Scripts not run until sent to R Console
When executed, Master script will call secondary scripts as needed
Messages displayed in console while running

## Slide 28: R calibration project R console messages
Black font: Messages indicate data processing/graphing progress or
QA/QC issue
Stop sign indicates script actively running
Click to prematurely end script
Red font: Warnings (scripts completed) & Errors (scripts crashed)

## Slide 29: R calibration project Calibration output
Output saved in multiple subfolders
Can re-run scripts iteratively on new model results
  Overwrites existing calibration figures/statistics
To re-run w/ new model output
  Copy / paste new model *.BMD2 to BMD filepath
  Update *.BMD2 filename (optional) in Excel lookup
  Update Model_Run_Code (optional) in Excel lookup
  Re-run ‘Master’ script

## Slide 30: R calibration project Calibration manual & appendices
See manual and appendices for
  Additional details on setting-up & running scripts
  Instructions for running in *.BAT mode
  Explanation of figures & statistics
  Summary of common errors
Manual located in R Project folder

## Slide 31: Overview of running scripts in .BAT mode See manual for details

## Slide 32: Running scripts in .BAT mode Advantages/disadvantages
Advantages
  Maintain single version of scripts & apply to multiple projects
  Greater flexibility to read-in / write-out files to multiple locations
  Easier to calibrate multiple model runs w/o overwriting output
  Allows automation of scripts when WASP is also run in .bat mode
Disadvantages
  Easier to make a mistake / harder to troubleshoot
  Requires greater understanding of subfolder hierarchy
  Requires understanding of creating *.bat files
  Moving subfolders may limit ability to run interactively in R Studio
  Moving subfolders eliminates self-containment of R Project folder

## Slide 33: Running scripts in .BAT mode Creating .bat file
Filepath to R terminal .exe
Filepath to script subfolder & master .R script
Piping to write out error & message files
Filepath to lookup subfolder & Excel lookup file name
4-character model run code (optional; overrules Lookup table)
Create .bat file w/ everything on single line; separated by single space

## Slide 34: Questions?