## Slide 1: Introduction to Modeling Estuaries using WASP
General Characteristics of Estuaries

## Slide 2
Source: EPA 1987 EWLA Workshop

## Slide 3
Source: EPA 1987 EWLA Workshop

## Slide 4
Source: EPA 1987 EWLA Workshop

## Slide 5: Processes Impacting Transport
Tides
  Often dominate mixing in estuaries
  Produced principally by interaction of the gravitational fields of the earth, moon, sun and, to a lesser degree, other solar system bodies.

## Slide 6: Processes Impacting Transport
    The movement of the moon causes the principal effects to occur with a roughly 12.4-hour period. That is due to the time of the rotation of the moon with respect to the earth being, on average, 24.8 solar hours long (or 1.035 times as long as the mean solar day).

## Slide 7: Processes Impacting Transport
Tides
  Tides are expressed in terms of
    Amplitude: the variation of water level about some datum level, and
    Tidal current: the ebb and flood velocity fields

## Slide 8: Processes Impacting Transport
  Tidal amplitudes and currents are usually out of phase so the time of high water is not the same as the time of high water slack. Such differences in phase and interaction between main and side channels can lead to tidal trapping of parcels of water in side channels or embayments.

## Slide 9: Processes Impacting Transport
Tidal amplitude
  Tidal curve: plot of height of the water surface of a system that is subject to tidal action
    Generally, two high and two low tides on the tidal curve per tidal day (or lunar day, about 24.84 hours).

## Slide 10: Processes Impacting Transport
      Period corresponds to the time between successive passes of the moon over any point on the earth.
        Tidal period: time between low and high tides is known as the tidal period

## Slide 11: Processes Impacting Transport
Tidal amplitude
    Semidurnal tides: tides that occur twice during a tidal day are called semidiurnal tides
    Daily tides: have only one high and one low per day, such as in some area such as estuaries in the Gulf of Mexico

## Slide 12: Processes Impacting Transport
    Mixed tides: magnitude of high and low tides are quite different (e.g. Pacific estuaries)

## Slide 13: Processes Impacting Transport
Tidal amplitude
  Solar effects occur at 12 hours rather than 12.4 hour periods (the mean solar day is 24 hours).
  Because all the bodies in the solar system are in motion relative to one another, the effects of their gravitational fields vary in time. Therefore, tides may vary over longer periods such as days, weeks or years.

## Slide 14: Processes Impacting Transport
    Spring tides occur approximately every two weeks, usually within a few days of the times that the moon is full or new and the tidal range is larger than the mean tidal variations. During this period the sun and the moon act together, causing greater tidal variations.
    Neap Tides: occur during the first and third quarters of the moon.

## Slide 15
Tidal Amplitudes: San Francisco Harbor

## Slide 16
Seattle, WA
Pensacola, FL

## Slide 17: Processes Impacting Transport
Tidal Amplitude
  Sources of information
    NOAA
    Stage recorders

## Slide 18: Processes Impacting Transport
Tidal currents
  Horizontal water movements associated with the rising and falling tides
    Typically weak in the open sea, with velocities on the order of 5-10 cm s-1
    Highly variable in estuaries

## Slide 19: Processes Impacting Transport
  Progressive wave
    Flood current: occurs as the wave crest moves into an estuary, culminating in high tide
    Ebb current: occurs when the wave crest moves out of the estuary, culminating in low water or low tide
    Slack water: occurs Each time the water changes directions where there is a period of no net current

## Slide 20: Processes Impacting Transport
Tidal currents
  Standing wave: occurs in many estuaries when the tidal wave reaches the upper part of the estuary and is reflected back
    Progressive wave: maximum tidal amplitude and velocities occur at the same time

## Slide 21: Processes Impacting Transport
    Standing wave: tidal amplitude and velocities are out of phase
    Most estuaries have characteristics in between the standing and progressive waves

## Slide 22
Source: Martin and McCutcheon 1998

## Slide 23
Source: EPA 1987 EWLA Workshop

## Slide 24: Processes Impacting Transport
Tidal currents
  Tidal excursion: distance along the main axis of the estuary that the particle will transverse over the course of the tidal cycle
    Important in selecting size of system to be modeled (has to at least include tidal excursion)
    Important in selecting boundaries

## Slide 25: Processes Impacting Transport
  May be estimated from (for the principal M2 tidal component, Thomann and Mueller (1987)

## Slide 26: Processes Impacting Transport
Tidal currents
  Tidal excursion distance may be estimated from (for the principal M2 tidal component, Thomann and Mueller (1987)
where xte is the length of the tidal excursion, umax the average maximum tidal velocity, and Tm2 the period of the M2 tide (12.42 hours).

## Slide 27: Processes Impacting Transport
Coriolis force:
    Apparent force due to the earth’s rotation. In the Northern Hemisphere, the impact is to deflect the flow to the right side, looking seaward, of the estuary

## Slide 28: Processes Impacting Transport
Inflows
      Determine characteristic chemical gradients in estuaries; affect mixing; affect duration of flood and slack currents
Meteorological effects
      Wind: effects wave formation, mixing,and may cause surface currents.

## Slide 29
Source: Martin and McCutcheon 1998

## Slide 30: Processes Impacting Transport
Estuarine Morphometry
  Affects circulation patterns
    May cause residual circulation, such as tidal pumping (in analogy to using pipes and pumps to move water around and estuary)
    May also cause tidal trapping (like the trapping of particles in embayments during one phase of the tidal cycle)

## Slide 32: Water Quality Processes
Toxicity
  e.g. ammonia toxicity affected by salinity
Solids
  Fall velocities, flocculation, etc. impacted by salinity and salinity gradients
Nutrients and eutrophication
  Although different organisms, etc., the methods used for predicting eutrophication are similar to those used for lakes and reservoirs

## Slide 33: Factors Affecting Water Quality
Salinity
  Affects water density
  Affects concentration of dissolved gases

## Slide 34
Source: EPA 1987 EWLA Workshop

## Slide 35: Modeling Approaches Using WASP
Tidally-averaged model
  Flows and tidal mixing affects described (rather than predicted)
  Based on averaged effect of tides over multiple tidal cycles

## Slide 36: Modeling Approaches Using WASP
Inter-tidal model
  Predictions required within tidal cycles
  Requires use of hydrodynamic model used to predict variations in flows, volumes, depths, and velocities which are then specified to WASP

## Slide 37: Estuaries: Modeling Approaches using WASP
Tidally averaged models
  Assumption: the volume of the estuary, on average, remains constant
    River flow coming into the estuary travels out over averaging period (can be steady or time varying)

## Slide 38: Estuaries: Modeling Approaches using WASP
    The tidally flow coming in to the estuary during the flood tide goes back out (steady-tidal mixing)

## Slide 39: Tidally Averaged Estuary Modeling
Vertically well mixed estuaries
  Since the tidal flow in equals the tidal flow out, the impact of the tidal flow can be described using a dispersion or tidal mixing coefficient
+QTCo-QTC=
QT(Co-C)=EA/L(Co-C)
QRC
QRCR

## Slide 40: Tidally Averaged Model
Freshwater flow:
  Obtain from gaged flows
  Estimate ungaged flows
  Include other water (and loading source such as point and non-point) sources
  Route through estuary

## Slide 41: Tidally Averaged Model
Tidal Dispersion coefficient
  Estimate from similar estuaries or literature
  Estimate from concentrations of
    Dye
    Salinity

## Slide 42: Estimating Tidal Dispersion Coefficient
Example: analytical equation for a conservative material
which can be solved for E between two points, given, for example, measured salinities

## Slide 43
U=3.28 mi/day

## Slide 44: Dispersion Coefficients from Dye Tracers
Estimate using analytic solution to time variable spread of dye
Distance
Concentration
time =2
time =1

## Slide 45: Tidally Averaged Estuary Modeling
Stratified estuaries
  Steady flows
    Use simplified methods such as Pritchard’s method to back compute flows from salinity distribution (see Martin and McCutcheon 1998)
    Requires average salinity for each “box” in model

## Slide 46: Tidally Averaged Estuary Modeling
  Unsteady flows
    Typically requires inter-tidal model for hydrodynamics
    Tidally average inter-tidal predictions (as in Chesapeake Bay study)

## Slide 47: Sampling for Tidally Averaged Predictions
Question, when do you sample to determine the “average” condition since you are trying to “hit a moving target”
One alternative is to
  Sample over the tidal cycle
  Average results

## Slide 48: Sampling for Tidally Averaged Predictions
A second alternative is sampling a particular point in the tidal cycle
  Commonly take sample at slack-tide
  Slack-tide is when the flow goes to zero at the point when the tide reverses direction
    This point moves up or down the estuary

## Slide 49: Sampling for Tidally Averaged Predictions
    Should be measured synoptically, requiring
      A fast boat (typically moves at about 20 m/hr), or
      Multiple boats, equipment, etc.

## Slide 50: Modeling Approaches
Tidal Models of Estuaries

## Slide 51: Intertidal Models
Used to predict variations within as well as between tidal cycles
Typically requires application of
  Hydrodynamic model
  Water quality model such as WASP

## Slide 52: Example of Available Models
Examples of One-Dimensional Hydrodynamic Models
    DYNHYD (USEPA)
    RIVMOD (USEPA)
    UNET (USACE HEC)
    RIV1 (USACE WES)

## Slide 53: Example of Available Models
Examples of Two-Dimensional Hydrodynamic Models (XY)
    TABS-MD and RMA2 (USACE WES)
    WIFM (USACE WES)
    FESWMS (USGS)

## Slide 54: Example of Available Models
Example of a Two-Dimensional Hydrodynamic and Quality Model (XZ)
    CE-QUAL-W2 (USACE WES)

## Slide 55: Example of Available Models
Examples of Three Dimensional Hydrodynamic Models
    CH3D (USACE WES)
    EFDC (Tetra Tech)
    BFHYDRO (ASA)
    GLVHHT (Edinger and Associates)
    TIDE3D (USGS)