## Slide 1: WASP8 Temperature and Light
Processes and Equations Implemented in WASP8
Prepared by
Robert B. Ambrose, Jr.
August, 2016

## Slide 2: Light Module in WASP8 (1)
1. Solar radiation data in the sky (W/m2)
(1) Solar radiation data in the sky
(2) Light intensity at water surface
(3) Light intensity in the water column
(4) Environmental processes driven by light
Eutrophication: Algae growth, microbial, temperature
Toxicant: Organic contaminants and nanomaterials photodegradation
Attenuation by clouds, shading, ice, water reflection
Attenuation by suspended solids, algae, DOC in water
Gold: Data need to be input into WASP by WASP users
White: WASP can calculate itself

## Slide 3: Light Module in WASP8 (2)
2. Solar radiation data at water surface (W/m2)
(1) Solar radiation intensity at water surface (Hourly data available at NLDAS)
(2) Light intensity in the water column
(3) Environmental processes driven by light intensity
Eutrophication: Algae growth, microbial, temperature
Toxicant: Organic contaminants and nanomaterials photodegradation
Attenuation by suspended solids, algae, DOC in water
Gold: Data need to be input into WASP by WASP users
White: WASP can calculate itself

## Slide 4: Solar Radiation and Light Attenuation
Solar Radiation travels and attenuates through atmosphere, changes over the day and throughout year
Light attenuates through the water column varying by wavelength
Phototransformation rates are a function of wavelength intensity

## Slide 5: Solar Radiation
Light intensity, I [W/m2]
  Generally input as total solar radiation
  Temperature is calculated using total solar radiation
  Algal growth is calculated using the visible, photosynthetically active radiation (PAR)
    Default fraction is 46% of total solar radiation
    User must make sure that input light and phytoplankton Isat are in same units
    I [W/m2] = 0.48426 I [Ly/day]
Light extinction coefficient, Ke [1/meter]
  Overall Ke can be specified with parameter and time function
  Best to use model-calculated Ke

## Slide 6
Physical and chemical
  Temperature
  Photolysis
Microbial
  Photo degradation
Algal
  Photosynthesis
Light Affects WQ Reactions

## Slide 7: Solar Radiation Spectrum
https://en.wikipedia.org/wiki/Sunlight

## Slide 8: Solar Radiation Units and Wavelength Distribution
Model default values
  Input units are W/m2 total radiation
  Fraction ultraviolet (275-380 nm) – 0.036
  Fraction visible, or PAR (380-775 nm) – 0.464
  Fraction infrared (775-2500 nm) – 0.500
User-specified input in Constant Group “Light”
  Observed solar radiation time function multiplier
    Specify 0.48426 if input light is in Ly/day
  Fraction of light that is ultraviolet
  Fraction of light that is PAR
  Fraction of light that is infrared

## Slide 9: Solar Radiation Input Options
Light Option (in Constant Group “Light”)
  0: Model calculates clear sky radiation
    Based on user-specified latitude, longitude, and Julian day
    Model calculates diel and seasonal light variations
  1: User specifies time series of instantaneous solar radiation
    Hourly or less time scale
  2: User specifies time series of daily total solar radiation
    Daylight fraction can be specified or calculated internally
    Model calculates diel variation using half-sine curve

## Slide 10: Light Attenuation above the Water
Cloud cover
  Parameter pointer to time function
Shading
  Parameter pointer to time function
Ice
  Fraction surface – parameter and time function
  Thickness – calculated by temperature algorithms
  Reflectance – albedo of ice, in “Water Temperature” constant group
  Extinction coefficient in ice – in “Water Temperature” constant group
Water surface reflectance
  Default is 0.06 reflected
  User specified value in “Water Temperature” constant group

## Slide 11: Light Extinction in Water Column
Ke = 0.5 m-1
Ke = 2 m-1
Surface reflectance loss:
Beer-Lambert light attenuation with depth:
I0 = light just beneath surface, W/m2
Ke = light extinction coefficient, m-1 (0.05-5)
z = depth, m

## Slide 12: Calculated Light Extinction by Wavelength
Ke Water,λ = light extinction of water
Ke Chl,λ = algal self shading
Ke DOC,λ = DOC light extinction
Ke Solids,λ = solids light extinction

## Slide 13: Light Extinction Components
Water:
Solids:
DOC:

## Slide 14: Light Extinction Components
Algal Self Shading (PAR only):
Options:
Model Calculates (Default)
  Mult = 0.0587, Exp= 0.778
User Specifies Mult & Exp
Switch Off Self Shading

## Slide 15: Light Extinction Component Values
Component | uV Internally set | PAR Default values in red Recommended values in blue | IR Internally set
Water [1/m] | 0.11 | 0.10 | 0.50
Chl mult [(1/m)/(ug/L)] | 0.0812 | 0.0587 | 0
Chl exp | 0 | 0.7785 | 0
DOC mult [(1/m)/(mg/L)] | 4.79 | 0.0 (0.43) | 0
Solids mult, [(1/m)/(mg/L)] | 0.34 | 0.0 (0.34) | 0.34

## Slide 16: Simulating Water Temperature

## Slide 17
Physical and chemical
  Reaeration, volatilization
  Hydrolysis, oxidation, reduction (Eact)
Microbial
  Carbonaceous oxidation
  Biodegradation
  Nitrification, denitrification
Algal
  Photosynthesis (θ or Topt)
  Respiration
Temperature
Effects on WQ Reactions
“Theta” Formulation

## Slide 18: Temperature Standards to Protect Aquatic Life
General guidance by EPA
Criteria adopted by States
  Species and life stage
Standards implemented for specific water bodies
  Cold water, warm water reaches
  Season

## Slide 19: Criteria for Freshwater Fish EPA Guidance for Salmonids in Pacific NW
Summer:
  Bull trout rearing: 12C
  Salmon/trout core rearing (middle – upper reaches): 17C
  Salmon/trout noncore rearing (middle – lower reaches): 18C
  Salmon/trout migration: 20C
Spring/fall:
  Bull trout spawning: 9C
  Salmon/trout spawning: 13C
  Steelhead smoltification: 14C
Application of criteria
  Express as 7 day average of daily maximum temperature
  Apply at lowest downstream extent of use

## Slide 20: Technical Issues in Temperature Modeling
Temporal variability
  Diel variation
  Variation with flow regime
    Base flow versus runoff flow
Spatial variability
  Vertical
    Epilimnion, hypolimnion, sediment and pore water
  Longitudinal
    Pools and riffles, channels, shallows
Structures
Terrain and vegetation
Ice

## Slide 21: Heat Exchange Fluxes Typical Mid-Latitude Daily Average, W/m2
250 to 400
Solar Radiation
Atmospheric Radiation
Back Radiation
Conduction
Evaporation
Conduction
Diffusion
30 to 1000
5 to 25
5 to 15
-40 to 60
260 to 420
35 to 350
-5 to 10
Notes: From EPA Rates Manual, p. 62 (units converted from kcal/m2-hr to W/m2

## Slide 22: Heat Exchange Processes
shade
wind
Tair
Tsw
TG
Tair
Tsed
Solar Radiation
Atmospheric Radiation
Back Radiation
Conduction
Evaporation
Conduction
Diffusion
Tsw
Ke
cloud cover
Sr
wind
cloud cover
shade
Tsw
Tdew
freflect
3%
HG
Notes: User-specified input shown in green.

## Slide 23: Equilibrium Temperature Approach
shade
Tsw
TG
Tsed
Solar Radiation
Conduction
Diffusion
Ke
cloud cover
Sr
freflect
Equilibrium Temperature
Teq
= f (Sr, Tair, Tdew, Teq, cloud, wind)
Kaw
= f (Tdew, Teq, wind)
HG
= 10 – 80 W/m2-K
Notes: User-specified input shown in green.
Kaw values from “Heat Disposal in the Water Environment”, E.E. Adams, D.R.F. Harleman, G.H. Jirka, and K.D. Stolzenbach, 1981.

## Slide 24: Heat Exchange Processes - Ice
shade
wind
Tair
Tsw
TG
Tair
Tsed
Solar Radiation
Atmospheric Radiation
Back Radiation
Conduction
Evaporation
Conduction
Diffusion
cloud cover
Sr
wind
cloud cover
shade
Tdew
albedo
3%
Tice
Ke
Kice
Tice
Tice
Ice Melt
dice
Hwi
HG
Tm
Notes: User-specified input shown in green.

## Slide 25: Equilibrium Temperature - Ice
shade
TG
Tsed
Solar Radiation
Conduction
Diffusion
cloud cover
Sr
albedo
Ke
Ke,ice
dice
Tsw
Ice Melt
Equilibrium Temperature
Teq
= f (Sr, Tair, Tdew, Teq, cloud, wind)
Hice-a = 1/Hia + dice/Kice = f (Kaw)
Hwi
Ice Growth, Melt
HG
Tm
Notes: User-specified input shown in green.

## Slide 26: Heat Module -- Systems and Units
Variable | Concentration Units | Loading Units | Internal Mass Units
Temperature | C | kC-m3/day | C-m3

## Slide 27: Heat Module External Loadings
Paired inflows and boundary concentrations are preferred over the use of loadings
If loadings are specified for an inflow, the associated boundary conc. should be left at 0
Calculation of loadings for Qin in [m3/day]:
  For variables in their concentration units:
  Temperature: Lin = Qin * Tin/1000 [kC-m3/day]

## Slide 28: Heat Module Time Functions and Parameters
Observed daily solar radiation (W/m2)
Cloud cover (fraction)
Wind speed (m/sec)
Air temperature (°C)
Dew point (°C)
Shading coefficient (fraction)
Wind sheltering coefficient (fraction)
Light extinction coefficient (1/m)
Time functions 1 - 4 Parameter pointer Parameter multiplier.
Time function (1 only) Parameter multiplier.

## Slide 29: Heat Module Global Constants
Waterbody type (used for density calculations)
  0 = fresh water (default), 1 = salt water
Heat exchange option
  0 = full heat balance, 1 = equilibrium temperature (default)
Ice switch
  0 = no ice solution (default)
  1 = ice solution using equilibrium temperature
  2 = ice solution using detailed heat balance
Latitude, degrees
Longitude, degrees

## Slide 30: Heat Module General Thermal Constants
Observed solar radiation time function multiplier
  Default = 1 for [W/m2]
Fraction of solar radiation reflected at the water surface
  Default = 0.06
Coefficient of bottom heat exchange (Watts/m2-K)
  Suggested range = 0.2 to 0.8
Sediment (ground) temperature (°C)
  Suggested value = average air temperature
  Default = 10 °C

## Slide 31: Heat Module Thermal Constants - Ice
Initial ice thickness (m)
Ratio of reflection to incident radiation (albedo of ice)
  Suggested value = 0.25
Coefficient of water-ice heat exchange (Watts/m2-K)
  Suggested value = 10
Fraction of solar radiation absorbed in the ice surface
  Suggested value = 0.6
Solar radiation extinction coefficient for ice (1/meter)
  Suggested value = 0.07
Minimum ice thickness before ice formation allowed (m)
  Suggested value = 0.01 for streams; default = 0.005
Temperature above which ice formation not allowed (°C)