## Slide 1: The WASP8 Advanced Phytoplankton Processes
Processes and Equations Implemented in WASP8 Eutrophication Modules
Prepared by
Robert B. Ambrose, Jr.
July, 2017

## Slide 2: Variables and Processes
Periphyton Biomass
D : C : N : P : Chl
IP
IN
Phytoplankton Biomass
Group 3
D : C : N : P : Si: Chl
DO
Group 2
D : C : N : P : Si: Chl
Group 1
D : C : N : P : Si : Chl
TIC
H2CO3 – HCO3- – CO32-
Total
Alkalinity
Particulate Detrital OM
Si
P
N
C
D
Dissolved OM
Si
P
N
CBOD1
CBOD2
CBOD3
Inorganic Nutrients
NO3
PO4
SiO2
NH4
pH
atmosphere
uptake
excretion
Inorganic Solids
S3
S1
S2
oxidation
oxidation
nitrification
photosynthesis and respiration
death
dissolution
mineralization
sorption
reaeration

## Slide 3: Phytoplankton Biomass Cell Composition
Typical Dry Weight Stoichiometry
C106H263O110N16P1
Dry Weight Fractions |  | 
C | N | P
40% | 7.2% | 1%

## Slide 4: Phytoplankton Biomass Nutrient Ratios
Symbol | Description of kinetic constant | Units | Value | Range
DCRB | detritus to carbon ratio | gD/gC | 4 | 2 – 5
NCRB | nitrogen to carbon ratio | gN/gC | 0.18 | 0.15 – 0.25
PCRB | phosphorus to carbon ratio | gP/gC | 0.025 | 0.01 – 0.05
SiCRB | silicon to carbon ratio | gSi/gC | 0.8 | 0.5 – 2.5
CChla | carbon to chlorophyll ratio | gC/gChl | 50 | 25 – 125

## Slide 5: Phytoplankton Kinetic Processes
PO4
NO3
NH4
Light
Detrital
C,N,P, Si
DON, DOP,
DOSi, CBODi
SiO2
Phytoplankton Biomass
Group 3
D : C : N : P : Si: Chl
Group 2
D : C : N : P : Si: Chl
Group 1
D : C : N : P : Si : Chl
Zooplankton
Temperature
kDi
kRi
kGi
kRi
ksi
Salinity

## Slide 6: Phytoplankton Kinetic Equation
Where, for phytoplankton “i”: | 
Pci = | phytoplankton carbon concentration (mg/L)
kGi = | growth rate constant (1/day)
kRi = | respiration rate constant (1/day)
kDi = | overall death rate constant (1/day)
ksi = | settling rate constant (1/day)

## Slide 7: Phytoplankton Growth Equation
Where, for phytoplankton “i”: | 
kGmax,i = | maximum specific growth rate constant at 20 C, day-1 (2.5, 0.5 – 4.0)
XTi = | temperature growth multiplier (0 – 3)
XLi = | light growth multiplier (0 – 1)
XNi = | nutrient growth multiplier (0 – 1)
Growth rate constant for phytoplankton “i” (day-1):

## Slide 8: Standard Temperature Function for Phytoplankton Growth
Temperature multiplier:
Where, for phytoplankton “i”: | 
θGi = | temperature correction factor for growth (1.07, 1.05 – 1.1)
T = | water temperature, C
=

## Slide 9: Additional Temperature Function for Phytoplankton Growth*
Temperature multiplier:
* From Cerco and Cole, 1995, CE-QUAL-ICM
Where, for phytoplankton “i”: | 
Topt,i = | optimum temperature for growth, C (20, 10 – 27)
κ1i = | temperature coefficient below optimum, 1/C2 (0.024, 0.005 – 0.04)
κ2i = | temperature coefficient above optimum, 1/C2 (0.024, 0.005 – 0.04)

## Slide 10: Comparison of Temperature Functions
TF1 = | exponential temperature function, θG = 1.08
TF2a = | Topt temperature function: κ1, κ2 = 0.02
TF2b = | Topt temperature function: κ1, κ2 = 0.002

## Slide 11: Light Limitation of Phytoplankton Growth
Steele light limitation function:
Where, for total light energy (values are half for photosynthetically active radiation, PAR): | 
It,z = | light intensity at time t and depth z, W/m2 (0 – 200 daily average PAR), (0 – 600 instantaneous)
ISi = | saturating light intensity for phytoplankton “i”, W/m2 (60, 25 – 125 PAR)

## Slide 12: Light Limitation Function Depth Integrated
Steele function integrated over depth:
Where: | 
H = | segment depth, m
Ke = | segment light extinction coefficient , 1/m
I0 = | light intensity at top of segment, W/m2
ISi = | saturating light intensity for phytoplankton “i”, W/m2

## Slide 13: Nutrient Limitation of Phytoplankton Growth
Where, for phytoplankton “i”: | 
KMN,i = | half-saturation constant for N, mg/L (0.02, 0.005 – 0.40)
KMP,i = | half-saturation constant for P, mg/L (0.008, 0.001 – 0.08)
KMSi,i = | half-saturation constant for Si, mg/L (0.04, 0.02 – 0.10)

## Slide 14: Half-Saturation Nutrient Kinetics
Nutrient | KM, mg/L | Ref.
N | 0.001 – 0.40 | 1
 | 0.025 | 2
 | 0.010 – 0.020 | 3
P | 0.0005 – 0.08 | 1
 | 0.001 | 2
 | 0.001 – 0.005 | 3
Si | 0.020 – 0.080 | 3
1 | Bowie, et al., 1985
2 | Potomac River
3 | Thomann and Mueller, 1987

## Slide 15: Phytoplankton Attenuation
Where, for phytoplankton “i”: | 
Pci = | phytoplankton carbon concentration (mg/L)
kRi = | respiration rate constant (1/day)
kDi = | overall death rate constant (1/day)
ksi = | settling rate constant (1/day)

## Slide 16: Phytoplankton Respiration
Respiration rate constant, including excretion fraction (i.e., photorespiration):
Where, for phytoplankton “i”: | 
k20Ri = | respiration rate constant at 20 C, 1/day (0.1, 0.05 – 0.25)
θRi = | temperature correction factor for respiration (1.07, 1.05 – 1.08)
fON = | ON excretion fraction of respiration rate (0.2, 0.05 – 0.5)
fOP = | OP excretion fraction of respiration rate (0.2, 0.05 – 0.5)
fOSi = | OSi excretion fraction of respiration rate (0.2, 0.05 – 0.5)

## Slide 17: Phytoplankton Death
Overall death rate constant:
Where, for phytoplankton “i”: | 
kmi = | mortality rate constant, 1/day (0.02, 0.003 – 0.1)
kgraze,i = | grazing rate constant, 1/day (0.1, 0.0 – 0.2)
kgraze,i = | grazing rate constant, m3/gZ-day (0.2, 0.0 – 0.5)
Z = | zooplankton biomass (parameter and time function), gZ/m3
ksaltox,i = | salt toxicity death rate constant, 1/day
Ksaltox,i = | salt toxicity half-saturation constant, PSU
Si = | salinity, PSU

## Slide 18: Phytoplankton Settling
Settling rate constant:
Where, for phytoplankton “i”: | 
vSi = | settling velocity, m/day (0.03, 0.005 – 0.2)
AS = | segment surface area, m2
V = | segment volume, m3

## Slide 19: Advanced Eutro Module Phytoplankton Constants

## Slide 20: Summary of Kinetic Constants Phytoplankton Biomass
Symbol | Description of kinetic constant | Units | Value | Range
DCRB | detritus to carbon ratio | gD/gC | 4 | 2 – 5
NCRB | nitrogen to carbon ratio | gN/gC | 0.18 | 0.15 – 0.25
PCRB | phosphorus to carbon ratio | gP/gC | 0.025 | 0.01 – 0.05
SiCRB | silicon to carbon ratio | gSi/gC | 0.8 | 0.5 – 2.5
CChla | carbon to chlorophyll ratio | gC/gChl | 50 | 25 – 125

## Slide 21: Summary of Kinetic Constants Phytoplankton Growth
Symbol | Description of kinetic constant | Units | Value | Range
kGmax,i | maximum growth rate constant | 1/day | 2.5 | 0.5 – 4.0
θGi | temperature correction factor |  | 1.07 | 1.05 – 1.1
Topt,I | optimum temperature for growth | C | 20 | 10 - 27
κ1i, κ2i | temperature coefficients below and above optimum | 1/C2 | 0.024 | 0.005 – 0.04
Isi | saturating light intensity (total) | W/m2 | 125 | 50 – 250
Isi | saturating light intensity (PAR) | W/m2 | 60 | 25 – 125
KMN,i | half-saturation constant for N | mg/L | 0.02 | 0.005 – 0.40
KMP,I | half-saturation constant for P | mg/L | 0.008 | 0.001 – 0.08
KMSi,I | half-saturation constant for Si | mg/L | 0.04 | 0.02 – 0.10

## Slide 22: Summary of Kinetic Constants Phytoplankton Attenuation
Symbol | Description of kinetic constant | Units | Value | Range
k20Ri | respiration rate constant at 20 C | 1/day | 0.1 | 0.05 – 0.25
θRi | temperature correction factor |  | 1.07 | 1.05 – 1.08
fOnutr | organic nutrient excretion fractions |  | 0.2 | 0.05 – 0.5
kmi | mortality rate constant | 1/day | 0.02 | 0.003 – 0.1
kgraze,i | grazing rate constant (1st order) | 1/day | 0.1 | 0.0 – 0.2
kgraze,i | grazing rate constant (2nd order) | m3/gZ-d | 0.2 | 0.0 – 0.5
ksaltox,i | salt toxicity death rate constant | 1/day |  | 0.0 – 0.5
Ksaltox,i | salt toxicity half-saturation constant | PSU | 0.0 | 0.0 – 30
vSi = | settling velocity | m/day | 0.03 | 0.005 – 0.2

## Slide 23: Advanced Eutro Module Phytoplankton Time Functions - Parameters
Water temperature [°C]
Zooplankton density
Time function
Parameter multiplier
Time function (for each phyto)
Parameter multiplier

## Slide 24: Advanced Eutro Module Phytoplankton Display Variables
Num | Variable | Units
28 | Phytoplankton Carbon | mgC/L
29 | Phytoplankton Chlorophyll a | μg/L
30 | Phytoplankton Growth Rate | day-1
31 | Phytoplankton Death Rate | day-1
32 | Phytoplankton DO Production | mgDO/L/day
33 | Phytoplankton DO Consumption | mgDO/L/day
34 | Phytoplankton C:Chla Ratio | mgC/mgChla
35 | Phytoplankton Light Limit | -
36 | Phytoplankton Nutrient Limit | -
37 | Phytoplankton Nitrogen Limit | -
38 | Phytoplankton Phosphorus Limit | -