## Slide 1: Sorption and Equilibrium Partitioning
Summary of Process Equations and Model Input Data

## Slide 2: Sorption
Definition
  Movement of chemical between the dissolved phase and particulate or solid phase
  The chemical may be physically associated or chemically bound through attachment to functional groups on the surface of the solid.
Cdiss
Csorbed
K
Solid
particle

## Slide 3: Important Factors
Characteristics of the Chemical
  for neutral organics sorption is related to the hydrophobicity of the solid.
Characteristics of the Solid
  Size (sand, silt, clay)
    specific surface area
    cation exchange capacity
  Organic Carbon Content
Characteristics of the Aqueous Solution
  Presence of dissolved & colloidal organics such-as humic acid
  pH
  Temperature

## Slide 4: Implications of Sorption
Microbial degradation rates can be altered
Volatilization is diminished
Direct photolysis is inhibited
Transport is altered

## Slide 5: Sorption Assumption
Kinetic Equilibrium
  Available models assume
    Rate of adsorption >> any other transport or kinetic process affecting the chemical
    On the time scale of all other processes sorption appears to be at equilibrium.
Therefore, kinetics are not considered. Sorption is instantaneous

## Slide 6: Adsorption Isotherms
Linear Isotherm
Csorbed [mg sorbed/kg solid]
Cdissolved [mg dissolved/L water]
Freundlich Isotherm
Langmuir Isotherm

## Slide 7: Basic Relationships
WASP uses Linear Sorption Equilibrium Assumption
Kd = Partition Coefficient [L/kg]
Cdissolved = Dissolved Chemical [mg/L]
Csorbed = Sorbed Chemical [mg/kg]
Total Chemical, CT, is sum of sorbed/particulate and dissolved chemical
Kd,i = Partition Coefficient associated with solid particle, i [L/kg]
n = number of solid particle types
= porosity [liquid volume/total volume]
Si = Concentration of Solid Particle, i [mg/mg]
Cidissolved = Cdissolved Dissolved Chemical Associated with Environment, E
(solids + water) [mg/L]
Ciparticulate = Cisorbed * Si Chemical Sorbed to Solid Particle, i [mg/L]

## Slide 8: Basic Relationships
Fractional Representation of Dissolved and Sorbed Concentrations
Defining the fraction dissolved and sorbed as
Cidissolved = fdCT and Cisorbed = fP,iCT
Then each fraction can be represented by
and

## Slide 9: Hydrophobic Organic Sorption
Sites = Organic Matter on Particulate
KD = fOC*KOC
log KOC
log KOW
Relationship between KOC and KOW
EXAMS:
KOC = 0.41* KOW
Karickhoff:
log KOC = log KOW - 0.21
Schwarzenbach:
log KOC = 0.72 log KOW +0.49

## Slide 10: Sorption Input Data
In “Constants Data”
  Chemical 1,2,3
    Log KOC
    Log KOW
    KOW - KOC Intercept
    KOW - KOC Slope
    Solid 1, 2, and 3
      KPO
    KDOC
In “Parameter Data”
  Turn On
    Dissolved Organic Carbon [mg/L]
    Fraction Organic Carbon for Solids 1, 2, and 3.
In “Segments Data”
  Parameters
    Dissolved Organic Carbon [mg/L]
    Fraction Organic Carbon for Solids 1, 2, and 3.

## Slide 11
Chemical 1
Chemical 2
Chemical 3

## Slide 12
Dissolved
Organic
Carbon
Turn on
Sorption
Parameters
Fraction
Organic
Carbon
Turn on Parameters

## Slide 13
Fraction Organic Carbon for Solids Type 1
Parameter Tab
in “Segments”
Dissolved Organic Carbon
Fraction Organic Carbon for Solids Type 2
Fraction Organic Carbon for Solids Type 3