## Slide 1: Light and Phototransformations
Processes and Equations Implemented in WASP8
Prepared by
Robert B. Ambrose, Jr.
August, 2016

## Slide 2: Light Module in WASP8 (1)
1. Solar radiation data in the sky (W/m2)
(1) Solar radiation data in the sky
(2) Light intensity at water surface
(3) Light intensity in the water column
(4) Environmental processes driven by light
Eutrophication: Algae growth, microbial, temperature
Toxicant: Organic contaminants and nanomaterials photodegradation
Attenuation by clouds, shading, ice, water reflection
Attenuation by suspended solids, algae, DOC in water
Gold: Data need to be input into WASP by WASP users
White: WASP can calculate itself

## Slide 3: Light Module in WASP8 (2)
2. Solar radiation data at water surface (W/m2)
(1) Solar radiation intensity at water surface (Hourly data available at NLDAS)
(2) Light intensity in the water column
(3) Environmental processes driven by light intensity
Eutrophication: Algae growth, microbial, temperature
Toxicant: Organic contaminants and nanomaterials photodegradation
Attenuation by suspended solids, algae, DOC in water
Gold: Data need to be input into WASP by WASP users
White: WASP can calculate itself

## Slide 4: Solar Radiation and Light Attenuation
Solar Radiation travels and attenuates through atmosphere, changes over the day and throughout year
Light attenuates through the water column varying by wavelength
Phototransformation rates are a function of wavelength intensity

## Slide 5: Solar Radiation Spectrum
https://en.wikipedia.org/wiki/Sunlight

## Slide 6: Solar Radiation
Light intensity, I [W/m2]
  Generally input as total solar radiation
  Temperature is calculated using total solar radiation
Light extinction coefficient, Ke [1/m]
  Overall Ke can be specified with parameter and time function
  Best to use model-calculated Ke

## Slide 7
Physical and chemical
  Temperature
  Phototransformations
Microbial
  Photo degradation
Algal
  Photosynthesis
Light Affects WQ Reactions

## Slide 8: Solar Radiation Units and Wavelength Distribution
Input units are W/m2 total radiation
User-specified input in Constant Group “Light”
  Observed solar radiation time function multiplier
    Specify 0.48426 if input light is in Ly/d
  Fraction of light that is ultraviolet (Default 0.036)
  Fraction of light that is PAR (Default 0.464)
  Fraction of light that is infrared (Default 0.500)

## Slide 9: Division of Wavelengths by Latitude
Index | Color | Wavelengths [nm] | 0o N | 10 o N | 20 o N | Latitude 30 o N | 40 o N | 50 o N | 60 o N
1 | UVB med | 295 – 304 | 0.00015 | 0.00015 | 0.00013 | 0.00011 | 0.00008 | 0.00006 | 0.00004
2 | UVB high | 305 – 314 | 0.00142 | 0.00139 | 0.00132 | 0.00120 | 0.00104 | 0.00085 | 0.00067
3 | UVA low | 315 – 334 | 0.00845 | 0.00839 | 0.00825 | 0.00801 | 0.00766 | 0.00721 | 0.00681
4 | UVA med | 335 – 354 | 0.01141 | 0.01137 | 0.01126 | 0.01108 | 0.01082 | 0.01052 | 0.01054
5 | UVA high | 355 – 379 | 0.01723 | 0.01718 | 0.01706 | 0.01686 | 0.01655 | 0.01619 | 0.01630
6 | violet | 380 – 449 | 0.07626 | 0.07617 | 0.07593 | 0.07550 | 0.07482 | 0.07394 | 0.07443
7 | blue | 450 – 494 | 0.06664 | 0.06663 | 0.06659 | 0.06652 | 0.06639 | 0.06616 | 0.06644
8 | green | 495 – 569 | 0.10386 | 0.10388 | 0.10394 | 0.10402 | 0.10406 | 0.10390 | 0.10285
9 | yellow-orange | 570 – 619 | 0.06546 | 0.06549 | 0.06556 | 0.06566 | 0.06576 | 0.06568 | 0.06422
10 | red | 620 – 749 | 0.14914 | 0.14934 | 0.14995 | 0.15106 | 0.15282 | 0.15550 | 0.15769

## Slide 10: Solar Radiation Input Options
Light Option (in Constant Group “Light”)
  0: Model calculates clear sky radiation
    Based on user-specified latitude, longitude, and Julian day
    Model calculates diel and seasonal light variations
  1: User specifies time series of instantaneous solar radiation
    Hourly or less time scale
  2: User specifies time series of daily total solar radiation
    Daylight fraction can be specified or calculated internally
    Model calculates diel variation using half-sine curve

## Slide 11: Light Attenuation above the Water
Cloud cover
  Parameter pointer to time function
Shading
  Parameter pointer to time function
Ice
  Fraction surface – parameter and time function
  Thickness – calculated by temperature algorithms
  Reflectance – albedo of ice, in “Water Temperature” constant group
  Extinction coefficient in ice – in “Water Temperature” constant group
Water surface reflectance
  Default is 0.06 reflected
  User specified value in “Water Temperature” constant group

## Slide 12: Light Extinction in Water Column
Ke = 0.5 m-1
Ke = 2 m-1
Surface reflectance loss:
Beer-Lambert light attenuation with depth:
I0 = light just beneath surface, W/m2
Ke = light extinction coefficient, m-1 (0.05-5)
z = depth, m

## Slide 13: Calculated Light Extinction by Wavelength
Ke Water,λ = light extinction of water
Ke Chl,λ = algal self shading
Ke DOC,λ = DOC light extinction
Ke Solids,λ = solids light extinction

## Slide 14: Light Extinction Components
Index | Color | Water [m-1] | Chlorophyll [m-1 (ug/L)-1] | DOC [m-1 (mg/L)-1] | Solids [m-1 (mg/L) -1]
1 | UVB med | 0.151 | 0.103 | 6.22 | 0.34
2 | UVB high | 0.109 | 0.0816 | 5.40 | 0.34
3 | UVA low | 0.0805 | 0.069 | 4.59 | 0.34
4 | UVA med | 0.0512 | 0.057 | 3.40 | 0.34
5 | UVA high | 0.0340 | 0.053 | 2.54 | 0.34
6 | violet | 0.0169 | 0.039 | 1.266 | 0.34
7 | blue | 0.0166 | 0.0262 | 0.514 | 0.34
8 | green | 0.0475 | 0.0143 | 0.289 | 0.34
9 | yellow-orange | 0.217 | 0.0063 | 0.115 | 0.34
10 | red | 1.007 | 0.0065 | 0.0 | 0.34
11 | infrared | 2.07 | 0.0 | 0.0 | 0.34
WASP simulates the attenuation of 10 bands of light

## Slide 15: Phototransformations
Wavelength-dependent reaction rate for each wavelength band
Rate constant per wavelength
Overall rate constant for all photoreactions

## Slide 16: Light Example

## Slide 17: Incident Light
Using Option 0, Location needs to be entered
Athens, GA is 33° N, 83° W.

## Slide 18: Incident Light
Choose Light Option 0
Fraction reflected, 0.06
Set fractions of light,
0.464 PAR
0.5 IR
0.036 UV

## Slide 21: Phototransformations
On Constants, Chemical Photolysis
  Enter Reaction Rates for each wavelength band
  0.1 d-1 (W/m2)-1