## Slide 1: Sediment Transport 2: Simple Transport
Theory and Implementation in WASP7
Prepared by
Robert B. Ambrose, Jr.
April, 2010

## Slide 2: Average Solids Transport Rates from Observations and Mass Balance
Solve for WR :
Surface Water
Surface Sediment
Subsurface Sediment
WD
WR
WB1
SW
SB1
Wi = solids velocity, m/day
Si = solids conc, g/m3
Fi = solids flux, g/m2/day
= Wi × Si
Long-term average solids flux balance:
WD × SW = WR × SB1 + WB1 × SB1
WR = WD × (SW / SB1 ) - WB1
Mass Balance Components:

## Slide 3: Settling Velocities, Ws from Stokes:
where:
g = acceleration of gravity, 9.81 [m/sec2]
m = absolute viscosity of water
= 0.001 poise [kg/m-sec] at 20oC
ρs = sediment particle density [kg/m3]
ρ = water density [kg/m3]
D = particle diameter [m]

## Slide 4: Stokes Settling Velocities, m/day
Particle Diameter, mm | Particle Density, g/cm3 |  |  | 
 | 1.8 | 2.0 | 2.5 | 2.7
Fine Sand |  |  |  | 
0.1 | 380 | 470 | 710 | 800
0.05 | 94 | 120 | 180 | 200
Silt |  |  |  | 
0.05 | 94 | 120 | 180 | 200
0.02 | 15 | 19 | 28 | 32
0.01 | 3.8 | 4.7 | 7.1 | 8.0
0.005 | 0.94 | 1.2 | 1.8 | 2.0
0.002 | 0.15 | 0.19 | 0.28 | 0.32
Clay |  |  |  | 
0.002 | 0.15 | 0.19 | 0.28 | 0.32
0.001 | 0.04 | 0.05 | 0.07 | 0.08

## Slide 5: Sediment Transport Processes - noncohesive deposition
Noncohesive deposition is settling attenuated by the shear stress from water flow:
Stream sedimentation regimes
αD = probability of deposition upon contact with bed; varies roughly linearly from 1 to 0 (Krone, 1963):
αD = 1, = 0
αD = 0, ≥
where = 0.01 to 0.2 N/m2

## Slide 6: Sediment Transport Processes - burial
Burial velocities from any specified layer k are given by mass balance over solids types i.
Surficial sediment layer, k=1, bottom water = 0:
Subsurface sediment layers:
Where WD is deposition velocity, WR is resuspension velocity, WBL is bed load velocity, k is solids degradation rate constant, and d is layer depth.

## Slide 7: Implementation in WASP

## Slide 8: Systems Data
If unchanged, particle density defaults to 2.65 g/mL
If unchanged, maximum concentration for solids defaults to 3.0e+6 mg/L
This example shows the non-ionizing toxicant module.

## Slide 9: Segment Data
Input segment volumes, m3
Input segment depths, m
Specify segment types
Map bottom segments
Input segment descriptions

## Slide 10: Initial Conditions
In this example, the sediment bed is initially composed entirely of sand. Total dry density is 1 g/mL in the surface layer and 1.5 g/mL in the subsurface layer.
This example shows the non-ionizing toxicant module.

## Slide 11: Solids Loadings, 1
WASP displays the variable name and its concentration unit (not the units for loading)
To insert a loading function, highlight the variable name and right-click, then select a segment from the drop down menu.
This example shows the non-ionizing toxicant module.

## Slide 12: Solids Loadings, 2
ALL LOADING VALUES ARE IN [kg/day]!
Specify the dates, times, and values for the loading time function.

## Slide 13: Solids Flow Fields
Point and press “Insert” twice

## Slide 14: Solids Settling Data
days/second
surface area, m2
Settling velocity, m/day

## Slide 15: Solids Kinetic Data
Constants and Parameters are linked. Their product gives segment-specific production and dissolution rates.

## Slide 16: Pond Solids Example - External Parameters
Surface Water
Depth, 1 m
Surface Area, 104 m2
Surface Sediment, 2 cm
Subsurface Sediment, 5 cm
Water, 104 m3/day
Silt, 60 kg/day
Sand, 40 kg/day
Inflow

## Slide 17: Pond Solids Example – Internal Parameters
POM Dissolution, 0.004 day-1
Internal Biotic Production,
2 g/m3-day
Sand, 1.0 g/mL, Silt and POM, 0 g/mL
TSS
(Silt and POM)
Sand, 1.5 g/mL, Silt and POM, 0 g/mL
Deposition, 0.5 m/day
Resuspension, 0.05 mm/day

## Slide 18: Simulated Water Column Solids

## Slide 19: Simulated Surficial Benthic Solids

## Slide 20: Simulated Subsurface Benthic Solids

## Slide 21: Simulated Burial Rates