## Slide 1: Boundary Conditions & Pollutant Loads

## Slide 2: What is a Boundary?
Any Exchange of Water from outside the model network in or from inside the network to the outside.
1
2
3
4
5
6
Boundary
Boundary
We designate Boundaries as Segment 0
Limitation in WASP
Only 1 Boundary Per Segment

## Slide 3: What is a Boundary?
Defines Mass entering network
WASP Calculates Mass Leaving
What if Flow Reverses?
Implication of Boundaries
  Boundary concentrations (BCs) must be specified with reasonable accuracy
    Unknown BC is OK only if insensitive (i.e., changes in BC do not significantly change model prediction in Area of Interest)
    If the BC is sensitive and unknown, then extend the boundary location away from Area of Interest
Mass Loading = Flow ∙ Concentration

## Slide 4: Implication of Boundaries
  Boundary concentrations (BCs) must be specified with reasonable accuracy
    Unknown BC is OK only if insensitive (i.e., changes in BC do not significantly change model prediction in Area of Interest)
    If the BC is sensitive and unknown, then extend the boundary location away from Area of Interest

## Slide 5: Specifying Boundaries
Boundaries are defined by
  User Specified Flow Paths
  User Specified Dispersion Paths
  Read from Hydrodynamic Interface File

## Slide 6: Boundaries
Steps to specify boundary concentrations (BCs):
    Boundary Segments are determined from the Transport (Dispersion/Flow) Screens
    Highlight segment
    In bottom window, fill in concentration values (mg/L) for beginning and ending times
    As needed, add time rows by pressing “+ Insert” and edit Date, Time, and Value
    Continue entering BC data for all variables and boundary segments
    Press “iOK” and save

## Slide 7: Loads
Mass per Time into Model Network
  kg/day
Loading Pathways
  Atmospheric Deposition
  Groundwater Infiltration
  Municipal, Industrial Discharge
  Watershed Runoff and Erosion

## Slide 8: Loading Pathways
Direct Discharges (i.e., point sources)
External Loadings (i.e., non-point sources)
  Watershed Models
  Spreadsheet Tools
  Monitoring Data

## Slide 9: Direct Loading Time Functions
Flows, dispersion coefficients, boundary concentrations, and point source loads follow user-specified time functions, with linear interpolation between points; loading values may be specified at arbitrary intervals (fractions of a day to thousands of days):

## Slide 10: Direct Loads
Steps to specify loads:
    Select Add/Remove Loads
    Select Segment to Receive Load
    Click on State Variable to define load
    Enter Time Series in lower panel
    Press “iOK” at bottom of dialogue box

## Slide 11: Questions ?