## Slide 1: Introduction to Modeling Lakes and Reservoirs using WASP
General Characteristics of Lakes and Reservoirs

## Slide 2: General Characteristics
Lakes and reservoirs are lentic (from lenis, meaning calm) systems, characterized by standing water.
The impacts of the standing nature of lakes and reservoirs include:
  Velocities are much lower than in rivers and streams so that water quality constituents and contaminants are moved slowly.
  Wind mixing and solar heating dominant gravity-driven flow.
  Water is stored for relatively long periods of time
  The increased storage or residence time allows for internal cycling and matter originating within the lake or reservoir (autochthonous materials) to have an increased importance relative to materials originating outside and carried in to the lake or reservoir (allochthonous materials).

## Slide 3: General Characteristics
Lakes and reservoirs are generally much deeper than streams and rivers
  Light does not penetrate to the bottom of many lakes and reservoirs so that heat exchange and productivity is limited to surface layers.
  Stratification retards vertical mixing during periods of the year and large vertical gradients in temperature, density, and water quality often result.

## Slide 4: Factors Distinguishing Lakes and Reservoirs
    Reservoirs much more common in the south than natural lakes
    Reservoirs are mainly formed by damming a steep sided valley with a concrete structure, like Hoover Dam, or an earthen embankment.
    Reservoirs differ primarily from lakes in that their out-flows and volumes are regulated to achieve a beneficial use. The degree of regulation, and the manner in which the reservoirs are operated has a large influence on transport and mixing patterns within the reservoir and, consequently, the water quality within the reservoir and of its releases

## Slide 5: Hydropower Facilities
    Hydropower releases
      Many dams built for hydropower are constructed in areas where steep slopes allow sufficient head drop to generate electricity.
        Base load hydropower: constant or unregulated flows
        Peaking operations, where the reservoir stores water for release when electrical power demands are greatest, such as in the morning or evening.

## Slide 6: Reservoirs: Storage Areas
Useful storage: reservoirs authorized for a variety of uses. Some uses often result in conflict, particular for what were considered secondary uses (recreation, fisheries management, water quality enhancement).

## Slide 7: Reservoirs: Storage Areas
The storage may be used for:
  Flood control and mitigation
  Water supply
  Hydropower
  Navigation
  Recreation
  Water quality enhancement
  Fisheries management

## Slide 8: Processes Impacting Water Quality
Physical Processes:
Lake Morphometry
Stratification
Inflow and Outflow Mixing

## Slide 9: Lake Morphometry
Shapes:
  Artificial impoundments almost always made by damming a river and tend to be dendritic and elongated
  Lakes tend to be less elongated and more round
Size
  Important factors are volumes (affecting residence time), depth, and interfacial areas

## Slide 10
Metalimnion
Hypolimnion
Epilimnion
Cold, complete mixing
DO low or absent
increased reduced materials (Fe, Mn, metals)
Warm, complete mixing
Abundant DO
Productive
Sediments: region of sorption and release
Water Surface
Heat and DO Exchange
wind

## Slide 11
Source: EPA Workshop notes

## Slide 12: Mixing Processes
Mixing may be due to
  The mixing energy that results from inflows,
  The mixing energy from outflows or withdrawals, and
  The transfer of energy across the air-water interface due to wind and other meteorological conditions
The relative importance of the mixing processes may vary widely along the length of a reservoir as well as with depth

## Slide 13
Source: Martin and McCutcheon 1998

## Slide 14
Lacustrine
Zone of
Transition
Riverine

## Slide 15: Outflow mixing processes
Outflow mixing affected by
  Location, size and characteristics of outflow port
  Magnitude of withdrawal
  Stratification
Source: Martin and McCutcheon 1998

## Slide 16: Water Balance for a Lake or Reservoir
Computed from a mass balance for water
where S is storage

## Slide 17: Components of the Water Balance
Storage
  The actual volume of water in the lake or reservoir at any given time
  Not measured directly but is inferred from lake stage and bathymetry measurements, reduced to a relationship between lake stage and storage
  Sources of error
    Errors in measurements of stage
    Month to month temperature changes increase or decrease the density of water
    Measurements of bathymetry are inexact or may be out of date

## Slide 18: Components of the Water Balance
Inflows
  Usually obtained from USGS or other gaging stations
  Sources of error
    Error in gage measurements
    Ungaged areas below station
    Ungaged tributaries
    Non-point source (distributed inflows)

## Slide 19: Components of the Water Balance
Outflows
  usually measured at control structure
  Sources of error
    Seepage or leakage flows through turbines may be large
    Some flows may be ungaged

## Slide 20: Components of the Water Balance
Direct precipitation onto lakes surface
  Measured using standard rain gage and converted to flow by surface area
  Sources of error
    Localized nature of rain

## Slide 21: Components of the Water Balance
Evaporation
  Usually measured using the standard Class A pan or computed from energy balance
  Sources of error
    Errors in pan measurement
    Transpiration

## Slide 22: Components of the Water Balance
Ground water seepage and infiltration
  Usually estimated by difference in the water balance but may be estimated from ground water models or seepage meters
  Sources of error
    Difficult to measure
    Cumulative errors in other terms of water balance if estimated by difference

## Slide 23: Components of the Water Balance
Methodology for typical application
  Obtain records of outflows and estimates of seepage losses
  Obtain records of water surface elevations
  Obtain storage capacity curve for reservoir
  Estimate all inflows and losses (gaged and ungaged inflows, precipitation, evaporation, groundwater infiltration/seepage)

## Slide 24: Components of Water Balance
Methodology (continued)
  Estimate total inflows from stage, discharge, and storage capacity curve
    From stage and storage capacity curve, estimate storage
    From mass balance equation, compute inflows

## Slide 25: Components of Water Balance
Methodology (cont)
  Example for storage induction method (using averages of values at time 1 and time 2 (time 1 + t)
  Since S (storage) and O (outflow) are known, can solve for inflow (I)

## Slide 26: Components of Water Balance
Methodology (continued)
  Once the total inflow is known, it can be compared to the inflow computed from all sources
  Errors can be corrected by additional studies or field measurement

## Slide 27: Components of Water Balance
For water quality modeling, concentrations for all constituents modeled must be determined for each inflow source

## Slide 28: Example of a Whole Lake Model
constituent mass balance
water balance

## Slide 29: Whole Lake Models
Have been widely used in modeling eutrophication and toxics
Example: Lake Ontario has been modeled using this approach
  Overall average assumption is that it is completely mixed

## Slide 30: Example of a Two-layer Lake Model
constituent mass balance
water balance
hypolimnion
epilimnion
hypolimnion
epilimnion

## Slide 31: Two Layer Model (or Greater Segmentation)
Have to determine
  Volumes and shapes for individual layers
  Where the inflows go
  Where the outflows come from
    Note in the previous slide we assumed all the inflows and outflows were confined to the epilimnion (not necessarily a good assumption, see inflow mixing)
  Vertical exchange coefficient

## Slide 32: Inflow Placement
Often estimated from density alone
Plume methods available to compute whether an overflow, underflow, or interflow (see Martin and McCutcheon 1998)

## Slide 33: Outflow Envelope
Estimated from density pattern
Estimated using models such as SELECT (from USACOE WES)
  SELECT is incorporated into WES’s reservoir models (CE-QUAL-R1 and CE-QUAL-W2)
  Can also be run as stand alone program
    Requires structure of port
    Outflow rates and thermal profile (and constituent profile)
    Estimates withdrawal locations, temperatures and concentrations of other materials in outflows

## Slide 34: Estimation of Vertical Exchange Rate
May be estimated from seasonal changes in temperatures of the hypolimnion
May be estimated by model calibration

## Slide 35: Estimation of Vertical Exchange Rate
where
May be estimated from empirical equations

## Slide 36: Estimation of Vertical Exchange Rate
Or, in other words
  There is a normal rate of vertical exchange (Ez,o) that occurs in the absence of stratification
  That rate is reduced by stratification or the stability of the stratification [f(s)]
  The stability can be estimated from the ratio of the buoyancy of the system (density differences) that oppose the mixing to the force (due to wind) that would cause mixing (the Ri or Richardson number)

## Slide 37: Lakes: Modeling Approaches
Steady-state models (rarely used)
Dynamic analysis (usually required)
  Whole lake models
  Segmentation using box modeling approach
  One-dimensional (vertical) models
  Two-dimensional (longitudinal-vertical) models
  Three dimensional models

## Slide 38: Examples of Available Models
Box type models
  WASP (US EPA)
  BETTER (TVA)
  CE-QUAL-ICM (US COE WES)
One-dimensional (vertical) models
  CE-QUAL-R1 (US COE WES)
Two-dimensional (longitudinal-vertical)
  -CE-QUAL-W2 (US COE WES)
Three dimensional (???)