## Slide 1: Advanced Toxicant Module Class Example: Lake Waccamaw, NC

## Slide 2: Lake Waccamaw, NC
34.3191° N, 78.5000° W
Freshwater drainage lake in Columbus County, North Carolina
Surface area 36 km2 (36,000,000 m2)
Average depth 2.3 m
Average flow 2.6 m3/s
Investigate a steady release (1kg/d) into the lake an organic chemical that biodegrades and sorbs strongly to solids

## Slide 3: Lake Waccamaw Conceptual Model
Inflow and outflow
Load
Two chemicals: Chem1 and Chem2
4 solids: sand, silt, clay, POM
DOC
Processes:
Biodegradation, sorption, DOC complexation, settling, resuspension, burial
inflow
outflow
load
biodegradation
sand
silt
clay
POM
DOC
Chem1
Chem2
sorption
DOC
complexation
settling
resuspension
burial

## Slide 4
New wif
Model Type: Advanced Toxicant
Time Range: 1/1/2020 12:00 pm
1/1/2025 12:00 pm
Bed Volume: Static
Model Output Interval:
0.042 d (~hourly)

## Slide 5
State Variables
2 Chemicals
4 Solids
1 DOC

## Slide 6
Segments
3 Segments:
Surface Water
Surface Benthic
Subsurface Benthic
Set “Segment Below”
(this stacks segments)

## Slide 7
Layer | Sand | Silt | Clay | POM | DOC
Lake | 0 | 0.2 | 4 | 6 | 6
Surface Sediments | 10,400 | 21,000 | 127,800 | 27,000 | 0
Subsurface Sediments | 11,600 | 23,000 | 14,100 | 27,245 | 0
Initial Conditions for all state variables

## Slide 8
Physical dimensions of the lake set in “Channel Geometry” in Flow tab
Segment | Volume (m3) | Average Depth (m)
Lake Waccamaw | 8.28x107 | 2.3
Surface sediments | 1.8x106 | .05
Subsurface sediments | 3.6x106 | .1

## Slide 9
Flow in/out of Lake
Surface water tab
Turn on Flow Function
Set up flow path:
  Boundary to 1: Lake
  1:Lake to Boundary
Flow of 2.6 m3/s

## Slide 10
Set up Outputs

## Slide 13
View model output. Make sure everything is set so far. Solids concentration in Lake

## Slide 14
State Variable | Boundary Condition (mg/L)
Sand | 0
Silt | 0.2
Clay | 4
POM | 6
DOC | 6
Add Boundary Conditions

## Slide 15
View model output. Make sure everything is set so far. Solids concentration in Lake

## Slide 16
Process | Particle | Velocity [m/d]
Settling | Silt | 0.2
 | Clay | 0.07
 | POM | 0.21
Resuspension | Silt | 4x10-5
 | Clay | 4x10-5
 | POM | 4x10-5
Add solids processes

## Slide 17
Sand settles fast
Instead of adding to water column
Add directly to the surface sediment layer

## Slide 18
Solids in the Water Column
Solids in the Sediments

## Slide 20
 | Chem1 | Chem2
DOC Complexation | 1000 | 10
Sorption - Sand | 500 | 5
Sorption - Silt | 25000 | 2500
Sorption - Clay | 50000 | 5000
Sorption - POM | 4000 | 40
Add portioning to solids for two chemicals

## Slide 21
Total and Dissolved Concentrations in Lake
Total and Dissolved Concentrations in Sediments

## Slide 22
Process /Parameter | Rate Constant
Biodegradation of Chem 1 | 0.1 /d
Biodegradation of Chem 2 | 0 /d
Chemical reaction product of Chem1 | 2 (Identifies that Chem1 -> Chem2)
Chemical reaction yield of Chem1 to Chem2 | 0.8 (says that 0.8 mg of Chem2 are formed from 1 mg of Chem1)

## Slide 23
Total and Dissolved Concentrations in Lake
Total and Dissolved Concentrations in Sediments