## Slide 1: Watershed Mercury Processes
Anthropogenic Emissions
Wet Deposition
Dry Deposition
Evasion
Natural Emissions
Percolation
Shallow
Ground Water
Settling
Resuspension
Diffusion
Runoff and Erosion
Rivers and Streams
Weathering
Evasion
Litterfall and Throughfall

## Slide 2
http://www.healthbenchmarks.org/Mercury/AquaticeCycle.cfm

## Slide 3: Mercury in the Food Web
Predator Fish: Yellow Perch
Benthos
MeHg
Prey Fish: Yellow Perch
Zooplankton
Phytoplankton
Images from:
www.glerl.noaa.gov/pubs/photogallery/gallery.html, www.dnr.state.wi.us

## Slide 4: Overview of WASP Mercury Module
Volatile
Exchange
of Hg(0)
Watershed and
Atmospheric Loads
of Hg(II) and MeHg
State Variables
Hg(0) Silt
Hg(II) Sand
MeHg
Methylation
Demethylation
Oxidation
Reduction
Burial
Point Source
Loads of Hg(II)
DOC

## Slide 5: Mercury Processes in WASP
<footer>
<date/time>
Partitioning
Transport
  Volatilization of Hg0(aq) to Hg0(air)
Transformation
  Oxidation: Hg0  HgII
  Reduction: HgII  Hg0
  Methylation: HgII  MeHg
  Demethylation: MeHg  HgII
  Photoreduction: MeHg  Hg0

## Slide 6: Mercury Partitioning Processes
<footer>
<date/time>
Partition Coefficients | HgII | MeHg | Hg0
Kfines | 1.0e5 - 1.0e6 | 1.0e5 - 1.0e6 | 0
Ksand | 1.0e2 – 1.0e4 | 1.0e2 – 1.0e4 | 0
log KDOC | 4 – 5 | 5-6 | 0
Parameters: Enter Dissolved Organic Carbon Concentration
Example Ranges:
Oligotrophic Lake: <1 – 3 mg/L
Mesotrophic Lake: <1 – 5 mg/L
Eutrophic Lake: 5 – 30 mg/L
Dystrophic Lake: 3 – 30 mg/L
from Wetzel, 2001.

## Slide 7: Hg0 Volatilization
<footer>
<date/time>
Hg(0)diss to gaseous Hg(0)
  Constants:
    Set volatilization option
      (1 to 5),
    Henry’s Law constant
      (e.g., 7.1e-3 atm/M)
    Atmospheric concentration
      (e.g., 1.6e-9 g/m3)

## Slide 8: Hg0 Oxidation
<footer>
<date/time>
Oxidation: Hg(0) to Hg(II)
  Hg0 Constants:
    Set phase switches (1 for dissolved)
    Yield coefficient (1.0)
  Parameters:
    Rate constants for water column segments
      (e.g., 1e-2 to 1e-3 day-1)

## Slide 9: HgII Transformation Processes
<footer>
<date/time>
Reduction: HgII to Hg(0)
  HgII Constants:
    Set photolysis option (2),
    Quantum yield coefficients (1 for diss, sorb),
    Yield coefficient (1.0),
    Surface rate constant (e.g., 1e-3 to 1e-1)
  Parameters:
  Light attenuation coefficients for water column segments
    (e.g., 0.5-2 m-1)

## Slide 10: HgII Transformation Processes
<footer>
<date/time>
Methylation: HgII to MeHg
  Constants:
    Set phase switches (1 for diss, sorb),
    Temperature correction factors (2.0 per 10 C change),
    Yield coefficient (1.07)
  Parameters:
  Methylation rate constants for water column and benthic segments
    (e.g., 1e-5 to 1e-2 day-1)

## Slide 11: MeHg Transformation Processes
<footer>
<date/time>
Photoreduction: MeHg to Hg(0)
  MeHg Constants:
    Set photolysis option (2),
    Quantum yield coefficients (1 for diss, sorb),
    Yield coefficient (0.93),
    Surface rate constant (e.g., 1e-3 to 1e-1)
  Parameters:
    Enter light attenuation coefficients for water column segments
      (e.g., 0.5-2 m-1)

## Slide 12: MeHg Transformation Processes
<footer>
<date/time>
Bacterial Demethylation: MeHg to HgII
  Constants:
    Set phase switches (1 for diss, sorb),
    Temperature correction factors (10 kcal/mole),
    Yield coefficient (0.93)
  Parameters:
    Enter demethylation rate constants for benthic segments (e.g., 1e-5 to 1e-2 day-1)

## Slide 13: Watershed Mercury Process Models
<footer>
<date/time>
HgII in Soil
Tributaries
reduction,
evasion
Atmospheric Wet and Dry Deposition
reduction,
volatilization
Impervious Surface
volatilization
export
export
Water Surface
runoff
export
runoff and erosion
sediment layer
MeHg Hg(II) Hg0
Silt water column Sand
WCS
Watershed Model
MDS
Tributary Model
Wasp5/6
Water Body Model
Burial
Leaching

## Slide 14: Modeled Fluxes - Ochlockonee Basin
<footer>
<date/time>
Soil
74 μg/kg
Tributaries
12 μg/m2-yr
Atmospheric Deposition
12 (wet), 6 (dry) μg/m2-yr
0.4 μg/m2-yr
Impervious Surface
River
5 – 6 ng/L
water column
sediment layer
10 - 13 μg/kg
< 0.1 μg/m2-yr
1.7 μg/m2-yr
1.7 μg/m2-yr
Water Surface
0.6 μg/m2-yr
0.2 μg/m2-yr
0.2 %
1.3 %
3.4 %
95 %
1.3 μg/m2-yr