## Slide 1
Simulating the Fate and Transport of Chemicals Using WASP8
Yanlai Han
07/20/2017

## Slide 2
Outline of Presentation
Introduction
WASP8 Chemicals Simulation Module
  Chemical Reaction
  Physical Process
WASP8 Case Study: PAHs Transport in Brier Creek

## Slide 3: Introduction
WASP8 covers all important chemicals fate processes
  Chemical Reactions: Biodegradation, Reduction, Oxidation, Photoreaction
  Physical Process: Partition, Volatilization
  Transport Process: Stream Flow, Sediment Transport
  WASP8 can simulate organic and inorganic (metals) contaminants
WASP8 can simulate 10 Chemicals
  WASP7 can only simulate 3 Chemicals
  WASP8 enables users to handle more complicated situations

## Slide 4
Water Column
Sediment
Photolysis
Volatilization (Henry’s Law)
Inflow
outflow
solid
Burial
settling
resuspension
partition
partition
solid

## Slide 5
Outline of Presentation
Introduction
WASP8 Chemicals Simulation Module
  Chemical Reaction
  Physical Process
WASP8 Case Study: PAHs Transport in Brier Creek

## Slide 6
General Reaction Module
=
kreaction: Overall reaction rate constant (day-1)
krate: Rate constant specified by WASP user (day-1)
Xtemp: Temperature correction term
Xseg: Segment type multiplication factor
Xphase: Phase multiplication factor
Xmonod_env: Monod for environmental factors (bacteria, oxidants, reductants)
Xmonod_conc: Monod concentration factor (C/(KM+C) )

## Slide 7
Photolysis Module
=
kphotolysis: Overall photolysis rate constant (day-1)
Krate, λ: Photolysis rate constant for each specific wavelength
(day-1/(W/m2))
Iλ: Average light intensity in WASP segment for each specific wavelength (W/m2)
Ultraviolet and visible light spectrum are divided into 10 specific wavelength

## Slide 8
Wavelength Specification

## Slide 9: Chemical Reactions
Simple one step reaction (First-order):

## Slide 10: Chemical Reactions
Multiple steps reactions

## Slide 11: Chemical Reactions
Multiple steps reactions

## Slide 13: Physical Process – Partitioning
Partition – Evaluation of contaminant distribution between solid and aqueous
Assumption: Partition process instantly reaches to equilibrium
WASP input: Initial contaminant concentration and solid concentration
WASP input: Partition coefficient (L/kg), kd =
WASP output: Dissolved chemical concentration (mg/L), and chemical sorbed on solid (mg/kg)

## Slide 14: Physical Process – Sorption and Desorption
Sorption and desorption
Assumption: Partition is a slow process, and desorption happens
WASP input: Sorption coefficient and desorption coefficient
WASP input: Initial chemical and initial solid concentration
Sorption ( kfor)
Desorption (krev)
Solid

## Slide 16: Physical Process – Volatilization
Volatilization – Henry’s Law
WASP input: Partial vapor pressure of contaminant of interest (atm)
WASP input: Henry’s constant of contaminant (atm·m3/mole)

## Slide 18: Outline of Presentation
Introduction
WASP8 Chemicals Simulation Module
  Chemical Reactions
  Physical Process
WASP8 Case Study: PAHs Transport in Brier Creek

## Slide 19: Case Study - Introduction
Anthracene accidentally releases into a river.
Anthracene releasing load is 5 kg/d, and this releasing lasts for 10 days.
Anthracene undergoes first-order biodegradation, and degradation rate is 0.2 day-1.
Anthracene degrades into naphthalene and carbon dioxide. 90% of anthracene mass transforms into naphthalene, 10% of anthracene mass transforms into carboxylic group.
Evaluate anthracene and its biodegradation product concentrations in river, and conduct ecological assessment.

## Slide 20
Case Study – Chemical Reactions
= -k[A]
= -kY[A], Y is mass yield (0.9 g/g)
Anthracene (A)
Naphthalene (N)

## Slide 21: Case Study: PAHs transport in Brier Creek
Anthracene

## Slide 22: Case Study - PAHs Properties
Contaminant released: Anthracene
Density: 1.25 g/cm3
Henry’s constant: 0.039 x 10-3 atm·m3/mol
Vapor pressure: 0.08 Pa = 0.08 x 9.869 x 10-6 atm
Partition coefficient: 104.37 L/kg

## Slide 23: Case Study – PAHs Properties
Biodegradation product: Naphthalene
Density: 1.025 g/cm3
Henry’s constant: 0.42 x 10-3 atm·m3/mol
Vapor pressure: 8.64 Pa = 8.64 x 9.869 x 10-6 atm
Partition coefficient: 2800 L/kg

## Slide 30
Case Study – Results
Free PAHs concentrations in water column in segment 3

## Slide 31
Concentrations of PAHs sorbed on solids in water column in segment 3
Case Study – Results

## Slide 32
Concentrations of PAHs sorbed on solids in surface sediment in segment 3
Case Study – Results

## Slide 33
Concentrations of PAHs sorbed on solids in deep sediment in segment 3
Case Study – Results

## Slide 34
Thanks so much!!
Email: han.yanlai@epa.gov
Tel: +1 (706) 355 - 8151