## Slide 1: Dispersion and Exchanges

## Slide 2: Diffusion and Dispersion
Diffusion: process where a constituent moves from a higher concentration to a lower concentration
Dispersion: mixing caused by physical processes
time

## Slide 3: Diffusion and Dispersion
Molecular Diffusion: Random motion of particles
Eddy Diffusion: Turbulent mixing of particles
Mechanical Dispersion: mixing caused by variations in velocities

## Slide 4: Mathematical Representations
Diffusion:
  Fick’s First Law of Diffusion
    Flux =
Dispersion:
  Analogous to Fick’s First Law
C1
C2
L12
  Exchange =

## Slide 5: Range of Values for Diffusion and Dispersion
Process | Direction | Typical Range [m2/s]
Molecular Diffusion | Vertical | 10-8 to 10-9
 | Lateral | 10-8 to 10-9
 | Longitudinal | 10-8 to 10-9
Turbulent Diffusion | Vertical | 10-6 to 10-2
 | Lateral | 10-2 to 102
 | Longitudinal | 10-2 to 102
Dispersion | Vertical | 10-3 to 10-1
 | Lateral | 10-2 to 100
 | Longitudinal | 10-1 to 104

## Slide 6: Diffusion Coefficients
Condition | Dispersion Coefficient [m2/s]
Molecular Diffusion | 10-9
Compacted Sediment | 10-11 to 10-9
Bioturbated Sediment | 10-9 to 10-8
Lakes – Vertically | 10-6 to 10-4
Large Rivers – Lateral | 10-4 to 10-3
Large Rivers – Longitudinal | 100 to 102
Estuaries – Longitudinal | 102 to 103
From Schnoor, Environmental Modeling: Fate and Transport of Pollutants in Water, Air, and Soil, 1996.

## Slide 7: Determining Dispersion
Streams & Rivers
  Generally Neglect Dispersion
  Determine by Calibration or Dye Study
Estuaries
  Calibration to Salinity data using observed downstream boundary concentration as the forcing function
Lakes
  Calibration to Temperature Data
  Calibration to Chloride Data

## Slide 8: Dispersion in Rivers
U = Mean Velocity [m/sec]
B = Width, [m]
d = Depth (hydraulic radius), [m]
u* = Shear Velocity, [m/sec]
=
S = Channel Slope [m/m]
Longitudinal Dispersion Coefficient in Rivers, Ex [m2/sec]
Fischer, et al., 1979.

## Slide 9: Dispersion in Rivers
Lateral Dispersion Coefficient in Rivers, Ey [m2/sec]
d = Depth (hydraulic radius), [m]
u* = Shear Velocity, [m/sec]
f = 0.23 (long, wide lab flume) Elder, 1959
= 0.17 (straight lab flume)
Sayre (1973), Sayre and Chang (1968)
= 0.22 – 0.65, most 0.3
Yotsukura and Cobb(1972), Yotsukura and Sayre (1976)
Elder, 1959.
Ey = fdu*

## Slide 10: Dispersion in Rivers
Vertical Dispersion Coefficient in Rivers, Ez [m2/sec]
K = von Karman coefficient, ~ 0.4
d = Depth (hydraulic radius), [m]
u* = Shear Velocity, [m/sec]
Jobson and Sayre, 1970.

## Slide 11: Dispersion in Lakes
Vertical Dispersion Coefficient in Lakes, Ez [m2/sec]
d = Depth, [m]
Jobson and Sayre, 1970.

## Slide 12: Dispersion Measurements
Chattahoochee River, GA | Ex = 32.5 m2/s
Susquehanna River, PA | Ex = 92.9 m2/s
Missouri River, NB-IA | Ex = 465 – 1487 m2/s
Antietam Creek, MD | Ex = 9.3 - 25.6 m2/s
Powell River, TN | Ex = 9.5 m2/s
Lake Onondaga, NY | Ez = 0.005 – 0.09 cm2/s (across thermocline)
Lake Zurich, Switzerland | Ez = 0.02 – 0.71 cm2/s (across thermocline)
Lake Erie | Ez = 0.21 cm2/s (across thermocline)
Lake Ontario | Ez = 0.063 – 0.0125 cm2/s (across thermocline)
Lake Erie | Ez = 15 cm2/s (whole lake)
Lake Huron | Ez = 1.16 cm2/s (whole lake)
Cayuga Lake | Ez = 2.31 cm2/s (whole lake)
Lake Ontario | Ez = 3.47 cm2/s (whole lake)