## Slide 1: Simulating the Fate and Transport of Nanomaterials Using WASP8

## Slide 2: Nanomaterials
Materials with a size of 1 to 100 nm
Have special optical, electronic, and/or mechanical properties
Their properties have resulted in increased production and therefore increased release to the environment
They cannot be simulated as solids or as solutes because of their properties
They are now a specific state variable in WASP8

## Slide 3: Hetero-aggregation
3
khetagg = ahetagg x kcoll x Cspm
Brownian Motion
Fluid Motion
Differential Settling

## Slide 4: Reactions
Aside from hetero-aggregation, nanomaterials may undergo reactions
  Photochemical Reactions
  General Reaction
Nanomaterials can break down into other nanomaterials or chemicals
  Nano1  Nano2
  Nano1  Chem1

## Slide 5: Photochemical Reactions
kphotochemical,l = krate,l*Il [per day]
krate,l : photoreaction reaction rate constant,
for given wavelength [per day per W/m2]
Il : Average light in WASP segment for given wavelength [W/m2]
Il is calculated using surface light attenuated using Beer’s law

## Slide 6: General Reaction
kreaction = krate*Xtemp*Xseg*Xphase*Xmonod,env*Xmonod,conc [per day]
krate : base rate constant [per day]
Xtemp : temperature correction term
Xseg : segment multiplication factor
Xphase : phase multiplication factor
Xmonod,env : Monod for environmental factors (bacteria, oxidants, reductants)
Xmonod,conc : Monod concentration factor

## Slide 7: Implementing Nanomaterials
System Type: NANO
Systems (Model State Variable Activation)
  Choose as many NANO state variables are phases of nanomaterial that will be present:
    NANO1 = Free Nano
    NANO2 = Nano attached to silt
    Define Density for Free Nano

## Slide 8: Implementing Nanomaterials
Parameter Data:
  For hetero-aggregation, on Parameter Data define
    Collision efficiency for the Free Nano
    Settling velocity for the Free Nano

## Slide 9: Implementing Nanomaterials
On Constants Page
  On Nano Chemical Partitioning, Define particle diameter for Free Nano

## Slide 10: Implementing Nanomaterials
On Constants Page
  On Nano Chemical Kinetic Sorption, link Nano chemical sorbed to solid type:
    Since we want Nano-Silt sorbed to our solids type (1), we enter a “2”

## Slide 11: Implementing Nanomaterials
Adding to simple pond system:
0.1 kg/day load of nanomaterials into WC
  Density = 2.1 g/cm3
  Diameter = 100 nm
Nano -> Silt heteroaggregation
  α = 1.04E-06
Nano settling, 1.3E-03 m/day
WC
Surface Sediment
Subsurface Sediment
Qin
Qout
Silt
Nano

## Slide 12: Simulated Water Column - Nano

## Slide 13: Simulated Surface Sediment - Nano

## Slide 14: Simulated Subsurface Sediment - Nano