## Slide 1
Chemical Reactions
Yanlai Han
06-14-2017

## Slide 2: Introduction
WASP8 covers all the important chemical’s fate processes
  Chemical Reactions: Biodegradation, Reduction, Oxidation, Photoreaction
  Physical Process: Partition, Sorption, Volatilization
  Transport Process: Stream Flow, Sediment Transport
  WASP8 can simulate organic and inorganic (metals) contaminants
WASP8 can simulate 10 Chemicals
  WASP7 can only simulate 3 Chemicals
  WASP8 enables users to handle more complicated situations

## Slide 3
Water Column
Sediment
Chemical reaction
Volatilization
Inflow
Outflow
Solid
Burial
Settling
Resuspension
Partition
Partition
Solid
C1
C2
C1
C2

## Slide 4
General Reaction Module
kreaction: Overall reaction rate constant (d-1) that WASP8 internally calculates
Overall reaction rate in WASP is programmed as
Default chemical reaction is programmed as the first-order reaction
=

## Slide 5
General Reaction Module
=
kreaction: Overall reaction rate constant (d-1) that WASP8 internally calculates
krate: Reaction rate constant specified by WASP users (d-1) at 20°C
Xtemp: Temperature correction term
Xseg: Segment type multiplication factor
Xphase: Phase multiplication factor
Xmonod_conc: Monod kinetic equation
Xmonod_env: Monod environmental factors (bacteria, oxidants, reductants)
Users need to input them into WASP8
Default values are ‘1’ if users don’t turn them on

## Slide 6: Class Examples – PAHs (P450) Biodegradation
Phenanthrene undergoes biodegradation in a surface water system
Key to model Chemical (Nano) reaction is to correctly specify reactant and products number
Biodegradation pathway is

## Slide 7: 1. Only Consider Reaction Rate Constant
Reaction pathway is
Stoichiometric relationships are

## Slide 8: PAHs (P450) Biodegradation
Set reaction model from C1 to C2 in WASP
Reaction Parameters:
1. Biodegradation reaction rate k1: 0.1 d-1
2. Reaction yield (gram/gram)
3. Other parameters: Molecular weight, henry’s law constant, density, etc

## Slide 9: Reaction Yield (g/g) Calculation
k1 is reaction rate, d-1.
C1 and C2 are in the unit of mole/L.
k1 is reaction rate, d-1.
C1 and C2 are in the unit of mg/L.
Reaction yield
input in WASP.
Its unit is g/g
In WASP, unit of chemicals
is mg/L
Unit Conversion
Reaction:

## Slide 10: Reaction Yield Calculation Example
Reaction yield input into WASP8 is calculated as
= 0.6() = 0.70
Reaction yield input into WASP8 is calculated as
= 0.4() = 0.48
Balanced relation:

## Slide 11: PAHs (P450) Biodegradation
Set reaction model from C1 to C2 in WASP
Parameters:
1. Biodegradation reaction rate k1 is 0.1 d-1
2. Reaction yield is 0.70 (g/g).
3. Other parameters: Molecular weight, henry’s law constant, density, etc
All parameters for defining a reaction is ready!

## Slide 12: Procedures to Build a Biodegradation Model
Procedures to set up the reaction in WASP8
1. Create surface water WASP model. In this case, a simple river model has been created already, and no flow condition will be simulated firstly.
2. Create chemical state variables
3. Input initial conditions (concentrations)
4. Specify reactants and products number, input reaction rate constant, and reaction yield
5. Define how contaminants enter into the surface water system (Using Loading Function or Initial Conditions)
6. Select output parameters
7. Run the WASP model

## Slide 13: River Model Illustration
River 1
River 2
Lake
Pollution source

## Slide 14: Turn off water flow

## Slide 15: Create chemical state variables

## Slide 16: Input initial conditions

## Slide 17: Input reactant and products number, reaction constant, and reaction yield

## Slide 18: Select output parameters

## Slide 19: Results
C1
C2

## Slide 20: PAHs (P450) Biodegradation
Set reaction model from C1 to C3 then to C4 in WASP
Reaction pathways

## Slide 21: PAHs (P450) Biodegradation
Set reaction model from C1 to C3 then to C4 in WASP
Parameters:
1. Biodegradation reaction rate from C1 to C3: 0.1 d-1
2. Biodegradation reaction rate from C3 to C4: 0.15 d-1.
3. Reaction yield C1 to C3 is 0.48 (g/g), and C3 to C4 is 1.02 (g/g), based on stoichiometric relations.

## Slide 22: Procedures to Build Biodegradation Model
Procedures to set up the reaction in WASP8
1. Create surface water WASP model
2. Create chemical state variables
3. Input initial conditions (concentrations)
4. Specify reactants and products number, input reaction rate constant, and reaction yield
5. Define how contaminants enter into the surface water system (Using Loading Function or Initial Conditions)
6. Select output parameters
7. Run the WASP model

## Slide 23: Add two more chemical state variables

## Slide 24: Input initial conditions

## Slide 25: Input reactant and products number, reaction constant, and reaction yield

## Slide 26: Select output parameters

## Slide 27: Result
C1
C2
C3
C4

## Slide 28
2. Temperature Corrector
=
kreaction: Overall reaction rate constant (d-1) that WASP8 internally calculates
krate: Rate constant specified by WASP user (d-1) at 20°C
Xtemp: Temperature correction term
Time function can be used to simulate temperature effects on reaction rate over certain period.

## Slide 29
Temperature Corrector Options
Temperature corrector options
Option 1: Theta temperature correction factor (dimensionless)
Xtemp = θ(T-20)
where is θ temperature-activity coefficient, and T is temperature (°C).
Option 2: Q10 temperature correction factor (dimensionless)
Xtemp = θ[(T-20)/10]
where T is temperature (°C).

## Slide 30
Temperature Corrector Options
Temperature corrector options
Option 3: Activation energy temperature correction factor
=
= ( )
Xtemp = )
where k1 is reaction rate at certain temperature (d-1) ,
k2 is reaction rate when temperature is at 20°C (293.15K)
Ea is activation energy (kcal/mol), R is gas constant (J/(mol-K)),
T is temperature (K).

## Slide 31
Temperature Corrector Example Description
Previous model doesn’t consider the temperature effects on the biodegradation rate.
So this model includes the temperature effect.
Time Function is used to simulate temperature effect on fates of chemicals over a six-month period. Users also need to obtain temperature data.

## Slide 32
Example Procedures
Procedures to include temperature corrector in WASP8
1. Build reaction model first (previous example)
2. Choose temperature corrector options (option 1 for this example)
3. Input parameters of temperature corrector equation
4. Turn on Temperature Function in Environmental Group
5. Input temperature data into Time Function
6. Select output parameters
7. Run the model

## Slide 33
Choose temperature corrector options

## Slide 34
Input parameters for temperature corrector options

## Slide 35
Turn on temperature function in Environmental Group

## Slide 36
Input temp data into Time Function

## Slide 37
Results
C1 influenced by temperature
C1 without temperature influence

## Slide 38
Results
C2 influenced by temperature
C1 without temperature influence

## Slide 39
3. Consider the Water Flow
Consider the water flow for this example
Use the Loading function to specify how contaminant enters into this surface water system
Procedures
Input the water flow rate on the same WASP8 wif file
Input the loading of contaminant
Run WASP8 model

## Slide 40
Turn on water flow

## Slide 41: Input the loading of contaminant into the surface water system
Unit is kg

## Slide 42: Set initial conditions as ‘0’

## Slide 43: Set boundary conditions as ‘0’

## Slide 44
Results in First Segment

## Slide 45
Results in Third Segment (Lake)

## Slide 46
4. Segment Multiplication Factor
Surface waters system (e.g., river) usually is divided into different segments
Segment multiplication factor is an easy way to set parameters in different segments (e.g., reaction rate, temperature, pH, etc)
Examples: Set different biodegradation rates in different segments in the surface water system.
=

## Slide 47
Segment Multiplication Factor Example
Biodegradation reaction rate in the lake is 3 times as much as the ones in two river segments

## Slide 48
5. Phase Multiplication Factor
Chemical reaction rate might different if chemical is present in different forms. e.g.: (1) a chemical sorbed on a suspended solid (e.g., catalytic effect)
(2) a nanoparticle surface is coated with DOC (e.g., reduced dissolution rate)
An example will be given in next class (sorption and partition).
=

## Slide 49
6. Monod Kinetic Equation in WASP
1. For biodegradation, WASP has two options: (1) First-order reaction, and (2) Monod kinetic reaction.
2. Monod general kinetic equation is Eq. (1)
where k is the max substrate utilization rate (d-1), Ks is monod half-saturation constant
(mg/L), and X is biomass (mg/L).
3. Monod general kinetic equation (Eq.(1)) can be rearranged as
Eq.(2)
where k’ is in the unit of mg/L-d.
4. Monod kinetic is constructed followed Eq. (2). Users need to input and Ks in WASP.

## Slide 50
Monod Kinetic Example Description
For Monod kinetic simulation, you need to input k’ and Ks values from Eq.(2) into WASP.
Here still uses the first reaction pathway of P450 biodegradation as an example.
Key parameters: k = 3 d-1, X = 15 mg/L, Ks= 60 mg/L
So k’ = kX = 45 mg/L-d
k’ and Ks need to be input into WASP for Monod kinetic simulation.

## Slide 51
Monod Kinetic Example

## Slide 52
Monod Kinetic Example 2

## Slide 53
Monod Kinetic Simulation Result
C1
C2

## Slide 54
7. Monod Environmental Factor
Biokinetic activity can be affected by dissolved oxygen, nitrate or other factors in environment
Monod environmental factor accounts for the influences from these factors
WASP has three options for Monod Environmental Factor
Option 1: Xmonod_env = 1 (Default)
Option 2: Xmonod_env = E
Option 3: Xmonod_env =
where E is chemical concentration in environment (e.g., DO, NO3), Kenv is environmental half-saturation coefficient (mg/L)

## Slide 55
Monod Environmental Factor Example
Example still uses previous previous Monod kinetic example
Suppose biodegradation is inhibited by DO in the surface water system
This example use option 3
Biodegradation of C1 is expressed as

## Slide 56
1. Continue to set parameters of Monod environmental factor
Parameters: Choose option 3, and Kenv = 45 mg/L.

## Slide 57
3. Input Daily average DO concentration for Monod environmental factor in Time Function

## Slide 58
4. Activate the Time Function

## Slide 59
Result
C1 biodegradation influenced by DO
C1 biodegradation