## Slide 1: Biodegradation
Summary of Process Equations and Model Input Data

## Slide 2: Bacterial Degradation
Reaction
Kinetic
Equation
Data
  kBW or kBS, day-1
  kB, (cells/mL)-1day-1
  bacterial population density, bac, (cells/mL)

## Slide 3: Biodegradation
Biodegradation: Microbially mediated breakdown of organics
Biotransformation: Microbial transformation
Intermediate: Compound formed in biodegradation pathway
Mineralization: Microbial reactions lead to complete breakdown of substrate, i.e., result in CO2 and H2O.
e.g., C6 H6 +7.5 O2  6 CO2 + 3 H2O
Dead-End Product: Intermediates in Biodegradation Pathway
that are not further biodegraded
A general expression of biodegradation rate is:
C = Substrate Concentration [g/L]
kb = first-order biodegradation rate [day-1]

## Slide 4
Biodegradation
of
Benzene
From
http://www.ence.umd.edu/
~eseagren/bioAHC97.htm

## Slide 5: Example Biodegradation Rates
Chemical Class | Example | first-order kb [per day]
Pesticides | DDT | 0.03
 | Atrazine | 0.05 – 0.06
PCBs | Aroclor 1248 | 0.0 – 0.007
Halogenated HCs | Chloroform | 0.09 – 0.10
Halogenated Ethers | 2-Chloroethyl vinyl ether | 0.0 – 0.20
Monocyclic Aromatics | Pentachlorophenol | 0.00 – 33.6
 | Benzene | 0.006 – 0.01
 | Toluene | 0.01 – 0.019
Polycyclic Aromatics | Anthracene | 0.007 – 15.0
 | Benzo[a]pyrene | 0.0 – 0.075
Phthalate Esters | Bis(2-ethylhexyl)phthalate | 0.00 – 0.14
Misc. | Benzidine | <0.001
 | Dimethyl nitrosamine | <0.001

## Slide 6: Biodegradation Kinetics
Monod Kinetics:
General Kinetics:
Second Order Kinetics:
Pseudo First Order Kinetics:
Biomass Growth:
C: Substrate [mg/L]
X: Biomass [cell/L]
Ks: Half-Saturation Coefficient [mg/L]
Y: Stoichiometric Yield
Coefficient [cell/mg]
Utilization Rate Constants
q: general [mg/cell/hr]
q2: second order [L/cell/hr]
q1: pseudo first order [per hr]
q1: zero order [per hr]
qmax: maximum [mg/cell/hr]
Zero Order Kinetics:

## Slide 7: Monod Kinetics
Example: Aqueous Biodegradation of Naphthalene (Knightes and Peters, 2004)
qmax = 0.6 hr-1, KS = 0.57 mg/L, Y = 0.4, C0 = 5 mg/L, X0 = 0.1 mg/L
Zero Order Transition First Order
Zero Order
First Order
Transition
Zero Order
First Order
Transition

## Slide 8: Biodegradation Metabolism
Growth Metabolism
  Catabolism
    Breakdown of substrates
    Release of energy
  Anabolism
    Synthesis of products into building blocks
    Investment of Energy
Cometabolism

## Slide 9: Biodegradation Metabolism
Growth Metabolism
  Organic compound serves as a food source
  Microbial adaptation time -- 2-50 days
    faster for chronic exposure
    faster for high microbial population
    slower in presence of easily degradable carbon source
  Fast first-order rates after adaptation

## Slide 10: Types of Biodegradation
Cometabolism
  Compound of interest is degraded in the presence of a different compound
  Cometabolism does not result in bacterial growth
  No adaptation time (often)
  Slow degradation rates
    “B” unaffected by “C” or
    measure “B” on environment using same method (e.g., plate counts) as in lab
  Example: Methane and Trichloroethylene (TCE)
    TCE is fortuitously oxidized by same enzyme that degrades Methane. Bacteria gain nothing through this incidental reaction. Rather the TCE biodegradation products are toxic to the methane degraders.

## Slide 11: WASP Biodegradation Routine
kB = Second Order Biodegradation Rate Constant [ml/cell/hr]
B = Active Bacterial Population Concentration [cells/ml]
KB = Pseudo first-order rate constant [per hour]
Specify Bacteria Concentration [ml/cell/hr]
Water Column
Benthic
For Pseudo-First Order,
Bacteria Concentration is held Constant
lumped into kB
For time-varying first-order rate constants,
Set kB = 1, and use time-varying Bacteria concentration

## Slide 12: Environmental Influence
Temperature
  Rate of reactions and bacterial growth are functions of temperature
  Generally, growth rate doubles for each 10o C rise
  Q = 1.5 – 2.0
Nutrient Limitation
[PO4] = Conc of Phosphorous
Anoxia
  Rates decrease for Dissolved Oxygen < 1
  Anaerobic rates small

## Slide 13: Representative Population Sizes
Water Body Type | Bacterial Number
Oligotrophic Lake | 50 – 300
Mesotrophic Lake | 450 – 1400
Eutrophic Lake | 2,500 – 12,000
Eutrophic Reservoir | 1,000 – 58,000
Dystrophic Lake | 400 – 2,300
Lake Surficial Sediments | 8x109 - 5x1010 cells/g dry wt.
40 surface waters | 500 – 1x106
Stream Sediments | 107 - 108 cells/g
Rur River (winter) | 3x104

## Slide 14: Biodegradation Options and Inputs
In “Parameters Data”
  Turn On
    Temperature Function Pointer
    Segment Water Temperature
    Density of Active Bacteria
In “Constants Data”
  Constants
    kB: biodegradation rate constant
      Benthic [per day]
      Water [per day]
      Aqueous ions [mL/cell-day]
      DOC-complexed
    Q10, Temp correction factor
    Mass Yield Coefficient
In “Time Functions”
  Water Temperature
  Bacteria
    Water Column
    Benthic
In “Segments Data”
  Parameters
    Temperature Function Pointer
    Temperature Function Multiplier
    Density of Active Bacteria

## Slide 15
Chemical 1
Chemical 2
Chemical 3
kb, Biodegradation
Rate Constant
Q10,
Temperature
Correction Factor
Y, Mass Yield
Coefficient

## Slide 16
Temperature Function
Pointer
Density of
Active Bacteria
Segment
Water
Temperature
Turn on Parameters
Turn on
Biodegradation
Parameters

## Slide 17
Temperature
Function
Pointer
Segment
Water
Temperature
Density of
Active Bacteria
Parameter Tab
in “Segments”

## Slide 18
Adding
Time Functions
Turn on Time Functions
Water Temp
Functions
(Assoc.
w/pointers
1,2,3&4)
Bacteria
Concentrations
Water and
Sediment
Insert line,
Define Time Functions