## Slide 1: The WASP8 Advanced Eutrophication Module
Theory and Implementation in
Prepared by
Robert B. Ambrose, Jr.
August, 2016

## Slide 2: Good Reference Materials
Rates, Constants, and Kinetics
  http://www.epa.gov/ORD/WebPubs/surfaceH2O/surface.html
Steve Chapra
  Surface Water Quality Modeling
James Martin
  Hydrodynamics and Transport for Water Quality Modeling
Thomann and Mueller
  Principles of Surface Water: Quality Modeling and Control

## Slide 3: Eutrophication – Water Quality Issues
General Water Quality
  salinity, pH, solids, temperature
Nutrient Enrichment
Dissolved Oxygen Depletion
Algal Production
  Phytoplankton (lakes, reservoirs, estuaries)
  Periphyton (streams)
  Macro Algae

## Slide 4: Variables and Processes
Periphyton/Macroalgae Biomass
D : C : N : P : Chl
IP
IN
Phytoplankton Biomass
Group 3
D : C : N : P : Si: Chl
DO
Group 2
D : C : N : P : Si: Chl
Group 1
D : C : N : P : Si : Chl
TIC
H2CO3 – HCO3- – CO32-
Total
Alkalinity
Particulate Detrital OM
Si
P
N
C
D
Dissolved OM
Si
P
N
CBOD1
CBOD2
CBOD3
Inorganic Nutrients
NO3
PO4
SiO2
NH4
pH
atmosphere
uptake
excretion
Inorganic Solids
S3
S1
S2
oxidation
oxidation
nitrification
photosynthesis and respiration
death
dissolution
mineralization
sorption
reaeration

## Slide 5: WASP8 Eutrophication Module
Eutrophication Process
  5 phytoplankton classes
  3 Periphyton/Macroalgae (benthic algae)
  Nutrient cycling – N, P, Si
  3 CBOD and dissolved oxygen
  pH and alkalinity
  Water Temperature

## Slide 6: Eutrophication State Variables
Ammonia (NH3 / NH4+)
Nitrate (NO2- + NO3-)
Phosphate
(H2PO4 / HPO4- / PO42-)
Silicate (SiO4)
DO
Salinity
Alkalinity
TIC
(pH)
Solids (5 classes)
Phytoplankton (5 classes)
  Biomass D:C:N:P:Si:Chl
Periphyton/Macroalgae
  Biomass D:C:Chl
  Nitrogen
  Phosphorus
Particulate Detritus
  POM
  POC
  PON
  POP
  POSi
Dissolved Organic Matter
  CBOD (3 classes)
  DON
  DOP
  DOSi
Notes: Standard eutrophication module lumps particulate and dissolved organic matter (CBOD and nutrients), with specified dissolved fractions.

## Slide 7: Eutrophication Processes Covered in Separate Lectures
Nutrient Cycling
  Nitrogen, Phosphorus, Silicon
Dissolved Oxygen Balance
  CBOD/Organic Matter
Solar Radiation
Phytoplankton Kinetics
Periphyton/Macroalgae Kinetics
Sediment Diagenesis (separate module)

## Slide 8: Levels of Complexity in Implementing WASP8 Eutrophication Model

## Slide 9: Advanced Eutrophication Module External Loadings
Paired inflows and boundary concentrations are preferred over the use of loadings
If loadings are specified for an inflow, the associated boundary conc. should be left at 0
Calculation of loadings for Qin in [m3/day]:
  For variables in their concentration units:
  Std. Variables: Lin = Qin * Cin/1000 [kg/day]
  Phytoplankton: Lin = Qin * Chl-ain/106 [kg Chl-a/day]
  Periphyton: Lin = none

## Slide 10: Advanced Eutrophication Module Environmental Input Data
Atmospheric conditions
  Air temperature [C]
  Wind speed [m/sec]
  Solar radiation [Ly/day]
  Daylight [fraction]
Water body conditions
  Water temperature [C]
  Current velocity [m/sec]
  Salinity [PSU] (can be input or simulated)
  Ice cover [fraction]

## Slide 11: Advanced Eutrophication Module Time Functions and Parameters
Water temperature [°C]
Wind speed [m/sec]
Ice cover [fraction]
Solar radiation [Ly/day]
Canopy shading [fraction unshaded]
Air temperature [°C]
Daylight [fraction]
Cloud cover [fraction]
Time functions Parameter pointer Parameter multiplier
Time function (1 only) Parameter multiplier
Time function only
Time functions Parameter pointer

## Slide 12: Advanced Eutrophication Module Constants Groups
Globals
Inorganic Nutrient Kinetics
Inorganic Nutrient Partitioning
Organic Nutrients
CBOD
Dissolved Oxygen
Light
Solids
Benthic Algae
Phytoplankton 1, 2, and 3
Note: constants detailed in process lectures:
General Water Quality
Nutrient Cycling
Dissolved Oxygen
Phytoplankton
Benthic/Macro Algae

## Slide 13: Advanced Eutrophication Module Output Display Variables
Environmental properties
Transport information
Sediment transport
Nutrients
Dissolved Oxygen – CBOD
Phytoplankton
Benthic algae
Note: output display variables detailed in process lectures:
Sediment Transport
Nutrient Cycling
Dissolved Oxygen
Phytoplankton
Benthic Algae
General Groupings

## Slide 14: Advanced Eutrophication Module General Output Display Variables
Environmental Properties
Transport Information
Temperature
Salinity; TDS
Water density
Total Solids
Cobbles
Solids 1, 2, and 3
Daily light
Light extinction coefficient
Light at segment top, bottom
pH; Alkalinity, TIC
Maximum timestep
Actual timestep
Volume
Depth
Top width
Residence time
Flow in; Flow out
Dispersive flow
Water velocity
Bottom shear stress