## Slide 1: Model Calibration/Verification – How Good is Good Enough
Tim A. Wool
US EPA – Region 4
Atlanta Federal Center
61 Forsyth Street, SW
Atlanta, Georgia 30303
wool.tim@epa.gov

## Slide 2: The Premise
Models will always be constrained by computation limitations, assumptions and knowledge gaps. They can best be viewed as tools to help inform decisions rather than as machines to generate truth or make decisions. Scientific advances will never make it possible to build a perfect model that accounts for every aspect of reality or to prove that a given model is correct in all aspects for a particular regulatory application (NRC 2007).

## Slide 3: What is Model Calibration?
What is Calibration
  Process of Modifying Model Assumptions to Best Represent the System
    Most Commonly Kinetic Constants
    Model Boundary Assumptions
    Data Gaps
  Iterative Process
    Constrained by Knowledge of the System
      Available Monitoring Data
      Point Source Loadings
        DMR Data
        Data Gap Filling

## Slide 4: What is Model Calibration?
It is not Curve Fitting
  Model Assumptions have to be defended
  Kinetic Constants must be within range
  Model should be constrained by observations
  All stations should be compared

## Slide 5: What is Model Verification?
Historically
  Calibrated Model Applied to a “Different Condition”
Current
  Model Framework has application history
  QA/QC Plan

## Slide 6: Model Performance
The models performance needs to be proven
  Modeling Report
  Technical Memorandum
  Presentations
Model Skills Assessment
  How does it compare with measured data
  Is the model adequately constrained

## Slide 7: Model Performance
Two Methods for Assessing Models
  Quantitatively
    Statistical Skills Test
  Qualitatively
    Time Series Plots
    Animations
    Frequency/Probability

## Slide 8: Quantitative Analysis
  Statistical Measures
  Absolute RE = |(Observed – Predicted)|/Observed
  Root Mean Square Error
  Normalized RMSE
  Regression Analysis: correlation coefficients and standard error of the estimate
  Indexes of Agreement (Nash-Sutcliffe, etc.)

## Slide 9: Statistical Measures
Statistics can not be the only measure
  They aid with discovering bias
  Allows analysis of central tendencies
  They are and should be expected

## Slide 12: Final Thought on Model Assessment
To date most skill assessment is performed using qualitative metrics, but do not inform managers of confidence or uncertainty in projections
Currently, there is no one way to perform quantitative model skill assessment
Recommend a combination of statistical measures appropriate for the questions being asked of the model
Include graphical presentations of quantitative skill
Conduct sensitivity analysis on key model parameters
If possible, include multi-year data sets in the model calibration and model confirmation
Include qualitative skill
Peer Review (if possible)

## Slide 13
Perhaps, to some degree, skill, like beauty, is in the eye of …

## Slide 14: Trade Offs
It will never be perfect…

## Slide 15: The Trade Off
Chapra, 1997

## Slide 16: The Constraints
Time
  How much time do you have to make the decision
  Need immediate answer
Budget
  How much do you have to spend
Data
  How much information do you have to parameterize and constrain a model
Skill
  Do you have the expertise to use the models

## Slide 17: The Process
Stakeholder Involvement
  From both sides of the fence
  Build consensus among the group
  Share and discuss model assumptions
Revise or Collect New Data
  To fill gaps
  To support key modeling assumptions
Adapt Model Expectations
  As knowledge is gained
Perform Sensitivity/Uncertainty Analysis
  Key Assumptions
  Most Sensitive Parameters if they are uncertain

## Slide 18: The Decision
Public Comment
  Most Regulatory Processes solicit public comment before the decision is final
Peer Review
  Use outside experts to review the modeling work and the regulatory decision that is made.
Court Challenge
  It Could Happen… ….
  It Happens . . . . .

## Slide 19: Some Examples
Hydrology, Quick and Dirty, Highly Complex, Very Expensive

## Slide 20: Hydrology Calibration
Calibration Period
  January 1, 2001 through December 31, 2010
USGS Calibration Stations
  3 Main Stem
  4 Tributaries
Quantitative Calibration
  Miscellaneous Plots
  Summarized by Statistics
Qualitative Calibration
  Analyzed Statistics
  Qualitative Calibration

## Slide 25: Some Examples
TVA Fly Ash Slide in Kingston, TN
  Catastrophic Event December 22, 2008
  5.4 million cubic yards of Fly Ash
  Regulatory Agencies (State and Federal) are concerned about Selenium release from the fly ash
  Applied Mass Balance Model to predict selenium release from fly ash

## Slide 28: Savannah Harbor Dissolved Oxygen TMDL
Very Complex System
Many Dischargers
Very Interested Stakeholder Group (2 – States, Federal (EPA, Corps, Fish & Wildlife, Environmental Interest Groups)
Has a Modeling Technical Advisory Group

## Slide 29: TAG Developed Model Performance Standards
* 50% represent Absolute Mean Error for temperature
** 5% and 95% represent the max. ebb and flood conditions for current and flow

## Slide 31: Outcome
Interim Decisions
Drawn out process
Stakeholder Consensus is Slow
Constant Model Refinement
Very Expensive
Very Big Decision

## Slide 32: Neuse River Nitrogen TMDL
Complex System
Good Dataset
Technical Advisory Group
Collaborative Effort
High Magnitude Decision

## Slide 33: Knowledge

## Slide 34: Performance

## Slide 35: Comparative Statistics

## Slide 36: Decision
Decision is based upon best available
  Information
  Agreement of Stakeholder Groups
  Outside Peer Review
  Modeling Results because the regulatory process needs a number
    TMDL
    Permits
    Restoration Goal

## Slide 37: Conclusion
Calibration/Model Performance is an iterative process
  Model Refinement/Assumptions
  Feedback from Stakeholders
  Peer Review
  Always Constrained by knowledge

## Slide 38: Calibration Steps
Transport
Time of Travel
Transport Skills Test
Loading
Conservative Simulation
Dissolved Oxygen
BOD (multiple types)
Reaeration
Loadings Correct
Algal
Sediment Oxygen Demand
Numerical Dispersion
Mass Balance Check
Growth Rates
Death Rates
Settling Rates
Nutrients
Nitrogen/Phosphorus
Nitrification Rates
Mineralization Rates
Nutrient Re-Cycling
Light
Sediment Interaction
Sorption/Settling
Sediment Nutrient Fluxes

## Slide 39: Questions/Discussion