## Slide 1: Introduction to Hydrodynamics

## Slide 2: Outline of Presentation
Review of basic fluid mechanics
Hydrodynamics
Basic principles of hydrodynamic modeling
Types of hydrodynamic models
Generic Modeling principles
Description of EFDC

## Slide 3: Review of Basic Fluid Mechanics
Fluid Statics
  The pressure, p, on a plane surface inclined at an angle α to the vertical at a distance y (along the inclined plane) from the water surface is given by the hydrostatic equation:
    p = ρgy cos(α)
  where ρ = water mass density, and g = gravitational acceleration.
  The vertical pressure distribution deviates from that given by the hydrostatic equation when the vertical component of the acceleration of the fluid is not negligible.

## Slide 4: Review of Basic Fluid Mechanics
Fluid Dynamics
  Governed by the principles of conservation of mass and conservation of linear momentum.
Conservation of Mass
Continuity Equation: based on the conservation of mass as it applies to the flow of fluids. It states that the mass rate of flow out of a control volume minus the rate of flow into the control volume is equal to the rate at which the fluid mass is being evacuated from the control volume. The integral form of this equation is:

## Slide 5: Review of Basic Fluid Mechanics
where cs = control surface, cv = control volume, = dot product between the velocity vector and the differential area vector, and dv = differential volume.
Continuity at a point: In the limit that cv → 0, the integral form of the continuity equation becomes the following differential form:
where u, v, w = velocity components in the x, y, z coordinate directions.

## Slide 6: Review of Basic Fluid Mechanics
Conservation of Linear Momentum
This is based on Newton’s second law of motion – the sum of the external forces acting on a body is equal to the time rate of change of the linear momentum of the body. The integral form of this equation is:
where FS = surface forces, e.g., normal and shear stresses, and FB = body forces, e.g., force of gravity. The first term on the right-hand side is the convective acceleration and the second term is the temporal acceleration, both multiplied by ρ.

## Slide 7: Review of Basic Fluid Mechanics
Equations of Motion: In the limit that cv → 0, the integral form of the conservation of mass equation becomes the following differential forms:

## Slide 8: Review of Basic Fluid Mechanics
where Ax, Ay and Az = coefficients of turbulent viscosity. Ranges of values for Ax and Ay are 10-2 to 102, and for Az are 10-6 to 10-2.
These equations incorporate the following Boussinesq type relationship between the turbulent (Reynolds) shear stress and a spatial velocity gradient:

## Slide 9: Hydrodynamics
The hydrodynamics of a water body are described by the continuity equation, the equations of motion, an equation of state, i.e., ρ = F(p,S,T), and the following transport equations for temperature (T) and salinity (S), respectively:
where Ki = coefficients of turbulent diffusion, and QT = thermal sources/sinks

## Slide 10: Hydrodynamics
The system of equations described on the previous slide provides a closed system for the variables u, v, w, p, ζ, ρ, S, and T, provided that the vertical turbulent viscosity and diffusivity and the source and sink terms are specified. To determine values for the vertical turbulent viscosity and diffusivity, a turbulence closure model is typically used.
Isotropic eddy viscosity models such as i) the zero equation (mixing length) model in which the mixing length is assumed proportional to a characteristic length scale of the flow and obtained algebraically; ii) the one-equation model, which employs one additional partial differential equation for the velocity scale and the length scale is
specified algebraically; and iii) the two-equation (k-ε)

## Slide 11: Hydrodynamics
model, which employs two partial differential equations, one for the velocity scale and one for the length scale, are widely used in hydrodynamic models. These models assume that there exists an analogy between the action of viscous stresses and Reynolds stresses on mean flow; the transport of momentum by turbulent fluctuations is assumed similar to the random molecular motion in laminar flows.
Isotropic eddy viscosity models are based on the Boussinesq approximation [accounts for variations in density only in the gravity term], and cannot reproduce the anisotropy of Reynolds stresses. These models have been shown to fail in flows involving secondary motions

## Slide 12: Hydrodynamics
such as flows in strongly curved ducts and channels. When the fluctuations and the scale of the turbulence are not constant and the turbulence effects develop in different directions, equations for turbulent stress and mass flux are used instead of the kinetic energy equation (k).

## Slide 13: Basic Principles of Hydrodynamic Modeling
Identify and quantify driving forces
Identify and quantify sources and sinks of water mass
Choose appropriate modeling domain
  open water boundaries should be sufficiently far removed from the area of interest in the water body
  boundaries should be chosen where boundary values are known or can be measured
Decide what type of hydrodynamic model should be applied to the modeling domain
Decide what level of spatial discretization is needed to adequately represent the geometry and bathymetry of the water body as well as the driving forces and the significant physical processes that determine the movement of water

## Slide 14: Driving Forces
Freshwater stream/river with unidirectional flow
  Gravitational force (proportional to gradient)
  Tributary inflows
  Direct runoff into water body during runoff events
  Wind
Lake/reservoir
  Wind
  Tributary inflows
  Discharge from dam
  Thermal stratification
  Direct runoff into water body during runoff events

## Slide 15: Driving Forces
Stream/river with oscillatory flow
  Gravitational force (proportional to gradient)
  Astronomical tides
  Tributary inflows
  Spatial (horizontal and vertical) salinity gradients
  Direct runoff into water body during runoff events
  Wind
Estuary/Bay/Coastal seas
  Astronomical tides
  Freshwater discharge
  Spatial (horizontal and vertical) salinity gradients
  Wind
  Coriolis force
  Atmospheric pressure gradients
  Direct runoff into water body during runoff events

## Slide 17: Types of Hydrodynamic Models
Hydraulic models were developed only for one-dimensional (1D) applications for lateral and depth averaged streams and rivers and require several simplifying approximations to the equations of motion. Some hydraulic models were developed from empirical approximations such as the well known Manning’s equation for open channel flows. Even this simplified equation is based on conservation of linear momentum for steady, uniform flows (thus, the acceleration terms in the equations of motion are zero), and expresses the balance of the driving force (proportional to the bottom slope or gradient) and the retarding force (i.e., bottom friction).

## Slide 18: Types of Hydrodynamic Models
Hydrodynamic models use fewer approximations to the equations of motion. Using time-averaged forms of the Navier-Stokes equations for fluid motion, hydrodynamic models simulate the transport and mixing of surface waters where water motion is influenced by the geometry and bathymetry of the water body, freshwater inflows, water surface elevation, and physical processes such as bottom friction, winds, turbulent mixing, and horizontal and vertical thermal and salinity stratification. In estuarine and coastal waters, tidal forcing and salinity gradients are major factors that control circulation processes. These models can fairly realistically represent complex shoreline geometry and bathymetry with two-dimensional (2D) and three-dimensional (3D) grids. But they require advanced numerical methods to solve the time dependent governing equations for the spatial and temporal variations of water surface elevation, flow velocity, salinity, and water temperature.

## Slide 19: Types of Hydrodynamic Models
One-dimensional (1D) hydraulic models solve the cross-sectionally averaged conservation of mass and conservation of linear momentum equations. The state variables solved for are the water surface elevation (i.e., stage) and discharge at discrete locations along the modeled water body. An 1D hydrodynamic model is an appropriate representation for waterbodies in which the most significant water quality constituent gradient is along the longitudinal (x) axis in the direction of flow of the stream or river. The vertical (z) and lateral (y) dimensions are assumed to be well-mixed since the gradients of water quality constituents in these directions are considered to be negligible in relation to the dominant longitudinal (x) gradient. Thus, an 1D model would be appropriate for describing the flow of water and mass transport of sediment in low-order streams and rivers of moderate width and depth. However, the application of an 1D model to a reservoir characterized by vertical temperature

## Slide 20: Types of Hydrodynamic Models
stratification or a tidal river characterized by pronounced lateral and/or vertical gradients of salinity (e.g., partially mixed to salt-wedge estuaries) would not be an appropriate choice.
Transport in a free-flowing stream can be represented using a kinematic wave hydraulic model. The main limitations of a kinematic wave model are: 1) the slope of the free water surface matches the slope of the stream bed; and 2) mass is conserved, but linear momentum is not. Thus, in a kinematic wave model, downstream controls do not exert an influence on upstream flow conditions like they do for subcritical flows (Fr = V/(gH)1/2 < 1). Based on the Peclet number, mass transport in streams is dominated by advection, with dispersive transport normally a minor component of the mass flux of a constituent (Imhoff et al. 2003).

## Slide 21: Types of Hydrodynamic Models
Two-dimensional, laterally-averaged (2DV) models solve the laterally-averaged conservation of mass and conservation of momentum equations. The state variables solved for are the water surface elevation (i.e., stage) and the longitudinal (x) and vertical (z) components of the laterally-averaged velocities at specified elevations above the bottom of the water body. A 2DV model is an appropriate representation for waterbodies where the most significant water quality constituent gradients are observed in the longitudinal (x) and vertical (z) dimensions. Relatively deep, narrow stratified freshwater lakes (e.g., Finger Lakes in New York State), reservoirs, tidal rivers, estuaries and fjords are often modeled using 2DV hydrodynamic models. In such a vertically stratified waterbody, the lateral dimension (y) is considered well-mixed since the lateral (or cross-shore) gradients of water quality constituents are much smaller than the vertical and longitudinal gradients.

## Slide 22: Types of Hydrodynamic Models
In a 2DV model, advection and dispersion must both be represented in the longitudinal and vertical dimensions. Horizontal and vertical dispersion coefficients, at a minimum, must be defined by appropriate length scale empirical formulations. One-equation and two-equation methods provide increasingly realistic approximations for horizontal and vertical turbulent diffusivities required by turbulence closure. Time variable upstream and lateral boundary conditions of flow and/or water surface elevation, and downstream boundary conditions that represent a control structure based on a rating curve of stage height versus flow over the outlet should be capable of being specified for a 2DV model of flow in a reservoir.

## Slide 23: Types of Hydrodynamic Models
Two-dimensional, vertically-averaged (2DH) models solve the vertically-averaged conservation of mass and conservation of momentum equations. The state variables solved for are the water surface elevation (i.e., stage) and the longitudinal (x) and lateral (y) components of the vertically-averaged velocities at specified horizontal locations through the water body being modeled. A 2DH model is an appropriate representation for waterbodies where the most significant water quality constituent gradients are observed in the horizontal (x,y) dimensions. In a two-dimensional (horizontal) waterbody, the vertical dimension (z) is considered well-mixed since the vertical gradient of a water quality constituent is much smaller than horizontal gradients. Relatively shallow, wide, thermally unstratified freshwater lakes, reservoirs, tidal embayments and lagoons are typically modeled with a 2DH model. Where a temperature or salinity stratified water column exists, a 2DH model is not an appropriate

## Slide 24: Types of Hydrodynamic Models
choice. In addition, an 1D hydraulic model is not an appropriate choice for a well-mixed water body with horizontal constituent gradients.
In a 2DH model of a vertically well-mixed water body, advection and dispersion must both be represented in the horizontal dimensions. Horizontal dispersion coefficients must be defined by appropriate length scale empirical formulations. In addition, time variable upstream and lateral boundary conditions of flow and/or water surface elevation, and downstream boundary conditions of either flow or water surface elevation must be specified.

## Slide 25: Types of Hydrodynamic Models
Three-dimensional (3D) models solve the non-spatially integrated conservation of mass and conservation of momentum equations. The state variables solved for are the water surface elevation and the 3D components of the flow velocity at specified horizontal and vertical (i.e., distance above the bottom) locations through the water body being modeled. A 3D model is the most physically realistic representation for a water body where significant constituent gradients occur in the longitudinal (x), lateral (y) and/or vertical (z) dimensions. Relatively deep and large stratified lakes, reservoirs, bays, estuaries and coastal seas are usually most appropriately modeled with a 3D model. Estuaries in which significant horizontal and vertical gradients of salinity occur should be modeled with 3D hydrodynamic models.

## Slide 26: Types of Hydrodynamic Models
Both advection and dispersion must be represented in the horizontal and vertical dimensions. Horizontal and vertical dispersion coefficients must be defined by appropriate length scale zero-order empirical formulations. One-equation and two-equation methods provide increasingly realistic approximations for horizontal and vertical turbulent diffusivities required by turbulence closure.
3D models of estuarine and coastal ocean circulation need to simulate both barotropic and baroclinic components of flow as well as the Coriolis force. In addition, time variable upstream and lateral boundary conditions of freshwater inflow and/or water surface elevation and tidal forcing and salinity at the downstream open water boundary must be specified for a 3D model in a stratified estuary.

## Slide 27: Types of Hydrodynamic Models
For coastal ocean models, the more important boundary condition is the specification of the spatial gradient of longshore and cross-shelf sea surface elevations at the offshore, updrift and downdrift open water boundaries. For example, in the Middle Atlantic Bight off the mid-eastern US coastline there is a difference of approximately 10 to 15 cm in the ocean surface elevation over the 700 km from Cape Cod to Cape Hatteras. This head difference generates a mean southwest current of ~3 to 5 cm/sec. In addition to the description of ocean surface elevation as an open boundary condition, time variable boundary inputs of river discharge from the coast must be specified.

## Slide 28: Generic Modeling Principles
Consider modeling results in conjunction with empirical data to inform site decision-making
Develop and refine a conceptual site model that identifies the key areas of uncertainty where modeling information may be needed
Consider water body complexity before deciding if a numerical model is necessary

## Slide 29: Generic Modeling Principles
Determine what model output data are needed to facilitate decision-making
Conduct a complete modeling study
  Verified model(s) should be used
  Model calibration
  Model validation
  Sensitivity analysis
  Uncertainty analysis
  (see “Definitions of modeling terms.doc”)