## Slide 1: Introduction to Modeling Toxicity and Pathogens

## Slide 2: Ammonia and toxicity
Sources:
  About three-fourths of the ammonia produced in the United States is used in fertilizers either as the compound itself or as ammonium salts such as sulfate and nitrate.
  Large quantities of ammonia are used in the production of nitric acid, urea and nitrogen compounds.
  It is used in the production of ice and in refrigerating plants.
  "Household ammonia" is an aqueous solution of ammonia. It is used to remove carbonate from hard water.
  Since ammonia is a decomposition product from urea and protein, it is found in domestic wastewater.
  Aquatic life and fish also contribute to ammonia levels in a stream.

## Slide 3: Ammonia and toxicity
Impacts
  NH3 is the principal form of toxic ammonia.
  It has been reported toxic to fresh water organisms at concentrations ranging from 0.53 to 22.8 mg/L.
    Toxic levels are both pH and temperature dependent. Toxicity increases as pH increases and as temperature increases.
    Plants are more tolerant of ammonia than animals, and invertebrates are more tolerant than fish. Hatching and growth rates of fishes may be affected. In the structural development, changes in tissues of gills, liver, and kidneys may also occur.
    Toxic concentrations of ammonia in humans may cause loss of equilibrium, convulsions, coma, and death.

## Slide 4: Toxicity Reduction Procedures for State of Mississippi
1) A detailed review of the permit application and any historical bioassay data and the use of specific screening procedures.
  To identify the universe of those facilities which have discharges which are potentially toxic instream.
  To determine whether the data in an application has been submitted in strict adherence with EPA accepted analytical procedures with all of the appropriate parameters reported.

## Slide 5: Toxicity Reduction Procedures for State of Mississippi
2) The development of permit limits in accordance with accepted state and national water quality criteria for those facilities exhibiting potential toxicity. Permit limits may take the form of chemical specific and/or whole effluent toxicity based limits.
3) Additional testing and actual toxicity reduction for those facilities which fail any whole effluent toxicity requirements included in their permits. Permits addressing whole effluent toxicity have specific language requiring the permittee to perform a Toxicity Reduction Evaluation (TRE) upon non-compliance with the whole effluent toxicity limitations contained in the permit.

## Slide 6: Ammonia
Equilibrium Reaction
- The toxicity of aqueous ammonia to aquatic organisms is primarily attributable to the unionized form
- The percent unionized ammonia can be calculated from
Where Ka is a function of pH and temperature

## Slide 7: Ammonia
and
Where Ta is the absolute temperature (oK)

## Slide 9: Ammonia Toxicity
Ammonia nitrogen toxicity criterion (ANTC) shall be applied as follows:
  (1) Minor Municipal and Minor Industrial Dischargers
    (a) If application of the ANTC indicates a limit greater than 1 mg/l but less than 2 mg/l, the permit limit will be 2 mg/l and no effluent biomonitoring will be required.

## Slide 10: Ammonia Toxicity
Ammonia nitrogen toxicity criterion (ANTC) shall be applied as follows:
  (1) Minor Municipal and Minor Industrial Dischargers
    (b) If application of the ANTC indicates a limit less than 1 mg/l, the permit limit will be 2 mg/l, with a requirement for effluent biomonitoring. If existing effluent biomonitoring indicate no effluent toxicity, the permit will not require effluent biomonitoring.
    © If any existing biomonitoring data indicate adverse impact due to ammonia toxicity, a permit will contain an ammonia nitrogen limit protective of water quality.

## Slide 11: Ammonia Toxicity
(2) Major Municipal and Major Industrial Dischargers
  (a) If application of the ANTC indicates a limit less than 2 mg/l, the permit limit will be 2 mg/l, with a requirement for effluent biomonitoring. Effluent biomonitoring will not be required if existing data indicate that the discharge is not toxic.
  (b) If any biomonitoring data indicate adverse impact due to ammonia toxicity, a permit will contain a limit for ammonia nitrogen protective of water quality.

## Slide 12: Bacteria and Pathogens
Indicator organisms
  Total coliform (TC): exist in polluted and unpolluted solids and occur in feces of warm-blooded animals (E. coli is a common member of this group)
  Fecal coliform (FC): a subset of TC that come from intestines of warm blooded animals
  Fecal streptococci (FS): include several varieties of streptococci that come from humans and domesticated animals

## Slide 13: Modeling Approaches
Factors affecting
  temperature
  salinity
  settling
  solar radiation
  base mortality

## Slide 14: Estimation of loss rates
Light
Settling
Mortality
where PS is the fraction sea water, T temperature,  a proportionality constant, ke the light extinction coefficient, Io the surface light intensity, H depth, Fp the fraction attached, and vS a settling velocity. Note that the first equation assumes a fresh water mortality rate of 0.8/day at 20oC.