## Slide 1: WASP7 Periphyton (Benthic Algae) Processes
Processes and Equations Implemented in WASP7 Advanced Eutrophication Module
Prepared by
Robert B. Ambrose, Jr.
July, 2010; update July 2013

## Slide 2: Variables and Processes
Periphyton Biomass
D : C : N : P : Chl
qP
qN
Phytoplankton Biomass
Group 3
D : C : N : P : Si: Chl
DO
Group 2
D : C : N : P : Si: Chl
Group 1
D : C : N : P : Si : Chl
TIC
H2CO3 – HCO3- – CO32-
Total
Alkalinity
Particulate Detrital OM
Si
P
N
C
D
Dissolved OM
Si
P
N
CBOD1
CBOD2
CBOD3
Inorganic Nutrients
NO3
PO4
SiO2
NH4
pH
atmosphere
uptake
excretion
Inorganic Solids
S3
S1
S2
oxidation
oxidation
nitrification
photosynthesis and respiration
death
dissolution
mineralization
sorption
reaeration

## Slide 3: Benthic Algae Biomass Nutrient Ratios
Total Dry Weight
ab [gD/m2]
Biomass composition D : C : N : P : Chl
Total
cell N
qN
[mgN/gD]
Total
cell P
qP
[mgP/gD]
Symbol | Kinetic Constant | Units | Value | Range
ADC | detritus to carbon ratio | gD/gC | 2.5 | 2 – 5
ANC | nitrogen to carbon ratio | gN/gC | 0.18 | 0.06 – 0.3
APC | phosphorus to carbon ratio | gP/gC | 0.025 | 0.01 – 0.08
AChlC | chlorophyll to carbon ratio | gChl/gC | 0.02 | 0.008 – 0.04
ROC | oxygen to carbon ratio | gO2/gC | 2.67 | 
Input nutrient ratio constants describe structural biomass. Variables qN and qP are total cell nitrogen and phosphorus content, including biomass and stored inorganic N and P.
Notes: qP and qN are total internal P and N, including inorganic and organic fractions. The biomass ratios are for organic D, C, N, P, and Chl. The fractions fopb and fonb are calculated internally from simulated qN and qP along with input ADC, ANC, APC.

## Slide 4: Benthic Algae Kinetic Processes
Light
Temperature
PO4
NO3
NH4
Detrital
C,N,P
DON, DOP
ab [gD/m2]
biomass
D : C :
N : P : Chl
qN
mgN/gD
qP
mgP/gD
FDb
FEPb
FGb
FRb
FUPb
FENb
FUNb
fopb
fonb
1-fopb
1-fonb
Carrying
Capacity
Notes: qP and qN are total internal P and N, including inorganic and organic fractions. The biomass ratios are for organic D, C, N, P, and Chl. The fractions fopb and fonb are calculated internally from simulated qN and qP along with input ADC, ANC, APC.

## Slide 5: Benthic Algae Biomass Kinetic Equation
Where, for benthic algae in segment i: | 
ab = | benthic algal density (gD/m2)
FGb = | growth rate (gD/m2-day)
FRb = | respiration rate (gD/m2-day)
FDb = | death rate (gD/m2-day)
Ab = | bottom substrate surface area (m2)
Periphyton Biomass, ab
gD/m2
D : C : N : P : Chl
qN
mgN/gD
qP
mgP/gD

## Slide 6: Benthic Algal Growth, option 0
Zero-order growth rate (gD/m2-day):
Where, for benthic algae in segment i: | 
FGb20 = | maximum growth rate at 20 C, gD/m2-day (30, 10 – 100)
ΦTb = | temperature growth multiplier (0 – 3)
ΦLb = | light growth multiplier (0 – 1)
ΦNb = | nutrient growth multiplier (0 – 1)

## Slide 7: Benthic Algal Growth, option 1
First-order growth rate (gD/m2-day):
Where, for benthic algae in segment i: | 
kGb20 = | maximum growth rate constant at 20 C, 1/day (1.5, 0.5 – 2.5)
ΦTb = | temperature growth multiplier (0 – 3)
ΦLb = | light growth multiplier (0 – 1)
ΦNb = | nutrient growth multiplier (0 – 1)
ΦSb = | space growth multiplier (0 – 1)

## Slide 8: Standard Temperature Function for Benthic Algal Growth
Temperature multiplier:
Where, for benthic algae in segment i: | 
θGb = | temperature correction factor for growth (1.07, 1.05 – 1.1)
T = | water temperature, C

## Slide 9: Light Effect on Benthic Algal Growth
It , Ly/day
H, m
I0 = Xr XshdXice It
Ib = I0 e-keH
ke, m-1
Where, for total light energy (values are half for photosynthetically active radiation, PAR): | 
It = | surface light intensity at time t, Ly/day (0 – 800 daily average), (0 – 2200 instantaneous)
Xi = | surface reflection, canopy shading, and ice reduction loss (0 – 1)

## Slide 10: Light Limitation Equations
1. Half-Saturation:
2. Smith:
3. Steele:
Where, for total light energy (values are half for photosynthetically active radiation, PAR): | 
KLb = | saturating light intensity for bottom algae, Ly/day (130, 50 – 300 total radiation)

## Slide 11: Nutrient Limitation of Benthic Algal Growth
Where, for benthic algae in segment i: | 
q0N = | minimum N cell quota supporting growth, mgN/gD (7, 4 – 20)
q0P = | minimum P cell quota supporting growth, mgP/gD (1, 0.5 – 5)

## Slide 12: Space Limitation of Benthic Algal Growth
Where, for benthic algae in segment i: | 
abmax = | maximum carrying capacity, gD/m2 (5 – 100)
 | (used in first-order growth equation)

## Slide 13: Benthic Algal Attenuation
Where, for benthic algae in segment i: | 
ab = | benthic algal density (gD/m2)
FRb = | respiration rate (gD/m2-day)
FDb = | death rate (gD/m2-day)
Ab = | bottom substrate surface area (m2)
Periphyton Biomass, ab
gD/m2
D : C : N : P : Chl
qN
mgN/gD
qP
mgP/gD

## Slide 14: Benthic Algal Respiration and Death
First order respiration and death rates:
Where, for benthic algae in segment i: | 
kRb20 = | respiration rate constant at 20 C, 1/day (0.1, 0.05 – 0.2)
θRb = | temperature correction factor for respiration (1.07, 1.05 – 1.08)
kDb20 = | death rate constant at 20 C, 1/day (0.02, 0.001 – 0.2)
θDb = | temperature correction factor for respiration (1.07, 1.05 – 1.08)

## Slide 15: Benthic Algae Nutrient Kinetic Equations
Periphyton Biomass, ab
gD/m2
D : C : N : P : Chl
qN
mgN/gD
qP
mgP/gD
Where, for benthic algae in segment i: | 
qN, qP = | algal cell N, P (mgN/gD, mgP/gD)
FUNb , FUPb = | uptake rates (gN/m2-day, gP/m2-day)
FENb , FEPb = | excretion rates (gN/m2-day, gP/m2-day)
FDNb , FDPb = | death rates (gN/m2-day, gP/m2-day)
ab = | algal biomass density (gD/m2)

## Slide 16: Benthic Algal Nitrogen Uptake
Where: | 
ρmN | = maximum N uptake rate (mgN/gD-day)
KsNb | = external N half-saturation constant for uptake (mgN/L)
KqN q0N | = internal N half-saturation constant for uptake (mgN/gD) = minimum N cell quota supporting growth (mgN/gD)
ab | = bottom algal biomass (gD/m2)
qN
NO3
NH4

## Slide 17: Benthic Algal Ammonia Preference Factor
PNH4b
qN
NO3
NH4
1 – PNH4b
Where: | 
Khnxb | = ammonia preference factor, mgN/L (0.025, 0.01 – 0.5)
DIN = NH4 + NO3
for Khnxb >> DIN PNH4b = NH4 / DIN
for Khnxb = NH4 = NO3 PHN4b = 0.5
for Khnxb = 0 PNH4b = 1
for NO3 = 0 PNH4b = 1
for NH4 = 0 PNH4b = 0

## Slide 18: Benthic Algal Phosphorus Uptake
Where: | 
ρmP | = maximum P uptake rate (mgP/gD-day)
KsPb | = external P half-saturation constant for uptake (mgP/L)
KqP q0P | = internal P half-saturation constant for uptake (mgP/gD) = minimum P cell quota supporting growth (mgP/gD)
ab | = bottom algal biomass (gD/m2)
qP
PO4

## Slide 19: Benthic Algal Nutrient Excretion
Where: | 
kEb20 | = nutrient excretion rate constant at 20 C, 1/day (0.05, 0.02 – 0.1)
θEb20 | = temperature correction factor for excretion (1.07, 1.05 – 1.08)
fONb fOPb | = organic fraction of excreted N = organic fraction of excreted P
ab | = bottom algal biomass (gD/m2)
qN, qP
PO4
NH4
DON, DOP,
CBODi
fOPb
fONb
1-fOPb
1-fONb

## Slide 20: Benthic Algal Nutrient Loss with Death
Where: | 
FDb | = death rate, gD/m2-day (0.05, 0.01 – 0.5)
fONb fOPb | = organic fraction of algal N = organic fraction of algal P
qN, qP
PO4
NH4
Detrital
N, P
fOPb
fONb
1-fOPb
1-fONb

## Slide 21: Implementation in WASP

## Slide 22: Typical Benthic Algal Rates
Maximum growth rate  30 g/m2-day (10-100)
Respiration rate  0.1 day-1 (0.05-0.2)
Death rate  0.05 day-1 (0.01-0.5) (During sloughing could be higher)
Nutrient half-saturation constants tend to be higher that phytoplankton by a factor of 10 to 100

## Slide 23: Summary of Kinetic Constants Benthic Algal Biomass Composition
Symbol | Kinetic Constant | Units | Value | Range
ADC | Detritus to carbon ratio | gD/gC | 2.5 | 2 – 5
ANC | Nitrogen to carbon ratio | gN/gC | 0.18 | 0.06 – 0.3
APC | Phosphorus to carbon ratio | gP/gC | 0.025 | 0.01 – 0.08
AChlC | Chlorophyll to carbon ratio | gChl/gC | 0.02 | 0.008 – 0.04
ROC | Oxygen to carbon ratio | gO2/gC | 2.67 | 
Notes: qP and qN are total internal P and N, including inorganic and organic fractions. The biomass ratios are for organic D, C, N, P, and Chl. The fractions fopb and fonb are calculated internally from simulated qN and qP along with input ADC, ANC, APC.

## Slide 24: Summary of Kinetic Constants Benthic Algal Growth
Symbol | Kinetic Constant | Units | Value | Range
FGb20 | Maximum growth rate | gD/m2-day | 30 | 10 – 100
kGb20 | Maximum growth rate constant | 1/day | 1.5 | 0.5 – 2.5
θGb | Temperature correction factor |  | 1.07 | 1.05 – 1.1
KLb | Saturating light intensity (total) | Ly/day | 130 | 50 – 300
KLb | Saturating light intensity (PAR) | Ly/day | 65 | 25 – 140
q0N | Minimum cell quota for N | mgN/gD | 7 | 4 – 20
q0P | Minimum cell quota for P | mgP/gD | 1 | 0.5 – 5
abmax = | Maximum carrying capacity | gD/m2 | 20 | 5 – 100

## Slide 25: Summary of Kinetic Constants Benthic Algal Attenuation
Symbol | Kinetic Constant | Units | Value | Range
kRb20 | Respiration rate constant at 20 C | 1/day | 0.1 | 0.05 – 0.2
θRb | Temperature correction factor for respiration |  | 1.07 | 1.05 – 1.08
kDb20 | Death rate constant at 20 C | 1/day | 0.02 | 0.001 – 0.2
θDb | Temperature correction factor for death |  | 1.07 | 1.05 – 1.08
Notes: qP and qN are total internal P and N, including inorganic and organic fractions. The biomass ratios are for organic D, C, N, P, and Chl. The fractions fopb and fonb are calculated internally from simulated qN and qP along with input ADC, ANC, APC.

## Slide 26: Summary of Kinetic Constants Benthic Algal Nutrient Uptake
Symbol | Kinetic Constant | Units | Value | Range
ρmN | Maximum N uptake rate | mgN/gD-day | 720 | 200 – 2000
KsNb | External N half-sat constant for uptake | mgN/L | 0.2 | 0.05 – 0.8
KqN | Internal N half-sat constant for uptake | mgN/gD | 9 | 5 – 20
q0N | Minimum N cell quota for growth | mgN/gD | 7.2 | 100 – 500
Khnxb | Ammonia preference factor | mgN/L | 0.025 | 0.01 – 0.5
ρmN | Maximum P uptake rate | mgP/gD-day | 50 | 10 – 200
KsPb | External P half-sat constant for uptake | mgP/L | 0.03 | 0.002 – 0.1
KqP | Internal P half-sat constant for uptake | mgP/gD | 1.3 | 0.5 – 5
q0P | Minimum P cell quota for growth | mgP/gD | 1 | 0.5 – 5

## Slide 27: Summary of Kinetic Constants Benthic Algal Nutrient Excretion
Symbol | Kinetic Constant | Units | Value | Range
kEb20 | Nutrient excretion rate constant at 20 C | 1/day | 0.05 | 0.02 – 0.1
θEb20 | Temperature correction factor for excretion |  | 1.07 | 1.05 – 1.08
fONb | Organic fraction of excreted N |  | 0* | 0 – 0.5
fOPb | Organic fraction of excreted P |  | 0* | 0 – 0.5
* If constants fONb and fOPb are set to 0, WASP will calculate these as time-variable fractions equal to the structural biomass nutrient ratio divided by the total cell nutrient quota (qN and qP):
fONb = 1000 (ANC/ADC) / qN fOPb = 1000 (APC/ADC) / qP

## Slide 28: Benthic Algae Spatial Settings
Parameters
Bottom habitat [fraction of bottom area]
Initial Concentrations
Algal biomass [gD/m2]
Cell nitrogen [mgN/gD]
Cell phosphorus [mgP/gD]

## Slide 29: Benthic Algae Output
Num | Variable | Units
64 | Benthic Algae Biomass | gD/m2
65 | Benthic Algae Light Limit | -
66 | Benthic Algae Nutrient Limit | -
67 | Benthic Algae N Cell Quota | mgN/gD
68 | Benthic Algae P Cell Quota | mgP/gD
69 | Benthic Algae Chlorophyll | mgA/m2
70 | Benthic Algae Cell N:Chl | mgN/mgA
71 | Benthic Algae Cell P:Chl | mgP/mgA

## Slide 30: Test River Algae, DO Output

## Slide 31: Test River Nutrient Output

## Slide 32: Test River NH4, NO3 Output