## Slide 1: A Waterbody Specific Approach for Developing Mercury TMDLs
Tim Wool
Senior Water Quality Modeler
Standards, Monitoring and TMDL Branch
US EPA Region 4

## Slide 2: Who’s Idea was it to do Hg TMDLs
Lawsuit filed by Sierra Club et. al. in 1994/ settled in 1997
1997 Consent Decree requires a schedule for TMDL development in Georgia:
  1999/2004 - Savannah/Ogeechee Basins (Completed)
  2000 – Ochlockonee, St. Marys, Satilla, Suwannee Basins (Completed)
  2001 - Oconee/Ocmulgee/Altamaha Basins (Completed)
  2002 - Chattahoochee/Flint Basins (Propose 8/02)
  2003 - Coosa/Tallapoosa/Tennessee Basins (Propose 8/02)

## Slide 3: The TMDL Planning Process
Complete the Last TMDL Assigned to You
Management Informs you that Hg TMDL Needs to be proposed in 45 days
  15 Days is taken up from getting over the laughter
  30 Days Spent reaching into the magical hat
  44 Days Hope you pull something out of the Hat that looks like a……..
Hg TMDL

## Slide 4: Mercury TMDLs in Georgia
Savannah River (7 segments)
    Clarks Hill Lake to Tide Gate
    7 segments – Fish Consumption Guidelines
    1 segment – mercury in water
  Savannah River Mercury TMDL
    Proposed 2/8/00
    Granted Extension
    Finalize in 2/28/01

## Slide 5: Mercury TMDLs in GA (cont.)
South Georgia Four Basins: 22 TMDLs are Finalized
  Ochlockonee Basin: 4 segments
  St. Marys Basin: 3 segments
  Satilla Basin: 7 segments
  Suwannee Basin: 8 segments

## Slide 6: TMDL Development
Must do the TMDLs now
Waters Listed for Fish Tissue Contamination
Fish Tissue is the Appropriate TMDL End-Point
Latest Human Health Methodology (BAF) -Calculate Ambient
Protective Ambient Concentration Below State Aquatic Life Standard

## Slide 7: Mercury Characteristics
Persistent Chemical
  Does Not Degrade
  Naturally Occurring Element
    Weathering
  Readily Changes Form
    Mediated by both Chemical & Biological Processes
    It is not fully understood what controls the changes in form

## Slide 8: Mercury Cycling

## Slide 9: The Technical Approach

## Slide 10: End Point Determination (Original Approach)
Start with Fish Tissue Concentration (0.23 mg/kg) Threshold at which Georgia Issue Fish Consumption Guidelines
Gather Site Specific Data (fraction MeHg, BAF)
Back Calculate Water Concentration to Achieve Less than 0.23 mg/kg Total Hg in Fish
Determine Total Maximum Load of Total Hg to Achieve Target
Determine Current Loadings
  Point Sources
  Nonpoint Sources

## Slide 11: End Point Determination (Current Approach)
Using Methylmercury Criterion Trophic Weighed Fish Tissue Concentration of 0.3 mg/kg. New methodology adopted by State of Georgia to determine impairment
Gather Site Specific Data (Total Hg, fraction MeHg, Trophic Level BAF Values)
Back Calculate Water Concentration to Achieve Less than 0.3 mg/kg Total Hg in Fish Tissue
Determine Total Maximum Load of Total Hg to Achieve Target
Determine Current Loadings
  Point Sources
  Nonpoint Sources

## Slide 12
Hg, HgII, MeHg
Atmospheric Deposition
Wet & Dry
Watershed Loads
Interaction with Solids
Settling/Resuspension
Forage Fish/Plankton
Need to Develop Relationship Between:
Water Concentration & Loads
Fish Tissue & Water Concentration
NPDES Sources

## Slide 13: EPA Region 4 Mercury Sampling
Initiated Sampling Program for Mercury using ultra low-level analytical procedure (EPA 1631)
  Detection limit approximately 0.5 ng/l
  Previous detection limit much higher
Sampling 303(d) listed segments in Georgia
  Fish Tissue
  Water Column (Total Hg, MeHg, Filtered/Unfiltered)
  Sediments (Total Hg, MeHg, Filtered/Unfiltered)
  Soils (Total Hg, MeHg, Filtered/Unfiltered)

## Slide 14: EPA Region 4 Mercury Sampling
Data collected will be used for:
  Determination of appropriate End Point for the TMDL
    Site specific Bioaccumulation Factors
    Fraction of Total Hg that is MeHg
  Aid in the calibration of the watershed model
    Soil Concentration
  Aid in the calibration of the water quality model
    Fraction of Chemical that is MeHg
    Organic Carbon Content
    Site specific partition coefficients

## Slide 17: Step 1 - TMDL Target Determination
Georgia
  No Human Health Criteria/Interpret Narrative
  “End Point”=Fish Tissue less than 0.3 mg/kg
  Gather Site Specific Data
  Use EPA’s Human Health Methodology
  Back Calculate Water Concentration to achieve 0.3 mg/kg in fish
South Carolina
  Human Health Criteria = 12 ng/l

## Slide 18: Risk Based Calculation
where:
WQT= Water Quality Target
Reference Dose = 0.0001 mg/k MeHg
Body Weight (Average Person) = 70 kg
Units Conversion = 1.0E6
Consumption Rate = 0.0175 kg/day Fish (17.5 g/day)
Bioaccumulation Factor = ((Trophic 3 BAF * 8 g/day) + (Trophic 4 BAF * 5.7 g/day))/13.7 g/day
Fraction of the Total Mercury as Methyl Mercury = 0.21 as measured in the Alapaha Watershed

## Slide 20: Calculate the Total Allowable Load
Mercury Air Deposition Runoff Model (Developed by EPA/ORD)
  Added a soil runoff component (EPA/R4)
  Routes mercury deposition from impervious and water surfaces to tributaries
  Transports mercury bound to soil from watershed to tributaries
  Delivers mercury through tributary system with reduction/volatilization Loss
WASP Model transports mercury in the Waterbody
Determine annual average load of mercury
  Current loading
  Reductions needed to meet WQS

## Slide 21: Atmospheric Deposition Rates
RELMAP Coverage
  Atmospheric Model to predict the distribution and deposition rate of mercury (wet and dry)
  Used in the Mercury Report to Congress
    Based upon older emissions inventory
    Emissions inventory currently being updated
Mercury Deposition Network (MDN)
  Wet Deposition
  Site Specific

## Slide 23: Preliminary Characterization of Air Sources and Deposition
Atmospheric deposition of mercury to this basin is the main loading
  Deposition by: Wet (rain) and Dry (particles & gases)
  Deposition of mercury is significant across eastern USA
We used national RELMAP model, 1997 Mercury Study Report to Congress
  Inventory of emissions: point sources in all States
  Annual emissions data for 1994 -1996 period
  RELMAP models weather, transport, chemistry, & deposition

## Slide 24: Preliminary Characterization of Air Sources and Deposition
RELMAP data & results in Report to Congress got comprehensive review
For the Savannah River TMDL, we did
  Detailed study of RELMAP deposition (per square meter) to this basin
  Emissions data on sources in basin + 100 km (60 mi) around the basin

## Slide 25: Preliminary Characterization of Air Sources and Deposition
We define “Airshed” as: this basin and 100 km band around the basin
  Includes all/part of 51 Counties in GA and 29 counties in SC
  Emissions data (RELMAP) for 80 point sources in these Counties

## Slide 26: Preliminary Characterization of Air Sources and Deposition
Source categories within the Airshed
  Hospital, medical and infectious waste incinerators [36]
  Electric utility boilers (coal, oil, and gas) [17]
  Chlor-alkali plant (mercury cell) [1]
  Municipal solid waste combustors [3]
  Residential (heat) and Industrial boilers [80 Counties]
  Pulp and paper plant recovery furnaces [12]
  Portland cement manufacturing [3 including 2 that burn some hazardous waste]
  Municipal sewage sludge incinerators [6]
  Hazardous waste incinerators [2]

## Slide 27: Preliminary Characterization of Air Sources and Deposition
Year 2010 : predicted changed emissions from sources in airshed
  Growth estimate based on state or regional population growth
  Maximum Achievable Control Technology (MACT) for 4 categories
    results in reduced emissions
    Closed facilities as of 1999 -2000 given zero emissions in 2010

## Slide 28
This value indicates the number of counties in the study area with residential or industrial boilers.
The emissions inventory for the residential/industrial boiler source category provides total mercury emissions by county. Of the 80 total counties, 51 Counties are in Georgia and 29 are in South Carolina.

## Slide 29: Preliminary Conclusion :
Deposition of mercury to the basin between the base year (~1995) and 2010 will be greatly reduced based on:
  Maximum Achievable Control Technology (MACT)
  Additional reductions expected from air programs still being developed
  Voluntary controls and Pollution Prevention.

## Slide 30: Overview of Watershed Model
Extension to Watershed Characterization System
  ArcView Based
    DEM
    Meteorological Stations
    RF1/RF3/NHD
    Landuse
    Hg Deposition/RELMAP Model Predictions
    Soil Data
  Consistent with the approach used in the Mercury Report to Congress

## Slide 31
Atmospheric Deposition
Precipitation
Buildup in Soil
Reduction/Volatilization
Runoff
Erosion
Leaching
Attenuation
Receiving Waterbody Model

## Slide 34: Tributary Delivery from Watershed to Main Waterbody
Tributary delivery equation accounts for the attenuation of mercury loadings during the transport to main waterbody
  This module considers:
    watershed loading along the tributary length
    change in flow
    hydraulic geometry and residence time, TMAX
    reduction and volatilization, KRED
  Delivery Ratio = [1-exp(-Kred Tmax)]/KRED TMAX
  Applied for each subwatershed

## Slide 35: Waterbody Fate and Transport
Water Quality Model will be used to Determine Maximum Assimilative Capacity of the Savannah River
  This Considers:
    Change in Flow
    Chemical Cycling (Oxidation/Reduction, Methylation/Demethylation)
    Interaction with Sediments
    Volatilization

## Slide 36: Overview of Water Quality Model
US EPA’s Water Quality Assessment Simulation Program (WASP5)
  Used in EPA’s Mercury investigation in the Everglades

## Slide 37: Overview of Water Quality Model
Volatilization
Watershed Load
State Variables
Hg(0) Silt
Hg(II) Sand
MeHg
Burial
NPDES
DOC
Oxidation
Reduction
Methylation
Demethylation

## Slide 40: Fate & Transport

## Slide 42: Reduction Analysis

## Slide 43: WASP6 Workshops