## Slide 1: Sediment Transport

## Slide 2: Solids Effects on Water Quality
Sorption reduces dissolved NH4 and PO4
  Reduction in nitrification
  Reduction in algal uptake and growth
Deposition removes NH4 and PO4 from water
Sediment flux returns NH4 and PO4 to water
Solids increase light attenuation
  Reduction in algal growth

## Slide 3: Solids Effects on Toxicants
Sorption reduces dissolved fraction and bioavailability
Deposition removes some peak loading from water
Pore water diffusion, resuspension return chemical to water column between loading events
Large flood events scour significant amounts of sediment and chemical from the upper sediment to the water column
Net deposition stores chemical in sediments for long periods
Burial below bioturbation depth potentially sequesters chemical from biota

## Slide 4: WASP8 Solids Modeling
Independently models 1-10 solids state variables
  mg/L dry weight
Cobbles
  benthic segments only
  immobile, but can be buried

## Slide 5: WASP Solids Processes
Transport Processes
  Settling and deposition
  Scour (entrainment, resuspension)
  Bed load
  Burial
Kinetic Transformation Processes
  Production of biomass
  Respiration and death
  Dissolution of detritus

## Slide 6: Particle Size Classification
Size Range | Wentworth Name | Other Names
< 100 nm | nanoparticle | nanomaterial
< 1 μm | colloid | mud
1.0 – 3.9 μm | clay | mud
3.9 – 62.5 μm | silt | mud
62.5 - 125 μm | very fine sand | sand
125 - 250 μm | fine sand | sand
0.25 – 0.5 mm | medium sand | sand
0.5 – 1 mm | coarse sand | sand
1 – 2 mm | very coarse sand | sand
2 – 4 mm | granule | gravel
4 – 64 mm | pebble | gravel
64 – 256 mm | cobble | gravel
> 256 mm | boulder | gravel

## Slide 7: Particle Densities
Substance | Density [g/mL]
Organic matter (dry weight) | 1.27
Siliceous minerals | 2.65
Garnet sands | 4

## Slide 8: Benthic Parameter Equations
Where:
n = porosity [LW/L]
ρS = particle density, about 2.7 [gS/mLS]
ρW = water density, about 1.0 [gW/mLW]
Bulk Density [g/mL]
Dry Density [gS/mL]
Percent Water [g/gS]
sediment fresh weight / sediment volume
sediment dry weight / sediment volume
sediment fresh weight / sediment dry weight

## Slide 9: Solids Transport Methods
Solid flow fields (legacy approach)
Descriptive (option 0); user specified settling and resuspension
Process Based
  option 1: van Rijn equation
  option 2: Roberts equation

## Slide 10: Solid Flow Field Method
Legacy method used prior to WASP8 (Not recommended for new models)
Segment pairs for WC <--> Sed interactions
Allows compatibility of earlier wif files

## Slide 11: Descriptive Settling Method
User defines settling and resuspension rate for each solid state variable
Rates do not change with velocity
Settling rates should approximate Stokes’ Law
Rates are segment specific
Settling flux = deposition flux
where:
g = acceleration of gravity, 9.81 [m/sec2]
m = absolute viscosity of water
= 0.001 poise [kg/m-sec] at 20oC
ρs = sediment particle density [kg/m3]
ρ = water density [kg/m3]
D = particle diameter [m]

## Slide 12: Stokes Settling Velocities, m/day
Particle Diameter, mm | Particle Density, g/cm3 |  |  | 
 | 1.8 | 2.0 | 2.5 | 2.7
Fine Sand |  |  |  | 
0.1 | 380 | 470 | 710 | 800
0.05 | 94 | 120 | 180 | 200
Silt |  |  |  | 
0.05 | 94 | 120 | 180 | 200
0.02 | 15 | 19 | 28 | 32
0.01 | 3.8 | 4.7 | 7.1 | 8.0
0.005 | 0.94 | 1.2 | 1.8 | 2.0
0.002 | 0.15 | 0.19 | 0.28 | 0.32
Clay |  |  |  | 
0.002 | 0.15 | 0.19 | 0.28 | 0.32
0.001 | 0.04 | 0.05 | 0.07 | 0.08

## Slide 13: Process Based Solids Transport
Settling is a function of particle size and density
Deposition, erosion, bed load, and resuspension are functions of bottom shear stress, as well as particle size and density
Simulates cohesive and noncohesive transport
Burial based on mass balance of total solids within benthic segments
Van Rijn (option 1) or Roberts (option 2) erosion algorithms

## Slide 14: Noncohesive Deposition
Deposition Regimes
(mm)
Noncohesive deposition is settling attenuated by the shear stress from water flow:
αD = probability of deposition upon contact with bed; varies roughly linearly from 1 to 0 (Krone, 1963):
or, αD = 1 (Novotny and others)
.01 – 0.2 N/m2

## Slide 15: Noncohesive Erosion and Resuspension

## Slide 16: Sediment Transport Processes - Burial
Initial total solids concentration set reference bulk density (g/mL) and porosity (lw/L) for each segment
Bed Compaction Options
  Static (constant volumes)
  Dynamic (constant densities)
Dynamic option resets volume and depth each benthic time step

## Slide 17: Sediment Transport Processes - Burial
Burial velocities from any specified layer k are given by mass balance over solids types i.
Surficial sediment layer, k=1, bottom water = 0:
Subsurface sediment layers:
Where WD is deposition velocity, WR is resuspension velocity, WBL is bed load velocity, k is solids degradation rate constant, and d is layer depth.

## Slide 18: Basic Solids Transport Data
Systems
  Solid variable and name
  Particle density, g dw/mL (defaults to 2.65)
Constants
  Solids option (0 – descriptive; 1 & 2 – mechanistic)
  Particle diameter [mm]
Parameters
  Settling velocity [m/day]
  Resuspension velocity [m/day]
  Sediment cobble concentration [mg/L]

## Slide 19: Biotic Solids Toxicant Model
Net Production Rate for Solid i:
Net Dissolution Rate for solid i:
[g dw/m3-day]
[g dw/m3-day]

## Slide 20: Biotic Solids Eutrophication Model

## Slide 21: Biotic Solids Kinetic Data
Constants
  Solid Production Temperature Correction Factor (theta)
  Ash Dry Weight Residue [Fraction]
  Residue Solid Identification Number
  Organic Carbon Fraction [dimensionless]
  Dissolution Product DOC Identification Number
Parameters
  Biotic solids production rate [g/m3-day]
  Biotic solids dissolution rate [1/day]
Time Functions
  Biotic solids production rate multiplier
  Biotic solids dissolution rate multiplier

## Slide 22: River -> Lake - with Sediments
10 layer system, depths
  3 surface water, 1.5 m
  1 subsurface water, 1 m
  3 surface sediment, 2 cm
  3 subsurface sediment, 5 cm
Inflow
  Water, 104 m3/d
  Silt, 10 mg/L (BC)
  Sand, 40 kg/d
Ponded weir at lake boundary
Settling, 0.5 m/d
Resuspension, 0.05 mm/d
Silt

## Slide 23: Simulated Surface Sediment – River1

## Slide 24: Simulated Surface Sediment – River2

## Slide 25: Simulated Surface Sediment – Lake

## Slide 26: Simulated Subsurface Sediment – River1

## Slide 27: Simulated Subsurface Sediment – River2

## Slide 28: Simulated Subsurface Sediment – Lake

## Slide 29: River -> Lake - Dataset Parameters

## Slide 30: River -> Lake - State Variables

## Slide 31: River -> Lake - Segments

## Slide 32: River -> Lake - Initial Conditions

## Slide 33: River -> Lake Example - Parameters

## Slide 34: River -> Lake Example - Constants

## Slide 35: River -> Lake - Exchanges

## Slide 36: River -> Lake - Channel Geometry

## Slide 37: River -> Lake - Flow

## Slide 38: River -> Lake - Boundary Conditions

## Slide 39: River -> Lake - Loads

## Slide 40: River -> Lake - Output Selection