## Slide 1
Volatilization
Yanlai Han
09-20-2017

## Slide 2: Introduction
Volatilization process in WASP8
Programmed based on Two-Film Mass Transport Theory
Two driving forces for volatilization: Water flow and wind
Examples

## Slide 3: Two Films Theory

## Slide 4: Volatilization Theory
1. Volatilization process is expressed as
where KLA is mass transfer coefficient from water to air (d-1)
Cdiss is dissolved chemical concentration in aqueous (mg/L)
Cair is chemical concentration in air (mg/L)
Kaw is air-water partition coefficient (dimensionless).
2. Kaw is expressed as
where H is henry’s law constant (atm/M), R is ideal gas constant (atm/(M-K)), Tk
is temperature (K).

## Slide 5: Volatilization Theory
1. Volatilization process is expressed as
where KLA is mass transfer coefficient from water to air (d-1)
Cdiss is dissolved chemical concentration in aqueous (mg/L)
Cair is chemical concentration in air (mg/L)
Kaw is air-water partition coefficient (dimensionless).
2. Kaw is expressed as
where H is henry’s law constant (atm/M), R is ideal gas constant (atm/(M-K)), Tk
is temperature (K).

## Slide 6: Volatilization Theory
3. KLA is mass transfer coefficient from water to air (d-1)
]
where KL is the overall conductivity (m/d) at 20°C, and D is the depth of surface water,
θ is temperature correction coefficient, Tw is water temperature (°C).
4. The procedures to include temperature effects on volatilization is same as the ones for chemical reaction.

## Slide 7: Volatilization Theory
5. KL is determined by the conductivity in liquid film (KL_water) and in air film (KL_air), respectively.
Values of KL_water and KL_air are internally calculated by WASP8 based on the specific surface water systems.

## Slide 8: Volatilization Theory
WASP8 users only need to input parameters of the surface water system
WASP8 can internally compute volatilization process
Surface water system parameters include driving force for volatilization, surface water flow rate, surface water depth, water and air temperature.

## Slide 9: Volatilization Driving Force
Cair
Cdiss
Air
Water
Cair
Cdiss
Air
Water
Mass transfer can happen if there is mass difference between two phases
Cair
Cdiss
Air
Water
Water flow is driving force
This driving force applies to river and estuary
Wind is driving force
This driving force applies to lake and pond
Driving force 1
Driving force 2

## Slide 10: Volatilization Calculation Routines in WASP
When volatilization is driven by water flow, volatilization calculation routines are based on the values of water flow rate (v) and depth (D) that users input into the WASP8.
Routine 1: O’Connor-Dobbines Equation
Routine 2: Churchill Equation
Routine 3: Owens Equation

## Slide 11: Volatilization Driven by Water Flow

## Slide 12: Volatilization Calculation Routines in WASP
2. When volatilization is driven by wind, WASP8 has two options
Option 1: O’Connor Volatilization Equation (Default)
Option 2: MacKay Volatilization Equation

## Slide 13: Volatilization Example 1 – No Water Flow
Petrachloroethene (PCE) and trichloroethene (TCE) volatilization processes in a lake is driven by wind. In this example, don’t consider the chemical reaction.
Firstly users need to establish the simple lake model in WASP8. After creating lake model, users can create volatilization model.

## Slide 14: Result: Option 1 vs Option 2
Equation: ]
 | Wind = 5 m/s , water flow = 0 depth = 5 m |  | Wind = 15 m/s , water flow = 0 depth = 5 | 
 | Option 1 | Option 2 | Option 1 | Option 2
KL_water (m/d) | 0.77 | 0.66 | 2.30 | 5.14
KL_air (m/d) | 3781.57 | 32687.06 | 3781.57 | 32728.42
KL (m/d) | 0.77 | 0.66 | 2.30 | 5.14
KLA (d-1) | 0.15 | 0.13 | 0.46 | 1.02

## Slide 15: PCE Concentration in Pond When Wind = 5 m/s
Wind Option 1
Wind Option 2

## Slide 16: PCE Concentration in Pond When Wind = 15 m/s
Wind
Option 1
Wind Option 2

## Slide 17: Volatilization Summary
Choose driving force for volatilization (water flow or wind).
If driving force is water flow, WASP8 can choose right calculation routine based on the surface water system parameters that users input into WASP8.
When users input wind data into WASP8, WASP8 automatically considers wind influence on volatilization process.

## Slide 18: Example 1 – No Water Flow
Tetrachloroethene (PCE) and trichloroethene (TCE) volatilization processes in a simple lake is driven by wind. In this example, don’t consider the chemical reaction.
Firstly users need to establish the pond model in WASP8. After creating lake model, users can establish volatilization model.

## Slide 19: Create chemical state variables

## Slide 20: Create a simple lake

## Slide 21: Initial conditions for lake

## Slide 22: Lake geometry information

## Slide 23: Define boundary and flow (no flow condition)

## Slide 24: Input parameters for volatilization

## Slide 25: Input daily average wind speed in Time Function

## Slide 26: Turn on Time Function in Environmental Group

## Slide 27: PCE concentration in Pond (Option 1 vs 2)
Wind option 2
Wind option 1

## Slide 28: TCE concentration in Pond (Option 1 vs 2)
Wind option 2
Wind option 1

## Slide 29: Example 2 – Water Flow and Wind
This example shows how to build tetrachloroethene (PCE) and trichloroethene (TCE) volatilization processes in one river segment with water flows based on previous example.
Users need to add water flow based on previous model (v = 5 m/s).
Compare wind option 1 and 2 on volatilization results.