## Slide 1: WASP8 Nutrient Cycling Processes
Processes and Equations Implemented in WASP8 Eutrophication Module
Prepared by
Robert B. Ambrose, Jr.
Tim A. Wool
July, 2017

## Slide 2: Variables and Processes
Periphyton Biomass
D : C : N : P : Chl
IP
IN
Phytoplankton Biomass
Group 3
D : C : N : P : Si: Chl
DO
Group 2
D : C : N : P : Si: Chl
Group 1
D : C : N : P : Si : Chl
TIC
H2CO3 – HCO3- – CO32-
Total
Alkalinity
Particulate Detrital OM
Si
P
N
C
D
Dissolved OM
Si
P
N
CBOD1
CBOD2
CBOD3
Inorganic Nutrients
NO3
PO4
SiO2
NH4
pH
atmosphere
uptake
excretion
Inorganic Solids
S3
S1
S2
oxidation
oxidation
nitrification
photosynthesis and respiration
death
dissolution
mineralization
sorption
reaeration

## Slide 3: Equilibrium Reactions
Ionization
Sorption

## Slide 4: Phase Partitioning Equations
Dissolved fraction
Solid “k” fraction
n = porosity [Lw/L]

## Slide 5: Summary of Kinetic Constants Nutrient Sorption
Symbol | Kinetic Constant | Units | Value | Range
KSk,NH4 | Partition coefficient for NH4 onto solids “k” | L/kgS | 100 | 0 – 200
KSk,PO4 | Partition coefficient for PO4 onto solids “k” | L/kgS | 100 | 0 – 200
KSk,SiO4 | Partition coefficient for SiO4 onto solids “k” | L/kgS | 100 | 0 – 200

## Slide 6: Kinetic Reactions
Phosphorus and Silicon
Nitrogen
Growth/uptake
Respiration
Death
Dissolution
Mineralization
Settling
Growth/uptake
Respiration
Death
Dissolution
Mineralization
Nitrification
Denitrification
Settling

## Slide 7: Phosphorus Cycle
Phytoplankton
24, 25, 26
PO4
4
Detrital P
14
growth
death
Dissolved OP
5
respiration
dissolution
mineralization
settling
settling
respiration
settling

## Slide 8: Silicon Cycle
Phytoplankton
24, 25, 26
SiO4
6
Detrital Si
15
growth
death
Dissolved OSi
7
respiration
dissolution
mineralization
settling
settling
respiration
settling

## Slide 9: Nitrogen Cycle
settling
Phytoplankton
NO3
NH3
Detrital N
death
Dissolved ON
respiration
growth
denitrification
dissolution
mineralization
nitrification
settling
respiration
settling

## Slide 10: Summary of Kinetic Constants Nutrient Cycling
Symbol | Kinetic Constant | Units | Value | Range
kdiss | Detrital dissolution rate constant, 20C | 1/day | 0.1 | 0.01 – 0.2
kmin,x | Mineralization rate constants for organic P, N, Si | 1/day | 0.1 | 0.01 – 0.2
Kmpc | Algal half-saturation constant for mineralization | mgC/L | 0.025 | 0.01 – 0.5
knitr | Nitrification rate constant, 20C | 1/day | 0.1 | 0 – 0.4
Knit | Dissolved oxygen half-sat constant for nitrification | mgDO/L | 2 | 0 – 5
kdnit | Deitrification rate constant, 20C | 1/day | 0.1 | 0 – 0.4
KNO3 | Dissolved oxygen half-sat constant for denitrification | mgDO/L | 0.5 | 0 – 5
vs, vsdet | Solids and detrital settling velocities | m/day | 0.2 | 0 – 2
θx | Temperature correction factors |  | 1.07 | 1.04 – 1.1

## Slide 11: Summary - Phosphorus Cycle
Inorganic phosphorus
  DIP taken up by algae and used for growth
  DIP can sorb to solids and settle out
Organic phosphorus
  During algal respiration, a fraction of the cellular phosphorus is recycled to DIP
  The remaining fraction is recycled to the dissolved organic P
  Algal death transforms biomass P to detrital P
  Particulate detrital P may settle out at the same velocity as organic matter (vs3)
  Particulate detrital P dissolves to DOP
  DOP mineralizes to DIP

## Slide 12: Summary - Nitrogen Cycle
Inorganic nitrogen:
  Ammonia speciates between NH4+ and NH3
  Ammonium can sorb to solids and settle out
  Dissolved ammonium and nitrate N are taken up by algae and used for growth
    For physiological reasons ammonium is preferred
    The rate at which each form is taken up is proportional to its concentration relative to the total inorganic N (NH4+NO3) available
  Ammonium is nitrified to nitrate at a temperature and oxygen dependent rate
  Nitrate is denitrified to N2 gas at low DO levels at a temperature dependent rate

## Slide 13: Summary - Nitrogen Cycle
Organic nitrogen:
  During algal respiration, a fraction of the cellular nitrogen is recycled ammonia nitrogen
  The remaining fraction is recycled to the dissolved organic N
  Algal death transforms biomass N to detrital N
  Particulate detrital N may settle out at the same velocity as organic matter (vs3)
  Particulate detrital N dissolves to DON
  DON mineralizes to ammonia-N

## Slide 14: Appendix A: Summary of Equations by Kinetic Process

## Slide 15: Phytoplankton Growth

## Slide 16: Ammonia Preference Factor
kmN = 25 μg/L
NO3 , μg/L
PNH3

## Slide 17: Phytoplankton Respiration

## Slide 18: Phytoplankton Death

## Slide 19: Detrital Dissolution

## Slide 20: Organic Mineralization

## Slide 21: Additional Nitrogen Equations Nitrification and Denitrification

## Slide 22: Particulate Settling

## Slide 23: Appendix B: Summary of Equations by State Variable

## Slide 24: Phosphorus Equations
Phytoplankton “k” P
Detrital P
Settling
Death
Dissolution
Growth
Death
Settling
Respiration

## Slide 25: Phosphorus Equations
Mineralization
Dissolution
Respiration
Dissolved Organic P
Inorganic PO4
Settling
Mineralization
Growth
Respiration

## Slide 26: Nitrogen Equations organic components
Phytoplankton “k” N
Detrital N
Dissolved Organic N

## Slide 27: Nitrogen Equations inorganic components
NH4 N
Nitrification
Growth
Mineralization
Respiration
Settling

## Slide 28: Nitrogen Equations inorganic components
NO3 N
Denitrification
Nitrification
Growth

## Slide 29: Silicon Equations
Phytoplankton “k” Si
Detrital Si
Settling
Death
Dissolution
Growth
Death
Settling
Respiration

## Slide 30: Silicon Equations
Mineralization
Dissolution
Respiration
Dissolved Organic Si
Inorganic SiO4
Growth
Settling
Respiration
Mineralization