## Slide 1: Modeling Petroleum Mixtures in Surface Waters using WASP

## Slide 2: Example Problem: Leaking Crude Oil Tank
Crude Oil | Aliphatic | Aromatic | Asphaltic
Solvent Mix | 84 % | 13 % | 3 %
Sweden | 79 % | 18 % | 3 %
South Louisiana | 79 % | 17 % | 4 %
Lagomedio | 71 % | 23 % | 6 %
Prudhoe | 81 % | 17 % | 2 %
Mirando Humble | 68 % | 28 % | 4 %
AVERAGE | 77 % | 19 % | 4 %
From R. M. Atlas, 1975.

## Slide 3: Example Problem: Leaking Crude Oil Tank
Crude Oil | Aliphatic | Aromatic | Asphaltic
AVERAGE | 77 % | 19 % | 4 %
Assuming Aromatics are 30% PAHs and 70% BTEX
Crude Oil | Aliphatic | BTEX | PAHs
AVERAGE | 77 % | 13 % | 6 %

## Slide 4: Total Petroleum Hydrocarbon Working Group (TPHCWG) Hydrocarbon Fraction Approach
Group | Effective Carbon Number | Solubility1 [mg/L] | Henry’s Law1 Const [-] | Log(Koc) 1 | Biodegradation Rate Constant [per day]3 | Solid-Liquid Fugacity Ratio2
Aliphatics | >8 – 10 | 0.43 | 55 | 4.5 | 0.005 | 1
BTEX | >8 – 10 | 25 | 0.86 | 3.2 | 0.1 | 0.942
PAHs | >12 - 16 | 5.8 | 0.028 | 3.7 | 0.05 | 0.37
1 Gustafson et al, 1997. From the TPHCWG Series, Vol. 3
2 Brown et al, 1999.
3 Layton, et al., 1999 and Environmental Science Center, 1999.

## Slide 5: TPHCWG Hydrocarbon Fractions
Group | Approx. Mole Fraction [xi] | Aqueous Solubility [Si, mg/L] | Solid-Liquid Fugacity Ratio | Aqueous Concentration [Ci, mg/L]
Aliphatics | 0.77 | 0.43 | 1 | 0.33
BTEX | 0.13 | 25 | 0.942 | 3.5
PAHs | 0.06 | 5.8 | 0.37 | 0.94

## Slide 6: Compiled Crude Oil Parameters
WASP Chemical | Group | Henry’s Law Const [atm-m3/mol] | Log(Koc) | Biodegradation Rate Constant [per day] | Aqueous Conc [Ci, mg/L]
Chemical 1 | Aliphatics | 1.88 | 4.5 | 0.005 | 0.33
Chemical 2 | BTEX | 9.01E-3 | 3.2 | 0.1 | 3.5
Chemical 3 | PAHs | 1.51E-3 | 3.7 | 0.05 | 0.94