## Slide 1: Sediment Transport 1: Introduction
Theory and Implementation in WASP8

## Slide 2: TSS - Total Suspended Solids in [mg/L]
Measures combined particulate inorganic and organic material retained by a filter
Related to turbidity, but site-specific correlation is necessary
Typical concentrations [mg/L]1
  Lake Superior/Huron: 0.5
  Flint River, MI: 8 – 12
  Hudson River, NY: 10 – 60
  Rapid Creek, SD: 158
  Sacramento-San Joaquin Delta, CA: 50 - 175
1Chapra, Surface Water Quality Modeling

## Slide 3: Particle Size Classification
Size Range | Wentworth Name | Other Names
< 1 μm | colloid | mud
1.0 – 3.9 μm | clay | mud
3.9 – 62.5 μm | silt | mud
62.5 - 125 μm | very fine sand | sand
125 - 250 μm | fine sand | sand
0.25 – 0.5 mm | medium sand | sand
0.5 – 1 mm | coarse sand | sand
1 – 2 mm | very coarse sand | sand
2 – 4 mm | granule | gravel
4 – 64 mm | pebble | gravel
64 – 256 mm | cobble | gravel
> 256 mm | boulder | gravel

## Slide 4: Particle Densities
Substance | Density [g/mL]
Organic matter (dry weight) | 1.27
Siliceous minerals | 2.65
Garnet sands | 4

## Slide 5
Sorption reduces dissolved NH4 and PO4
  Reduction in nitrification
  Reduction in algal uptake and growth
Deposition removes NH4 and PO4 from water
Sediment flux returns NH4 and PO4 to water
Solids increase light attenuation
  Reduction in algal growth
Solids Effects on Water Quality

## Slide 6
Sorption reduces dissolved fraction and bioavailability
Deposition removes some peak loading from water
Pore water diffusion, resuspension return chemical to water column between loading events
Large flood events scour significant amounts of sediment and chemical from the upper sediment to the water column
Net deposition stores chemical in sediments for long periods
Burial below bioturbation depth potentially sequesters chemical from biota
Solids Effects on Toxicants

## Slide 7
Harm fish directly:
  Direct mortality
  Reducing growth rate, resistance to disease, etc.
Prevent the successful development of fish eggs and larvae
  Silts blanket bottom spawning areas and damage invertebrates
  Organic deposits reduce dissolved oxygen and imbalance natural biota
Modify natural movements and migrations of fish
Reduce the abundance of food available to the fish
  Reduce light penetration and extent of photic zone
  Increase surface heating
Biotic Effects of Excess Solids

## Slide 8: Criteria for Freshwater Fish and Other Aquatic Life
Gold Book:
  Settleable and suspended solids should not reduce the depth of the compensation point for photosynthetic activity by more than 10% from the seasonally established norm for aquatic life.

## Slide 9: State Aquatic Life Criteria
Most have numeric turbidity criteria
Most have narrative criteria
Numeric TSS criteria:
  HA: 10 mg/L (mean), 30 mg/L (<10%), 55 mg/L (<2%)
  NJ: 25 mg/L (no averaging period specified)
  SD: 30/90 mg/L for cold/warm waters (30 day mean)
  53/158 mg/L for cold/warm waters (daily max)
  ND: 30 mg/L (30-day mean)
  Utah: 35/90 mg/L for cold/warm waters (30-day)

## Slide 10: Some Technical Issues
Spatial heterogeneity
  Riffles, pools, impoundments, wetlands
  Water column, sediment, stream bank, floodplain
  Patchiness in aquatic vegetation, deposition zones
Temporal variability
  Runoff flow, base flow, drought flow
Variability in sediment properties
  Gravel, sand, silt, particulate organic matter, DOM
Availability of input data
  Meteorology, sediment properties, stream morphometry
  Input flow and erosion data from watershed models

## Slide 11: WASP Solids Variables
Eutrophication Module
Phytoplankton solids
  Multiple algal classes
Detrital solids
Inorganic Solids
  Multiple size classes
Cobble
Notes:
Up to 10 solids classes can be simulated
All solids variables are in mg/L dry weight.
Cobble is specified for benthic segments only.
Cobble Is immobile, but can be buried.
Toxicant Module
Inorganic Solids, e.g.:
  Coarse sand
  Fine sand
  Coarse silt
  Fine silt
  Clay
POM
Cobble

## Slide 12: WASP Solids Processes
Kinetic Transformation Processes
  Production of biomass
  Respiration and death
  Dissolution of detritus
Transport Processes
  Settling and deposition
  Scour (entrainment, resuspension)
  Bed load
  Burial

## Slide 13: Solids Kinetics in Eutrophication Module
Settling
Dissolution
Phytoplankton
Growth
Detritus
Respiration
Death
Periphyton
Growth
Death
Respiration
Settling
Inorganic Solids
Settling

## Slide 14: Solids Kinetics in Toxicant Module
Production
Inorganic Fines
Biotic Solids (POM)
Dissolution
(1-fash)
(fash)
Net Biotic
Settling
Settling
Sands
Settling

## Slide 15: Basic Solids Transport Data
Systems
  Solid variable and name
  Particle density, g dw/mL (defaults to 2.65)
Constants
  Solids option (0 – descriptive; 1 & 2 – mechanistic)
  Particle diameter [mm]
Parameters
  Settling velocity [m/day]
  Resuspension velocity [m/day]
  Sediment cobble concentration [mg/L]

## Slide 16: Biotic Solids Kinetic Data
Constants
  Solid Production Temperature Correction Factor (theta)
  Ash Dry Weight Residue [Fraction]
  Residue Solid Identification Number
  Organic Carbon Fraction [dimensionless]
  Dissolution Product DOC Identification Number
Parameters
  Biotic solids production rate [g/m3-day]
  Biotic solids dissolution rate [1/day]
Time Functions
  Biotic solids production rate multiplier
  Biotic solids dissolution rate multiplier

## Slide 17: Alternate Input of Biotic Solids Data - Water Quality Transfer File
Produced by Eutrophication module run
  WQTransfer-Eutr.wqm
  Located in same project folder
Contains daily average net production and dissolution rates by segment
Solids are re-simulated using specified transport parameters along with rate constants.

## Slide 18: Benthic Parameter Equations
Bulk Density [g/mL]
Dry Density [gS/mL]
Percent Water [g/gS]
Where:
n = porosity [LW/L]
ρS = particle density, about 2.7 [gS/mLS]
ρW = water density, about 1.0 [gW/mLW]
sediment fresh weight / sediment volume
sediment dry weight / sediment volume
sediment fresh weight / sediment dry weight

## Slide 19: Benthic Parameter Values
n | ρD | ρB | %water
0.1 | 2.43 | 2.53 | 104
0.2 | 2.16 | 2.36 | 109
0.3 | 1.89 | 2.19 | 116
0.4 | 1.62 | 2.02 | 125
0.5 | 1.35 | 1.85 | 137
0.6 | 1.08 | 1.68 | 156
0.7 | 0.81 | 1.51 | 186
0.8 | 0.54 | 1.34 | 248
0.9 | 0.27 | 1.17 | 433
0.95 | 0.135 | 1.085 | 804
0.99 | 0.027 | 1.017 | 3767

## Slide 20: Sediment Transport Processes
Burial
Biotic production
Dissolution