## Slide 1: Advective Flows

## Slide 2: Transport Flow Fields
Surface Water - Water column flows carry both dissolved and particulate material
Pore Water - Pore water flows carry dissolved material only
Solids 1, 2, 3 – Solids “i” flows (e.g., settling or resuspension) carry particulate material only (Legacy Option)
Evaporation/Precipitation – Evaporation and precipitation adjust surface water volume only

## Slide 3: Surface Water Flow Options
Calculated stream network flows
  Flow routing (steady specified flow reaches)
  Stream routing (unsteady specified flow reaches)
  Kinematic wave (free-flowing reaches)
  Ponded weir (weir overflow reaches)
  1-D Lake Transport (stratified water column)
  Dynamic flow (backwater reaches)
  Internal transfer flows (e.g., dam withdrawals)
Calculated flows from external hydrodynamic model

## Slide 4: Calculated Surface Flow Options
WASP internally calculates flows, volumes, depths, widths in:
free-flowing reaches (kinematic wave eq.), ponded reaches (weir overflow eq.), and backwater reaches (dynamic flow eq’s.)
Free-flowing main stream segments
Free-flowing tributary segment
Ponded tributary segment, e.g., riparian wetland with sill
Ponded segment, e.g., pool behind low head dam with spillover and/or specified withdrawals.
Backwater segment

## Slide 5: Flow Routing Reaches
Uses specified flow for each segment; volume, depth, and velocity are not adjusted with flow
Pertains to mass and water being moved without regard to net flow
Used for cases with steady flow

## Slide 6: Stream Routing Reaches
Uses specified flow for each segment; volume, depth, and velocity are adjusted for variable flow based on hydrogeometry
Default rectangular channel shape unless user specifies hydraulic coefficients

## Slide 7: Kinematic Wave Reaches
Calculates flow wave propagation and resulting variable flows, volumes, depths, and velocities throughout the network
Default rectangular channel shape unless user specifies hydraulic coefficients
Uses Manning’s equation

## Slide 8: Kinematic Wave Equations
Continuity equation (mass balance):
Momentum equation (momentum balance):
gravity
friction

## Slide 9: Kinematic Wave Equations
Substitute in Manning’s equation:
Kinematic wave differential equation:

## Slide 10: Kinematic Wave Input Data
Time-variable upstream and tributary inflows (m3/sec)
Continuity flow paths for main stem and each tributary (IQ, JQ, BQ)
Channel properties:
  length (m), mean-flow width (m), depth (m), vel (m/s)
  hydraulic exponents: set to 0 for velocity; options for depth:
    0 or 0.6: rectangular channel
    0.3 to 0.55: variable width
  minimum depth (m)
    residual depth when flow is 0
    0.001 to 0.1 (m)
  bottom slope (m/m)
  Manning’s roughness coefficient

## Slide 11: Kinematic Wave Dynamic Response Profiles
Chapra Kinematic Wave, Example 14.6 |  | 
Channel Width, "B", m | Channel Bottom Slope, "S", m/m | Manning's Roughness Coefficient, "n"
15 | 0.004 | 0.07
Boundary Pulse Flow Period, day | Boundary Pulse Flow Range, m3/sec | Duration of Boundary Pulse, day
0.5 | 2.5 | 0.25
Spatial Step, dx, m | Time Step, dt, day | 
1000 | 0.007 | 

## Slide 12: Kinematic Wave Response to Stepwise Flows
Small Stream, Gentle Slope |  |  | 
Segment Lengths m | Channel Width m | Channel Bottom Slope m/m | Manning's Roughness Coefficient
1000 | 2 | 0.0001 | 0.04

## Slide 13: Ponded Reaches
Calculates flow over top of low dam or weir
Uses sharp crested weir overflow equation
Specify height of weir or sill from segment bottom
Residual depth is set to 0.001 m

## Slide 14: Ponded Segments
For weir, specify weir or sill height, Hw
Set segment width to weir/sill width, Bw
Bottom slope < 10-6
Weir height, Hw
Overflow height, Hh
Pool depth, H
Outflow differential equation:
Qin

## Slide 15: Wetland Reach: Hydrology
Qin
Hh
Hw
H
E
Qstream
Hw
Qin
H
E
Qstream
Wet conditions: overflow over sill:
Dry conditions: no outflow:

## Slide 16: 1-D Lake Transport
Lake Module subdivides a lake or reservoir into a series of vertical layers
The physical characteristics of the lake or reservoir are a function of depth are described using a relationship between water surface elevation and the volume and surface area.
Changes in volume are computed from continuity based on a time series of inflows and outflows, and water temperatures computed based on a heat balance (Evaporation)
Inflows – Specified
Outflows - Controlled by ports, weirs and outflow timeseries
Heat Balance – Calculated by the WASP Water Temperature Routine
Water Quality – Both the Eutrophication and Toxicant can be used with Lake Module

## Slide 17: 1-D Lake Transport
Convective mixing due to density instabilities
Wind Driven Mixing
Distribution of inflowing waters at depths with comparable density and distributed as impacted by kinetic energy.
Withdrawal of outflowing waters from depths influenced by the outlet structure, discharge rate, and density stratification.

## Slide 18: Lake Module – Layer Definition

## Slide 19: Lake Module – Stage vs. Volume, Surface Area
Calculates Volume and Surface Area as a function changes in depth

## Slide 20: Lake Module – Weir Outflow
Fixed Height Weir
Submerged Weir enter timeseries of Ouflow

## Slide 21: Lake Module – Port Outflows
Defined Port – Elevation & Dimensions
Timeseries of Port Outflow

## Slide 22: Lake Module – Layer Parameters

## Slide 23: Lake Module – Layer Initial Conditions

## Slide 24: Lake Module – Output Options

## Slide 25: 1-D Lake Transport

## Slide 26: 1-D Lake Transport

## Slide 27: Dynamic Flow Reaches
Used for backwater flow reaches
Dynamic flow equations (1-D continuity and momentum)
Specify the bottom elevation and initial surface elevation
Residual depth is set to 0.001 m

## Slide 28: Dynamic Flow Option
Flow Calculation based on:
  Water Surface Elevation/Slope
  Bottom Slope
  Uses Downstream Water Surface Elevation
    Within Model Network
    Downstream Boundary
Unlike Kinematic Wave
  Need Consistent Vertical Datum

## Slide 29: Calculated Surface Flow Options
WASP internally calculates flows, volumes, depths, widths in:
free-flowing reaches (kinematic wave eq.), ponded reaches (weir overflow eq.), and backwater reaches (dynamic flow eq’s.)
Free-flowing main stream segments
Free-flowing tributary segment
Ponded tributary segment, e.g., riparian wetland with sill
Ponded segment, e.g., pool behind low head dam with spillover and/or specified withdrawals.
Backwater segment

## Slide 30: Dynamic Flow
Surface Elevation
Freshwater Flow
Vertical Datum
Bottom
Elevation

## Slide 31: Dynamic Flow
Freshwater Flow
Vertical Datum
Mean Sea Level
Surface Elevation
Bottom
Elevation

## Slide 32
Hydraulic Geometry
Channel | Velocity | Depth | Width
1. Rectangular | 0.40 | 0.60 | 0.00
2. U-Shape | 0.32 | 0.48 | 0.20
3. V-Shape | 0.26 | 0.39 | 0.35
4. Shallow | 0.20 | 0.30 | 0.50
Width = bmult * Q bexp
Depth = dmult * Q dxp
Velocity = vmult * Q vexp
Equations:
Hydraulic Exponents

## Slide 33
Hydraulic Geometry
Rectangular Channel
Width = constant
Depth = dmult * Q 0.6
Velocity = vmult * Q 0.4
Width = bmult * Q 0.4
Depth = dmult * Q 0.36
Velocity = vmult * Q 0.24
Semi Arid Channel
0.00
5.00
10.00
15.00
20.00
25.00
-50
-40
-30
-20
-10
0
10
20
30
40
50
Channel Cross Section
0.00
5.00
10.00
15.00
20.00
25.00
-50
-40
-30
-20
-10
0
10
20
30
40
50
Width, m
Depth, m
Width, m
0.00
2.00
4.00
6.00
8.00
10.00
12.00
14.00
-50
-40
-30
-20
-10
0
10
20
30
40
50
Channel Cross Section
Depth, m
0.00
1.00
2.00
3.00
4.00
5.00
6.00
7.00
8.00
9.00
10.00
-50
-40
-30
-20
-10
0
10
20
30
40
50
Channel Cross Section
0.00
1.00
2.00
3.00
4.00
5.00
6.00
7.00
8.00
9.00
10.00
-50
-40
-30
-20
-10
0
10
20
30
40
50
Width, m
Depth, m
Eastern Channel
Width = bmult * Q 0.25
Depth = dmult * Q0.45
Velocity = vmult * Q 0.3
Eastern Channel

## Slide 34: Specified Withdrawals (transfer flows)
Specified internal transfer flows (e.g., dam withdrawals )use a separate flow function
A single flow pathway is specified from segment “j” to “i”
The flow time function transfers water from segment “j” to “i”
Overflow will still occur if pond depth exceeds weir height
Segment “j”
Qin
Specified withdrawal flow
Segment “i”

## Slide 35: Surface Water Flow Options – WASP Screen

## Slide 36: Transport Fields – WASP Screen

## Slide 37: WASP Transport Scheme
Each Flow Field can have multiple flow patterns and time functions.
WASP sums the individual flows for each segment to determine overall transport

## Slide 38: Flow Boundary Forcing Types – WASP Screen
Flow
Water Surface Elevation
Internal Flow
Water Withdrawal
Weir Outflow

## Slide 39: Flow Boundary Forcing Types – WASP Screen
Flow – Conventional 1-Dimesional Flow
Water Surface Elevation – Measured Water Surface Elevation to be used as boundary forcing for Dynamic Flow Transport Option
Internal Flow – Time Series of Transfer of Flow from One Segment to Another
Water Withdrawal – Remove Water and Constituents from Segment.
Weir Outflow – Specify Outflow from Weir or Dam

## Slide 40: Flow Patterns – WASP Screen

## Slide 41: Flow Time Functions – WASP Screen

## Slide 42: Examples of Specifying Flows

## Slide 43: Flow through Simple Pond
0
1
0
Flow Time Function
Time, days
Flow Path
Continuity Function

## Slide 44: Upstream Flow Through River
1
2
3
4
5
6
0
0
Flow Time Function
Time, days
Flow Path
Continuity Function

## Slide 45: Flow through River with Tributary
Flow Path
Continuity Functions
Chart: 
| Jan | Feb | Mar | April | May | Jun | Jul | Aug | Sept | Oct | Nov | Dec
Flow | 10 | 15 | 120 | 180 | 70 | 85 | 60 | 45 | 20 | 110 | 155 | 95
Flow | 8 | 22 | 95 | 140 | 60 | 74 | 25 | 10 | 5 | 55 | 65 | 41
Flow Time Function
1
2
3
4
5
6
0
0
7
0

## Slide 46: Flow through River with Withdrawal
Flow Path
Continuity Functions
Flow Time Function
Time, days
1
2
3
4
5
6
0
0
0

## Slide 47: Branched Flow through River
1
7
6
3
2
4
5
0
0
Flow Time Function
Flow Path Continuity Function

## Slide 48: Hydrodynamic Linkage to WASP

## Slide 49: Hydrodynamic Linkage
Provides detailed flow, depth, volume and velocities to WASP at every timestep for every segment.

## Slide 50: When to use Hydrodynamic Model
High gradients
  For 1-dimensional, branching systems, use internal kinematic wave option
Accurate calculation of travel times under dynamic flow conditions
Where depth & velocity calculations are important for reaeration

## Slide 51: Why EFDC Hydrodynamic Simulation?
To drive the WASP water quality model

## Slide 52: Description of EFDC
Development History
Capabilities
Hydrodynamic module
Applications
Example Application
Linkage file to WASP

## Slide 53: ENVIRONMENTAL FLUID DYNAMICS CODE
EFDC is a public domain surface water modeling system incorporating fully integrated hydrodynamics
EFDC is extremely versatile, and can be used for 1D, 2DV, 2DH, or 3D simulations of rivers, lakes, reservoirs, estuaries, coastal seas, and wetlands

## Slide 54: EFDC Development History
Developed by John Hamrick at Virginia Institute of Marine Science (VIMS) with primary support from the State of Virginia
Additional support has been provided by
EPA and NOAA
Presently maintained by Tetra Tech, Inc.
Currently used by federal, state and local agencies, consultants and universities

## Slide 55: EFDC Capabilities
Three-Dimensional hydrodynamics with coupled salinity, temperature, sediment and contaminant transport modules
Simulates wetting & drying of flood plains, mud flats, and tidal marshes
Integrated near-field mixing zone model
Simulates hydraulic control structures such as dams and culverts
Simulates wave boundary layers and wave-induced currents

## Slide 56: EFDC Hydrodynamic Module
Fully 3D, with 2DV, 2DH and 1D options
Boundary fitted curvilinear-orthogonal grid or
Cartesian grid can be used
Includes turbulence closure model
Highly efficient finite difference semi-implicit solution
Functionally similar to POM/ECOM and CH3D-WES

## Slide 57: Example EFDC Applications
Rivers – Flint (AL), Housatonic (MA), Chattahoochee (GA), Los Angeles (CA)
Lakes - Lake Okeechobee (FL), Lake Jordan (NC), Coosa River Reservoirs (AL), Lake Allatoona (GA), Hartwell Reservoir (GA/SC)
Estuaries - Mobile Bay (AL), Neuse River (NC), Savannah River/Harbor (GA), Charleston Harbor (SC), St Johns River (FL), Lower Duwamish Waterway (WA)
Lagoons – Curonian Lagoon (Lithuania)

## Slide 58: Neuse River Network plan view

## Slide 59: Neuse Bathymetry