## Slide 1: WASP8 MacroAlgal Processes
Processes and Equations Implemented in WASP8 Advanced Eutrophication Module
Prepared by
James L. Martin
July, 2016

## Slide 2: Forms of Interest: Surface floating, Submersed Floating Autotrophs, Submersed Canopy Forming, and Benthic (mat forming) which may include some microalgae, macroalgae and macrophytes (attached but not root forming)
macroalgae on tidal flats
floating macroalgae in a closed lagoon
seagrass
Ruppia
sp., a type of brackish water
SAV

## Slide 3: Macroalgae in WASP8
 |  | Macroalgae |  |  | 
 | Phytoplankton | Surface Floating | Floating | Submersed | Benthic Algae
Transport | With ambient flow | Reduced transport with drag against flow | Reduced transport with drag against flow | Stationary on benthic substrate, but subject to scour | Stationary on benthic substrate
2. Nutrient uptake | From the water column | From the water column with luxury uptake | From the water column with luxury uptake | From the water column with luxury uptake | From the water column with luxury uptake
3. Light uptake | Throughout water column with self-shading | Light at the top of the water surface | Throughout water column with self-shading | Light reaching the top of canopy, followed by self shading | Light reaching the bottom
4. Biomass measure | Carbon and/or Chlorophyll-a | g DW/m2 | g DW/m2 | g DW/m2 | g DW/m2
Phytoplankton
Benthic Algae
Subsurface Floating
Macroalgae
canopy height
S
ubmersed Macroalgae
Surface Floating Macroalgae

## Slide 4: Variables and Processes
Periphyton Biomass
D : C : N : P : Chl
qP
qN
Phytoplankton Biomass
Group 3
D : C : N : P : Si: Chl
DO
Group 2
D : C : N : P : Si: Chl
Group 1
D : C : N : P : Si : Chl
TIC
H2CO3 – HCO3- – CO32-
Total
Alkalinity
Particulate Detrital OM
Si
P
N
C
D
Dissolved OM
Si
P
N
CBOD1
CBOD2
CBOD3
Inorganic Nutrients
NO3
PO4
SiO2
NH4
pH
atmosphere
uptake
excretion
Inorganic Solids
S3
S1
S2
oxidation
oxidation
nitrification
photosynthesis and respiration
death
dissolution
mineralization
sorption
reaeration
MacroAlgal Biomass
D : C : N : P : Chl
qP
qN
death

## Slide 5: Macro Algae Biomass Nutrient Ratios
Total Dry Weight
aMA [gD/m2]
Biomass composition D : C : N : P : Chl
Total
cell N
qN
[mgN/gD]
Total
cell P
qP
[mgP/gD]
Symbol | Kinetic Constant | Units |  | 
ADC | detritus to carbon ratio | gD/gC |  | 
ANC | nitrogen to carbon ratio | gN/gC |  | 
APC | phosphorus to carbon ratio | gP/gC |  | 
AChlC | chlorophyll to carbon ratio | gChl/gC |  | 
ROC | oxygen to carbon ratio | gO2/gC |  | 
Input nutrient ratio constants describe structural biomass. Variables qN and qP are total cell nitrogen and phosphorus content, including biomass and stored inorganic N and P.
Notes: qP and qN are total internal P and N, including inorganic and organic fractions. The biomass ratios are for organic D, C, N, P, and Chl. The fractions fopb and fonb are calculated internally from simulated qN and qP along with input ADC, ANC, APC.

## Slide 6: Macro Algae Kinetic Processes
Light
Temperature
PO4
NO3
NH4
Detrital
C,N,P
DON, DOP
aMA [gD/m2]
biomass
D : C :
N : P : Chl
qN
mgN/gD
qP
mgP/gD
FDb
FEP,MA
FG,MA
FR,MA
FUP,MA
FEN,MA
FUN,MA
fop,MA
fon,MA
1-fop,MA
1-fon,MA
Carrying
Capacity
Notes: qP and qN are total internal P and N, including inorganic and organic fractions. The biomass ratios are for organic D, C, N, P, and Chl. The fractions fopb and fonb are calculated internally from simulated qN and qP along with input ADC, ANC, APC.

## Slide 7: Macro Algae Biomass Kinetic Equation
Where, for macro algae in segment i: | 
aMA = | Macro algal density (gD/m2)
FG,MA = | growth rate (gD/m2-day)
FR,MA = | respiration rate (gD/m2-day)
FD,MA = | death rate (gD/m2-day)
AMA = | bottom substrate surface area (m2, benthic and submersed forms)
MacroAlgal Biomass, aMA
gD/m2
D : C : N : P : Chl
qN
mgN/gD
qP
mgP/gD

## Slide 8: Macro Algae Biomass Minimum Concentration
Macro Algal Seed or Minimum Concentration | 
aMA = | Macro algal density (gD/m2)>= Specified Seed Concentration (= 0 if not specified)

## Slide 9: Macro Algal Growth, option 0
Zero-order growth rate (gD/m2-day):
Where, for macro algae in segment i: | 
FG,MA20 | = maximum growth rate at 20 oC, gD/m2-day
ΦT,MA = | temperature growth multiplier
ΦL,MA = | light growth multiplier
ΦN,MA = | nutrient growth multiplier
ΦN,MA = | Salinity multiplier for salt or backish water species

## Slide 10: Macro Algal Growth, option 1
First-order growth rate (gD/m2-day):
Where, for macro algae in segment i: | 
kG,MA20 | maximum growth rate constant at 20 C, 1/day
ΦT,MA = | temperature growth multiplier
ΦL,MA = | light growth multiplier
ΦN,MA = | nutrient growth multiplier
ΦS,MA = | space growth multiplier

## Slide 11: Standard Temperature Function for Macro Algal Growth
Temperature multiplier:
Where, for macro algae in segment i: | 
θG,MA = | temperature correction factor for growth (1.07, 1.05 – 1.1)
T = | water temperature, C

## Slide 12: Optimal Temperature Function for Macro Algal Growth
Temperature multiplier:
Where, for macro algae in segment i: | 
θT,MA = | temperature correction factor for
T = | water temperature, C
Topt= | the optimal temperature
Κ1, κ2 = | shape parameters

## Slide 13: Comparison of Temperature Functions
TF1 = | exponential temperature function, θG = 1.08
TF2a = | Topt temperature function: κ1, κ2 = 0.02
TF2b = | Topt temperature function: κ1, κ2 = 0.002

## Slide 14: Light Limitation of Macro Algal Growth
Steele light limitation function:
Where, for total light energy (values are half for photosynthetically active radiation, PAR): | 
It,z = | light intensity at time t and depth z, Ly/day
ISi = | saturating light intensity for macro algae, Ly/day

## Slide 15: Light Limitation of Macro Algal Growth: Surface or Bottom
Steele light limitation function:
Where, for total light energy (values are half for photosynthetically active radiation, PAR): | 
It,z = | PAR light intensity (Ly/day) at time t and depth z = 0 for surface, = canopy height for submersed = bottom depth for benthic forms, Ly/day
ISi = | saturating light intensity for macro algae, Ly/day

## Slide 16: Light Limitation Function Depth Integrated: Subsurface Floating
Steele function integrated over depth:
Where: | 
H = | segment depth, m
Ke = | segment light extinction coefficient , 1/m
I0 = | light intensity at top of segment, Ly/day
ISi = | saturating light intensity for phytoplankton “i”, Ly/day Note for canopy formers, light is integrated over the canopy height

## Slide 17: Light Limitation Function Depth Integrated – Time Averaged
Steele function integrated over depth and averaged over day:
Where: | 
H = | segment depth, m
Ke = | segment light extinction coefficient , 1/m
I0 = | light intensity at top of segment, Ly/day
ISi = | saturating light intensity for phytoplankton “i”, Ly/day
fday= | daylight fraction Note for canopy formers, light is integrated over the canopy height

## Slide 18: Light
Beer-Lambert law,
where Io is the light at the water surface, for a surface water segment, or the light at the top of the segment for sub-surface water segments, ke is the light extinction coefficient (1/m) and and z is the depth of the segment (m).
Fraction of total radiation
Depth

## Slide 19: Light Extinction
where , ke,P is a model parameter and time function to which the impact of phytoplankton and macroalgal self-shading may be added based on the computed chlorophyll concentration or macroalgal biomass/depth and user specified multipliers (Mchl) and exponents (Exp,chl)
Alternatively, the extinction coefficient is based on an input background coefficient (Ke,b)to which the impacts of attenuation due to DOC, inorganic suspended solids (ISS) phytoplankton chlorophyll and macroalgae/depth are added based on computed concentrations and user-specified coefficients.
A=area (m2) and V=volume (m3)

## Slide 20: Submersed Macroalgae
Example case for segment with canopy height intermediate within segment with macroalgal self shading only applied to Z2,2
Based on Specified canopy height
canopy
height
Segment 1
Segment 2
depth to
canopy
height
Segment 3
Z
3
Z
2,1
Z
2,2
Z
1

## Slide 21: Nutrient Limitation of Macro Algal Growth
Where, for macro algae in segment i: | 
q0N = | minimum N cell quota supporting growth, mgN/gD (7, 4 – 20)
q0P = | minimum P cell quota supporting growth, mgP/gD (1, 0.5 – 5)

## Slide 22: Space Limitation of Macro Algal Growth
Where, for macro algae in segment i (Madden and Kemp 1996): | 
aMA,max = | maximum carrying capacity, gD/m2
 | (used in first-order growth equation)

## Slide 23: Salinity Limitation on Macro Algal Growth (Brackish or salt water forms)
Where, for macro algae in segment i: | 
θSAL,MA = | temperature correction factor for
S = | Salinity (parts per thousand)
Sopt= | the optimal salinity
Κ1, κ2 = | shape parameters

## Slide 24: Macro Algal Attenuation
Where, for macro algae in segment i: | 
aMA = | macro algal density (gD/m2)
FR,MA = | respiration rate (gD/m2-day)
FD,MA = | death rate (gD/m2-day)
Ab = | bottom substrate surface area (m2)
MacroAlgalBiomass, aMA
gD/m2
D : C : N : P : Chl
qN
mgN/gD
qP
mgP/gD

## Slide 25: Macro Algal Respiration
First order respiration:
Where, for macro algae in segment i: | 
kR,MA20 = | respiration rate constant at 20 C, 1/day
θR,MA = | temperature correction factor for respiration

## Slide 26: Macro Algal Death
First order death rates:
Where, for macro algae in segment i: | 
kD,MA20 = | death rate constant at 20 C, 1/day
θD,MA = | temperature correction factor for respiration
Kd,salMA= | Salinity dependent death rate for fresh-water species (1/day)
S, Ks= | Salinity (parts per thousand) and salinity at which death is ½ maximum
KGR,MA= | First-order grazing coefficient (not implemented)

## Slide 27: Macro Algae Nutrient Kinetic Equations
MaroAlgal Biomass, aMA
gD/m2
D : C : N : P : Chl
qN
mgN/gD
qP
mgP/gD
Where, for macro algae in segment i: | 
qN, qP = | algal cell N, P (mgN/gD, mgP/gD)
FUN,MA , FUP,MA = | uptake rates (gN/m2-day, gP/m2-day)
FEN,MA , FEP,MA = | excretion rates (gN/m2-day, gP/m2-day)
FDN,MA , FDP,MA = | death rates (gN/m2-day, gP/m2-day)
aMA = | algal biomass density (gD/m2)

## Slide 28: Macro Algal Nitrogen Uptake
Where: | 
ρmN | = maximum N uptake rate (mgN/gD-day)
KsNb | = external N half-saturation constant for uptake (mgN/L)
KqN q0N | = internal N half-saturation constant for uptake (mgN/gD) = minimum N cell quota supporting growth (mgN/gD)
aMA | = algal biomass (gD/m2)
qN
NO3
NH4

## Slide 29: Macro Algal Ammonia Preference Factor
PNH4,MA
qN
NO3
NH4
1 – PNH4,MA
Where: | 
Khnx,MA | = ammonia preference factor, mgN/L
DIN = NH4 + NO3
for Khnx,MA >> DIN PNH4,MA = NH4 / DIN
for Khnx,MA = NH4 = NO3 PHN4b = 0.5
for Khnx,MA = 0 PNH4b = 1
for NO3 = 0 PNH4,MA = 1
for NH4 = 0 PNH4,MA = 0

## Slide 30: Macro Algal Phosphorus Uptake
Where: | 
ρmP | = maximum P uptake rate (mgP/gD-day)
KsP,MA | = external P half-saturation constant for uptake (mgP/L)
KqP q0P | = internal P half-saturation constant for uptake (mgP/gD) = minimum P cell quota supporting growth (mgP/gD)
aMA | = algal biomass (gD/m2)
qP
PO4

## Slide 31: Macro Algal Nutrient Excretion
Where: | 
kE,MA20 | = nutrient excretion rate constant at 20 C, 1/day (0.05, 0.02 – 0.1)
θE,MA20 | = temperature correction factor for excretion (1.07, 1.05 – 1.08)
fON,MA fOP,MA | = organic fraction of excreted N = organic fraction of excreted P
aMA | = algal biomass (gD/m2)
qN, qP
PO4
NH4
DON, DOP,
CBODi
fOP,MA
fON,MA
1-fOP,MA
1-fON,MA

## Slide 32: Macro Algal Nutrient Loss with Death
Where: | 
FD,MA | = death rate, gD/m2-day (0.05, 0.01 – 0.5)
fON,MA fOP,MA | = organic fraction of algal N = organic fraction of algal P
qN, qP
PO4
NH4
Detrital
N, P
fOP,MA
fON,MA
1-fOP,MA
1-fON,MA

## Slide 33: WASP 8 Implementation

## Slide 34: WASP 8 Implementation
Select systems
Can simulate up to three forms of macroalage
Each consisting of MALGA (macroalage), MALGN (internal N) and MALGP (internal P)

## Slide 35: WASP 8 Implementation
Select parameters and time functions
The single parameter for macroalage specifies the fraction (0-1) of each segment that provides an adequate substrate for the growth of macroalgae (only applicable for submersed or benthic forms).
Other applicable parameters and time functions deal with light and temperature

## Slide 36: WASP 8 Implementation
Set boundary conditions (only applicable for surface end submerged forms that can be transported)

## Slide 37: WASP 8 Implementation
Set constants (value and default reflect typical values, see manual)

## Slide 38: WASP 8 Implementation
Select output variables under output control

## Slide 39: Output

## Slide 40: Modeling Study on Santa Margarita Lagoon (SML) Water Quality
By
Pei-Fang Wang
SSC PAC
SML Modeling Study Team
Contributions by
US EPA Region IV
Mississippi State University
USMC Camp Pendleton
Southern California Coastal Water Research Project (SCCWRP)
June 23, 2015

## Slide 41: Southern California Estuaries
Examples of three major estuarine geoforms in California: enclosed bay (left), lagoon (center) and river mouth estuary (right)

## Slide 42: Locations for Field Data Collected (for 2008 and 2009)

## Slide 43: Macroalgae Biomass (Model, 2008-2009)