## Slide 1: SEDIMENT DIAGENESIS
THE MISSING
LINK
External Loads
Sediment Demands and Releases
Prepared by
James L. Martin
July, 2016

## Slide 2: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
Sediment diagenesis results in oxygen demands and nutrient releases

## Slide 3: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
Sediment diagenesis results in oxygen demands and nutrient releases
  a major sink of oxygen in aquatic environments
    Leads to hypoxia
      Hypoxic or Dead zones are becoming more common in estuarine and coastal environments and have, as reported in Science (Diaz and Rosenberg, 2008), spread exponentially since the 1960s and resulting in serious consequences for ecosystem functioning
      As of 2008 (Diaz and Rosenberg 2008), dead zones have been reported from more than 400 systems, affecting a total area of more than 245,000 square kilometers.

## Slide 4: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
Sediment diagenesis results in oxygen demands and nutrient releases
  a major source of nutrients in aquatic environments
    Leads to eutrophication
    Impacts nutrient criteria development

## Slide 5: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE

## Slide 6: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
So, how is it determined?
  1) GUESS (e.g. model calibration)
SOD
BOD
Reaeration
A REALLY BAD IDEA!!

## Slide 7: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
So, how is it determined?
  2) MEASURE
    How many measurements?
    Where and When?
THIS IS EXPENSIVE!

## Slide 8: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
So, how is it determined?
  2) MEASURE (Core method)
    How many measurements?
    Where and When?
THIS IS EXPENSIVE!
University of Maryland Center for Environmental Science, 2006

## Slide 9: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
So, how is it determined?
  2) MEASURE
    ALSO: how do we relate these measurements to external loads?
    Sediment Diagenesis is driven by organic fluxes from the water column, which are ultimately derived from external loads
CAUSE
EFFECT
THE MISSING LINK

## Slide 10: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
Ex. For wasteload allocations assume it does not change in response to load changes (i.e., use measured values)?
Your permit will be based on assuming SOD will not change!
That’s ridiculous, I will see you in Court you %^$@!!+@!

## Slide 11: SEDIMENT OXYGEN DEMAND AND NUTRIENT RELEASE
So, how is it determined?
  3) MODEL (e.g. QUAL2K, CE-QUAL-ICM, WASP routines)
From Chapra Pelletier, 2003. QUAL2K User documentation

## Slide 12
Di Toro, D. M. 2001. Sediment Flux Modeling, Wiley-Interscience, New York, New York. 624 pp.

## Slide 13: Model Overview
Sediment Diagenesis
See: Martin and Wool, 2014, “WASP Sediment Diagenesis Routines: Model Theory and User's Guide”

## Slide 14: Sediment Diagenesis
Particulate Organics (C, N, P)
Oxygen
Dissolved Materials (N,P,CH4,H2S, etc.)

## Slide 15: Reactor
Surface Area
Solids Concentration in Layer 1 (kg/L)
Solids Concentration in Layer 2 (kg/L)
Thickness (assumed = 2 cm)
H2 =Thickness (≈= 10 cm)
Diffusion
Burial velocity to inactive sediments (m/day)
Particle Mixing
Diffusion: internal computation

## Slide 16: Benthic Stress
Particle Mixing
The rate of mixing of the sediment by macrobenthos (bioturbation, w12) is estimated by an apparent particle diffusion coefficient (Dp), temperature corrected that varies with the biomass of the benthos. Assuming that the mass of the benthos is proportional to the labile carbon in the sediment ( , or POC, in oxygen equivalents in layer 2 in G class 1),
where is a particle mixing coefficient and CPOC,R is a reference POC concentration. (Note POC is in units of oxygen equivalents).

## Slide 17: Benthic Stress
Particle Mixing
An additional impact is that if anoxia occurs for periods of time, the benthic population is ultimately reduced or eliminated, so that bioturbuation is consequently reduced or eliminated. To include this effect, Di Toro (2001) computes the stress that low dissolved oxygen conditions (benthic stress, S) imposes on the population assuming that the stress accumulates as
where ks = decay constant for benthic stress, KM,Dp = particle mixing half-saturation concentration for oxygen
As [O2(0)] approaches zero, then (1-ksS) approaches zero, so that the particle mixing coefficient is similarly reduced, as
The stress is continued at the minimum value for the year to conform with the observation that once the benthic population has been reduced by low dissolved oxygen, it does not recover until the next year (Di Toro 2001).

## Slide 18: Reactor Inputs
Constants |  | Value | Units | Description
SA | SA | 2832.68 | m2 | Surface area of sediments (computed)
m1 | m1 | 0.5 | kg/L | Solids concentration in layer 1
m2 | m2 | 0.5 | kg/L | Solids concentration in layer 2
Dd | Dd | 2.50E-03 | m2/d | Diffusion coefficient between layers 1 and 2
QDd | ThtaDd | 1.08 | none | Temperature correction factor for Dd
H2 | H2 | 0.1 | m | Thickness of layer 2
w2 | w2 | 6.85E-06 | m/d | Burial velocity for layer 2 to inactive sediments
Dp | Dp | 6.00E-05 | m2/day | Diffusion coefficient fo particle mixing
QDp | ThtaDp | 1.117 | none | Temperature correction factor for Dp
POC1,R | POC1R | 0.1 | mgC/g | Reference POC1 concentration for Dp measurement
ks | kBEN_STR | 0.03 | 1/day | First-order decay coefficient for accumulated benthic stress
KM,Dp | KM_O2_Dp | 4 | mgO/L | M-M half-saturation constant for oxygen wrt benthos

## Slide 19: Fluxes IN
JPOM
JPOM=vsACPOM
vs=settling velocity, A=area, CPOM =POM concentration
JPOM
JPOC
JPON
JPOP
G1
G2
G3
G1
G2
G3
G1
G2
G3
G classes represent reactivity: G1=labile, G2=refractory, G3=inert

## Slide 20: G Class Input
JPOM
fPON1 | fPON1 | 0.65 | Fraction of PON that is labile
fPON2 | fPON2 | 0.25 | Fraction of PON that is refractory
fPOP1 | fPOP1 | 0.65 | Fraction of POP that is labile
fPOP2 | fPOP2 | 0.2 | Fraction of POP that is refractory
fPOC1 | fPOC1 | 0.65 | Fraction of POC that is labile
fPOC2 | fPOC2 | 0.2 | Fraction of POC that is refractory
JPOM
JPOC
JPON
JPOP
G1
G2
G3
G1
G2
G3
G1
G2
G3

## Slide 21: Mass Balance (for each POM and G class)
JPOM
2
1
bioturbation
diffusion
diagenesis
burial
influx
s = surface transfer rate; SOD/[O2(0)], where SOD=SOD rate and O2(0) is the overlying water concentration
fd1 = fraction dissolved in layer 1
fd2 = fraction dissolved in layer 2
fp1 = fraction particulate in layer 1
fp2 = fraction particulate in layer 2
CT1t+t = total concentration in layer 1 at time t+t
CT2t+t = total concentration in layer 2 at time t+t
CT2t = total concentration in layer 2 at time t
CdOt+t = concentration in overlying water column
KL12 = mass transfer coefficient via diffusion
12 = particle mixing coefficient between layers 1 and 2
2 = sedimentation velocity for layer 2
JT1t+t = source term for total chemical in layer 1 at time t+t
JT2t+t = source term for total chemical in layer 2 at time t+t
12 = square of reaction velocity in layer 1
Diagenesis in Layer 2

## Slide 22: Diagenesis Input
JPOM
2
1
bioturbation
diffusion
diagenesis
burial
influx
Diagenesis in Layer 2
kPON1 | kdiaPON1 | 0.035 | 1/day | First order diagenesis (decay) rate constant for PON1
QPON1 | ThtaPON1 | 1.1 | none | Temperature correction factor for kdiaPON1
kPON2 | kdiaPON2 | 0.0018 | 1/day | First order diagenesis (decay) rate constant for PON2
QPON2 | ThtaPON2 | 1.15 | none | Temperature correction factor for kdiaPON2
kPON3 | kdiaPON3 | 0 | 1/day | First order diagenesis (decay) rate constant for PON3
QPON3 | ThtaPON3 | 1.17 | none | Temperature correction factor for kdiaPON3
kPOP1 | kdiaPOP1 | 0.035 | 1/day | First order diagenesis (decay) rate constant for POP1
QPOP1 | ThtaPOP1 | 1.1 | none | Temperature correction factor for kdiaPOP1
kPOP2 | kdiaPOP2 | 0.0018 | 1/day | First order diagenesis (decay) rate constant for POP2
QPOP2 | ThtaPOP2 | 1.15 | none | Temperature correction factor for kdiaPOP2
kPOP3 | kdiaPOP3 | 0 | 1/day | First order diagenesis (decay) rate constant for POP3
QPOP3 | ThtaPOP3 | 1.17 | none | Temperature correction factor for kdiaPOP3
kPOC1 | kdiaPOC1 | 0.035 | 1/day | First order diagenesis (decay) rate constant for POC1
QPOC1 | ThtaPOC1 | 1.1 | none | Temperature correction factor for kdiaPOC1
kPOC2 | kdiaPOC2 | 0.0018 | 1/day | First order diagenesis (decay) rate constant for POC2
QPOC2 | ThtaPOC2 | 1.15 | none | Temperature correction factor for kdiaPOC2
kPOC3 | kdiaPOC3 | 0 | 1/day | First order diagenesis (decay) rate constant for POC3
QPOC3 | ThtaPOC3 | 1.17 | none | Temperature correction factor for kdiaPOC3

## Slide 23: Ammonia
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PON
-Nitrification

## Slide 24: Ammonia Input
Partitioning
where S1 and S2 are solids concentrations in layer 1 and 2 and  is a partition coefficient
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PON
-nitrification
s=surface transfer/diffusion rate with water column, NH4 = reaction velocity, =temperature coefficient, O2,0 =dissolved oxygen concentration in the overlying water column, and KNH4,O2 =half-saturation concentration of dissolved oxygen in the nitrification reaction, CNH4
= ammonia concentration from the previous time step, KNH4 = half-saturation concentration of ammonia in the nitrification reaction

## Slide 25: Ammonia Input
kNH3 | KappaNH3F | 1.31E-01 | m/d | First nitrification step (NH3®NO2) reaction velocity, fresh water
kNH3 | KappaNH3S | 1.31E-01 | m/d | First nitrification step (NH3®NO2) reaction velocity, salt water
QNH3 | ThtaNH3 | 1.123 | none | Temperature correction factor for kNH3
KM,NH3 | KM_NH3 | 0.728 | mg/L | M-M half-saturation constant for ammonia in NH3®NO2
KM,O2,NH3 | KM_O2_NH3 | 0.37 | mg/L | M-M half-saturation constant for oxygen in NH3®NO2
KdNH3 | KdNH3 | 1 | L/kg | NH3 distribution (partition) coefficient (both Layer 1 and Layer 2)
Note impact of salinity!
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PON
-nitrification
SALTND | 1 | ppt
Salinity above which salt water nitrification and denitrification rates apply

## Slide 26: Nitrite
JPOM
2
1
Diffusion (dissolved)
Diffusion (dissolved)
Burial (particulate)
+Nitrification to NO2 – Reaction (Nitrification) to NO3
Notes:
assumed all dissolved;
reaction rate modified by oxygen in overlaying water and temperature
rate not impacted by salinity,
Annamox not considered
Sedimentation (Burial)

## Slide 27: Nitrite Input
JPOM
2
1
Diffusion (dissolved)
Diffusion (dissolved)
Burial (particulate)
+Nitrification to NO2 – Reaction (Nitrification) to NO3
kN02 | KappaNO2F | 100 | m/d | Second nitrification step (NO2®NO3) reaction velocity, fresh water
kN02 | KappaNO2S | 100 | m/d | Second nitrification step (NO2®NO3) reaction velocity, salt water
QNO2 | ThtaNO2 | 1.123 | none | Temperature correction factor for kNO2
KM,O2,NO2 | KM_O2_NO2 | 0.37 | mg/L | M-M half-saturation constant for oxygen in NO2®NO3

## Slide 28: Nitrate
JPOM
2
1
Diffusion (dissolved)
Diffusion (dissolved)
Sedimentation (Burial)
+Nitrification to NO3
Notes:
assumed all dissolved;
reaction rate modified by oxygen in overlaying water and temperature
denitrification rate impacted by salinity,
Annamox not considered
-Denitrification
-Denitrification
Sedimentation (Burial)

## Slide 29: Nitrate
JPOM
2
1
Diffusion (dissolved)
Diffusion (dissolved)
Sedimentation (Burial)
+Nitrification to NO3
-Denitrification
-Denitrification
Sedimentation (Burial)
kN03,1 | KappaNO3_1F | 0.1 | m/d | Denitrification reaction velocity in layer 1, fresh water
kN03,1 | KappaNO3_1S | 0.1 | m/d | Denitrification reaction velocity in layer 1, salt water
QNO3 | ThtaNO3 | 1.08 | none | Temperature correction factor for kNO3 in both layer 1 and 2

## Slide 30: Sulfides (Salt water only)
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of POC (in oxygen units and corrected for denitrification)
-decomposition of particulate sulfide and dissolved sulfide

## Slide 31: Sulfide Input
Partitioning
where S1 and S2 are solids concentrations in layer 1 and 2 and  are partition coefficients for layer 1 and 2
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PON
-decay
s=surface transfer/diffusion rate with water column,  = reaction velocities for particulate or dissolved form, O2,0 =dissolved oxygen, and KMHS,O2 =half-saturation concentration of dissolved oxygen in the reaction, CH2S
= sulfide concentration

## Slide 32: Sulfide Input
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PON
-decay
kHS1 | KappaHSD_1 | 0.2 | m/d | Dissolved sulfide oxidation reaction velocity in layer 1
kHS2 | KappaHSP_1 | 0.4 | m/d | Particulate sulfide oxidation reaction velocity in layer 1
ThtaHS | ThtaHS | 1.079 | none | Temperature coefficient for sulfide oxidation
KM_O2_HS | KM_O2_HS | 4 | mgO2/l | Sulfide oxidation normalization constant
KdHS1 | KdHS1 | 100 | L/kg | Sulfide partition coefficient in layer 1
KdHS2 | KdHS2 | 100 | L/kg | Sulfide partition coefficient in layer 2

## Slide 33: Methane (Fresh water only)
JPOM
2
1
Diffusion (dissolved)
+ flux from carbon diagenesis: Maximum methane production related to diagenesis of POC (in oxygen units and corrected for denitrification); that is remaining carbon diagenesis is converted to carbon dioxide and methane
Diffusion (dissolved)
- oxidation

## Slide 34: Methane Solubility: Gas production
JPOM
2
1
Diffusion (dissolved)
+ flux from carbon diagenesis: Maximum methane production related to diagenesis of POC (in oxygen units and corrected for denitrification); that is remaining carbon diagenesis is converted to carbon dioxide and methane
Diffusion (dissolved)
- oxidation
where Ho is the depth of the water column over the sediment.
Methane may be oxidized, producing sediment oxygen demand, or exchanged with the water column in either gaseous or dissolved form.

## Slide 35: Methane Inputs
JPOM
2
1
Diffusion (dissolved)
+ flux from carbon diagenesis: Maximum methane production related to diagenesis of POC (in oxygen units and corrected for denitrification); that is remaining carbon diagenesis is converted to carbon dioxide and methane
Diffusion (dissolved)
- oxidation
kCH4 | KappaCH4 | 0.7 | m/d | Methane oxidation reaction velocity
QCH4 | ThtaCH4 | 1.079 | none | Temperature correction factor for kCH4

## Slide 36: Solution Procedures
Solution may be
  steady-state
  time variable
Assume two layers, a “thin” (oxic, depending on overlying water) upper layer and anaerobic layer
  assume that layer 1 can be considered at steady-state in relation to layer 2 (matrix solution)

## Slide 37: Fluxes to water column
Computed based on surface transfer rate (s)
So, the computation of SOD requires an iterative solution
That depends upon the SOD and overlying oxygen concentration

## Slide 38: Computation of SOD
Start with an initial estimate of the SOD
Solve layer 1 and 2 equations for ammonia, nitrate, sulfide and methane
  Solve for the ammonia flux by establishing the chemical specific conditions
  Compute the oxygen consumed by nitrification (NCOD)
  Solve for the nitrate flux by establishing the chemical specific conditions
  Compute methane (fresh water) or sulfide (salt water) oxidation
    For salt water, compute sulfide reaction terms and compute SOD due to hydrogen sulfide
    For fresh water, compute methane flux by establishing the chemical specific
      Compare computed and saturation concentrations and correct
      Calculate the CSOD due to methane
  Compute the total CSOD due to sulfides or methane
  Compute flux terms
  Compute the total SOD due to the sulfide or methane, adding term for NCOD
  Refine the estimate of SOD. A root finding method is used to make the new estimate
Go to step (2) if no convergence

## Slide 39
Salt water
Fresh water

## Slide 40: Other Variables
Once the SOD and s are known (computed), then other model variables, not impacting SOD, may be computed
  Phosphates
  Silica

## Slide 41: Phosphates
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of POP

## Slide 42: Phosphate Input
Partitioning
where S1 and S2 are solids concentrations in layer 1 and 2 and  is a partition coefficient
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of POP
For layer 1, the aerobic layer, if the oxygen concentration in the overlying water column exceeds a critical concentration (O2CRIT, specified in input) then the partition coefficient is increased to represent the trapping of phosphates, or sorption onto iron oxyhydroxide. If the dissolved oxygen is below the critical value, then the sorption coefficient in layer 1 goes to zero.

## Slide 43: Phosphate Input
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PON
-nitrification
KdPO4,2 | KdPO42 | 20 | L/kg | PO4 distribution (partition) coefficient under anaerobic conditions (layer 2)
DKdPO4,1 | dKdPO41F | 20 | none | Incremental distribution coefficient under aerobic conditions, fresh water
DKdPO4,1 | dKdPO41S | 20 | none | Incremental distribution coefficient under aerobic conditions, salt water
O2crit,PO4 | O2critPO4 | 2 | mgO/L | Critical oxygen conc. where Kd begins to decrease due to low DO

## Slide 44: Silica
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PSi
- decay

## Slide 45: Silica Input
Partitioning
where S1 and S2 are solids concentrations in layer 1 and 2 and  is a partition coefficient
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PSi - dissolution
For layer 1, the aerobic layer, if the oxygen concentration in the overlying water column exceeds a critical concentration (O2CRITSI, specified in input) then the partition coefficient is increased to represent the trapping of silica, or sorption onto iron oxyhydroxide. If the dissolved oxygen is below the critical value, then the sorption coefficient in layer 1 goes to zero as in (Di Toro 2001, Eq. 7.18)
PSi = the biogenic silica diagenesis flux to which detrital silica was added; Km,PSi=half saturation constant; kSi= rate of silica dissolution;

## Slide 46: Silica Input
JPOM
2
1
Diffusion (dissolved)
Bioturbation (particulate)
Diffusion (dissolved)
Burial (particulate)
Burial (particulate)
+ Flux due to diagenesis of PSi-dissolution
-nitrification
? Presently not in WASP; need to add

## Slide 47: Inputs to Diagenesis Model
Fluxes (C,N,P, Si; see previous slides)
Rates and constants (see previous slides)
Overlying water column [f(time, space)]
  NH4
  NO2
  NO3
  PO4
  O2
  Salinity
  Available Silica
  CH4
  Temperature
  Salinity

## Slide 48: Inputs to Diagenesis Model
Initial Conditions
  POM for each G-class in Layer 2
    PON(1), PON(2), PON(3)
    POP(1), POP(2), POP(3)
    POC(1), POC(2), POC(3
  Dissolved concentrations (for layers 1 and 2)
    Dissolved NH3
    NO2
    NO3
    Dissolved PO4
From restart file, discussed later

## Slide 49: Outputs from Diagenesis Model
Ammonia flux to water column (mg/m2-day)
Nitrite flux to water column (mg/m2-day)
Nitrate flux to water column (mg/m2-day)
PO4 flux to water column (mg/m2-day)
Aqueous Methane flux to water column (gO2/m2-day)
Gas Methane flux to water column (gO2/m2-day)
SOD Sediment Oxygen demand (gO2/m2-day)
Sulfide flux to water column (gO2/m2-day)
Dissolved (available) silica flux to water column

## Slide 50: What’s Missing
Iron and manganese
multiple layers and ability to simulate impact of scour and sedimentation
Impact of benthic algae
Impacts/simulation of rooted macrophytes
Other stuff?

## Slide 51: WASP 8 Implementation

## Slide 52: WASP 8 Implementation: Model Time step
See: Martin and Wool, 2014, “WASP Sediment Diagenesis Routines: Model Theory and User's Guide”

## Slide 53: WASP 8 Implementation: Model Parameters
See: Martin and Wool, 2014, “WASP Sediment Diagenesis Routines: Model Theory and User's Guide”
Descriptive
Descriptive

## Slide 54: WASP 8 Implementation: Model Parameters
See: Martin and Wool, 2014, “WASP Sediment Diagenesis Routines: Model Theory and User's Guide”
WC 1
WC 2
SD 1

## Slide 55: WASP 8 Implementation: Model Constants
See: Martin and Wool, 2014, “WASP Sediment Diagenesis Routines: Model Theory and User's Guide”

## Slide 56: WASP 8 Implementation: Typical Process
Preliminary Calibration and Model Set-Up
Run model (including diagenesis model) for extended period (years) with Restart Option
Estimate diagenesis Initial Conditions, etc.
Check model predictions for quasi-steady and realistic conditions
Iterate as necessary

## Slide 57: QUESTIONS?
COMMENTS?